## Slide 1: 第四章：处理器
[Adapted from Computer Organization and Design, 4th Edition,
Patterson & Hennessy, © 2008, MK]
Courtesy for Mary Jane Irwin of PSU
Notes: Be aware that this first part of new chapter 4 is review for this class, so doesn’t go into detail. If your students are learning computer organization for the first time, this set of slides needs to be expanded greatly.

## Slide 2: 处理器: 数据通路 & 控制器
MIPS 的简化实现
  存储器访问指令: lw, sw
  算术逻辑指令: add, sub, and, or, slt
  分支指令: beq, j
一般实现
  程序计数器（PC）指向指令所在的存储单元，
  并从中取出指令
  对指令进行解码（并读寄存器的内容）
  执行指令
所有指令（除了跳转指令j）在读取寄存器后，都是用算术逻辑单元ALU。
How? memory-reference? arithmetic? control flow?
Fetch
PC = PC+4
Decode
Exec
Notes: memory reference use ALU to compute addresses
arithmetic use the ALU to do the require arithmetic
control use the ALU to compute branch conditions.

## Slide 3: 时钟方法
时钟方法（clocking methodology ）规定了信号可以读出和写入的时间。
  状态单元-一个存储单元，如寄存器或存储器
  边沿触发– 一种所有的状态改变发生于时钟沿的时钟机制
Typical execution
  读取状态单元的内容-> 通过组合逻辑传送数据->将结果写入一个或者多个状态单元
状态
单元1
状态
单元2
组合逻辑
clock
一个时钟周期
假设状态单元在每个有效的时钟边沿都进行写入操作，则可忽略写控制信号；如果不是，将需要一个写控制信号
  当写控制信号有效且时钟边沿到来时，写入才有效，状态单元才改变状态
Notes: State elements (a memory element) – instruction memory, data memory, registers
With edge-triggered state elements, there is no worry about feedback within a single clock cycle (it’s a single-sided clock constraint (just have to worry about making sure the clock is long enough, don’t have to worry about it being too short))

## Slide 4: 取指指令
取指包括
  从存储单元中将指令取出
  更新程序计数器的值（PC自增），使其指向下一条指令
Read
Address
Instruction
Instruction
Memory
Add
PC
4
  在每个时钟周期PC都会更新，因此它不需要写控制信号，只需要一个时钟信号即可
  读取指令存储器是一项组合逻辑活动，因此它也不需要读控制信号
Fetch
PC = PC+4
Decode
Exec
clock

## Slide 5: 译码指令
译码包括
  将取出的指令的操作码和功能字段的比特位发给控制单元
  and
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit
  从寄存器堆中读取两个值
    指令中包含了寄存器堆的地址
Fetch
PC = PC+4
Decode
Exec

## Slide 6: 执行 R 型指令操作
R 型指令：(add, sub, slt, and, or)
  源操作数在rs 和rt 字段中，op字段为操作码，funct字段指明功能
  将结果存回寄存器堆中(存于目的字段 rd)
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
  注意：寄存器堆并不是每个周期都进行写操作，所以对于寄存器堆来说，需要一个写控制信号
Fetch
PC = PC+4
Decode
Exec
Notes: Since writes to the register file are edge-triggered, we can legally read and write the same register within a clock cycle – the read will get the value written in an earlier clock cycle, which the value written will be available to a read in a subsequent cycle.

## Slide 7: 执行装载和存储操作
装载和存储指令包括
  将基址寄存器中存放的基址（译码阶段从寄存器堆中读取）与指令中16位有符号扩展的偏移量字段相加，计算出访存地址
  存储数据，译码阶段从寄存器堆中读取，写入数据存储器
  装载数据，从数据存储器中读取，写入寄存器堆
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
16
32
Notes: Note there are separate read and write controls to the memory – only one of which may be asserted on any given clock cycle. The memory unit needs a read signal, since, unlike the register file, reading the value of an invalid address can cause problems as we will see later. (Standard memory chips actually have a write enable signal that is used for writes.)

## Slide 8: 执行分支操作
分支操作包括
  比较在译码阶段从寄存器堆中读取的操作数是否相等
  计算出分支目标地址：把更新后的PC值与指令中的16位符号扩展的偏移量字段相加
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch control logic)

## Slide 9: 执行跳转操作
跳转操作包括
  跳转指令将偏移地址的低26位左移两位后，以之代替PC的低28位
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Jump
address
26
4
28

## Slide 10: 创建一个简单的数据通路
需要将各数据通路部件装配在一起，还要控制线和多选器
单周期设计– 每个时钟周期执行一条指令（取指，译码，执行）
  每条指令执行过程中任何数据通路单元只能被用一次，所以如果需要使用多次则必须将该数据通路单元复制多份，(例如：separate Instruction Memory and Data Memory, several adders)，但在执行不同指令时，很多单元可以被共享。
  为了实现不同类型的指令间共享数据通路单元，需要让功能单元有多个输入，使用多选器和控制线（控制信号）来从多个输入中进行选择
  写信号用于控制寄存器堆和数据存储单元的写入
Cycle time is determined by length of the longest path

## Slide 11: 取指，R型，访存指令数据通路部分
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 12: Adding the Control
选择要执行的操作(ALU, Register File and Memory read/write)
控制数据的流向(multiplexor inputs)
I-Type:
op
rs
rt
address offset
31
25
20
15
0
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
Observations
  op （操作码）字 段总是为31-26位
  要读取的两个寄 存器为 rs 字段(25-21位)
  和 rt 字段(20-16位); 对于取字（lw）和存储字（sw）来说，rs是基址寄存器
  有两个地方放目标寄存器。对于装载指令为20:16位（rt字段），对于R型指令为15:11位（rd字段）。
  相等则分支指令、存储字和取字指令的16位偏移量在 15-0位中
J-type:
31
25
0
op
target address

## Slide 13: 包含控制单元的单周期数据通路
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 14: 执行R型指令时数据通路的操作
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 15: 执行装载指令时数据通路的操作
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 16: 执行装载指令时数据通路的操作
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 17: 执行分支指令时数据通路的操作
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 18: 执行分支指令时数据通路的操作
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 19: 加入跳转操作
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Shift
left 2
0
1
Jump
32
Instr[25-0]
26
PC+4[31-28]
28
Notes: For lecture
Good exam questions
Add jalr rs,rd 0 rs 0 rd 0 9
jump to instr whose addr is in rs and save addr of next inst (PC+4) in rd
Add the PowerPC addressing modes of update addressing and indexed addressing (will have to expand the RegFile to be three read port and two write port)
Add andi, ori, addi - have to have both a signextend and a zeroextend and choose between the two, will have to augment the ALUop encoding (since can’t get the op information out of the funct bits as with R-type)
Add mult rs, rt with the result being left in hi|lo - so also include the mfhi and mflo instructions (will have to add a multiplier, the hi and lo registers and then a couple of muxes and their control).
Add barrel shifter

## Slide 20: 指令周期(关键路径)
Instr. | I Mem | Reg Rd | ALU Op | D Mem | Reg Wr | Total
R-type |  |  |  |  |  | 
load |  |  |  |  |  | 
store |  |  |  |  |  | 
beq |  |  |  |  |  | 
jump |  |  |  |  |  | 
What is the clock cycle time：假设多路选择器，控制单元，符号扩展，PC读取，左移两位，线路建立和保持时间等所带来的延迟忽略不计，除了：
  Instruction and Data Memory (200 ps)
  ALU and adders (200 ps)
  Register File access (reads or writes) (100 ps)
Notes: For class handout

## Slide 21: 指令关键路径
Instr. | I Mem | Reg Rd | ALU Op | D Mem | Reg Wr | Total
R-type |  |  |  |  |  | 
load |  |  |  |  |  | 
store |  |  |  |  |  | 
beq |  |  |  |  |  | 
jump |  |  |  |  |  | 
200 | 100 | 200 |  | 100 | 600
200 | 100 | 200 | 200 | 100 | 800
What is the clock cycle time：假设多路选择器，控制单元，符号扩展，PC读取，左移两位，线路建立和保持时间等所带来的延迟忽略不计，除了：
  Instruction and Data Memory (200 ps)
  ALU and adders (200 ps)
  Register File access (reads or writes) (100 ps)
200 | 100 | 200 | 200 |  | 700
200 | 100 | 200 |  |  | 500
200 |  |  |  |  | 200
Notes: For lecture
Note that PC is updated during I Mem read

## Slide 22: 单周期的缺点和优点
使用时钟周期效率不高– 单周期设计中，时钟周期对所有指令等长，这样时钟周期要由执行时间最长的（最慢的）那条指令决定。
  特别对于更复杂的指令，这样的问题更明显，如浮点乘法
可能会浪费芯片的面积，因为有些功能单元必须被复制，只是由于它们不能在一个时钟周期内被共享
优点：简单且易于理解
Clk
lw
sw
Waste
Cycle 1
Cycle 2
Notes: In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.

## Slide 23: 怎样使它速度更快？
一次获取（和执行）多条指令
  超标量技术-敬请期待
在当前指令完成之前开始取指和执行下一条指令
  流水线– (all?)现代处理器都是部署了流水线技术以提高性能
  记住性能公式: CPU 时间= CPI * 指令数 * 时钟周期时间
在理想情况和有大量指令的情况下，流水线所带来的加速比与流水线的级数近似相同
  一个5级流水线能获得的加速比接近于5
Notes: In reality the time per instruction in a pipeline processor is longer than the minimum possible because 1) the pipeline stages may not be perfectly balanced and 2) pipelining involves some overhead (like pipeline stage isolation registers).

## Slide 24: 装载指令的五个阶段
IFetch:指令读取和更新PC
Dec: 寄存器取值和指令译码
Exec:执行R类型指令; 计算存储地址
Mem:读/写数据从/到数据存储器
WB:将结果数据写入寄存器堆中
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
Notes: As shown here, each of these five steps will take one clock cycle to complete.

## Slide 25: 采用流水线结构的MIPS处理器
在当前指令完成前开始下一条指令
  提高了吞吐量 - 在给定的时间内完成的工作量
  指令延迟(执行时间, 等待/延迟时间, 响应时间- 指令开始到结束的时间) 并没得到减少
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
Cycle 7
Cycle 6
Cycle 8
sw
IFetch
Dec
Exec
Mem
WB
R-type
IFetch
Dec
Exec
Mem
WB
    时钟周期(流水线阶段时间) ) 受到最慢的阶段限制
      有些阶段是不需要整个时钟周期(如写回阶段WB)
      对于一些指令，有些阶段是浪费的 (例如在该指令内什么工作也没做)
Notes: Latency = execution time (delay or response time) – the total time from start to finish of ONE instruction
For processors one important measure is THROUGHPUT (or the execution bandwidth) – the total amount of work done in a given amount of time
For memories one important measure is BANDWIDTH – the amount of information communicated across an interconnect (e.g., bus) per unit time; the number of operations performed per second (the WIDTH of the operation and the RATE of the operation)

## Slide 26: 单周期 vs 流水线
lw
IFetch
Dec
Exec
Mem
WB
流水线执行(CC = 200 ps):
IFetch
Dec
Exec
Mem
WB
sw
IFetch
Dec
Exec
Mem
WB
R-type
Clk
单周期执行(CC = 800 ps):
lw
sw
Waste
Cycle 1
Cycle 2
要完成一个完整的指令在流水线的情况下需要1000 ps(与之对比，在单周期执行的情况下要 800 ps). Why ?
How long does each take to complete 1,000,000 adds ?
400 ps
Notes: 1,000,000 adds for single cycle = 800,000,000 ps
1,000,000 adds for pipelined = 200,000,000 ps + 800 ps (fill or flush time)

## Slide 27: 面向流水线的MIPS指令集设计
为什么MIPS使流水线更简单？
  所有的MIPS指令长度都相同(32 bits)
    在1st 阶段取指，在2nd阶段译码
  只有很少的几种指令格式，并且每一条指令中的源寄存器位置都是相同的
    这意味着流水线的第二级2nd在确定取指类型的同时就能够开始读寄存器堆
  MIPS中的存储器操作仅出现在存取指令中
    这意味着可利用执行级计算存储器地址
  每条指令最多只能写一个结果(i.e, changes the machine state) ，并且是在流水线最后的阶段（存储器访问或写回阶段）
  所有操作数必须在存储器中对齐，因此，一个数据传输指令只需访问一次存储器

## Slide 28: MIPS数据通路（加了流水线）
流水线各阶段间的状态寄存器用于各段流水线的隔离
IF:IFetch
ID:Dec
EX:Execute
MEM:
MemAccess
WB:
WriteBack
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
System Clock
Notes: Any info that is needed in a later pipe stage must be passed to that stage via a pipeline register (e.g., need to preserve the destination register address in the pipeline state registers)
Note two exceptions to right-to-left flow
WB that writes the result back into the register file in the middle of the datapath
Selection of the next value of the PC, one input comes from the calculated branch address from the MEM stage
Only later instructions in the pipeline can be influenced by these two REVERSE data movements.
The first one (WB to ID) leads to data hazards.
The second one (MEM to IF) leads to control hazards.
All instructions must update some state in the processor – the register file, the memory, or the PC – so separate pipeline registers are redundant to the state that is updated (not needed).
PC can be thought of as a pipeline register: the one that feeds the IF stage of the pipeline. Unlike all of the other pipeline registers, the PC is part of the visible architecture state – its content must be saved when an exception occurs (the contents of the other pipe registers are discarded).

## Slide 29: MIPS Pipeline Control Path Modifications
所有的控制信号都可以在译码阶段中决定
  and held in the state registers between pipeline stages
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc

## Slide 30: 流水线控制
IF Stage（取指阶段）: 读指令存储器(always asserted) and 写 PC 寄存器(on System Clock)
ID Stage（译码阶段）: 没有可选的控制信号去设置
 | EX Stage |  |  |  | MEM Stage |  |  | WB Stage | 
 | RegDst | ALUOp1 | ALUOp0 | ALUSrc | Brch | MemRead | MemWrite | RegWrite | Mem toReg
R | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
lw | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
sw | X | 0 | 0 | 1 | 0 | 0 | 1 | 0 | X
beq | X | 0 | 1 | 0 | 1 | 0 | 0 | 0 | X

## Slide 31: 图形表示MIPS流水线
Can help with answering questions like:
  How many cycles does it take to execute this code?
  What is the ALU doing during cycle 4?
  Is there a hazard, why does it occur, and how can it be fixed?
ALU
IM
Reg
DM
Reg

## Slide 32: 为何采用流水线？为了提高性能
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Once the pipeline is full, one instruction is completed every cycle, so CPI = 1
Time to fill the pipeline

## Slide 33: 流水线技术是否会带来麻烦？
Yes: 流水线冒险
  结构冒险: 多条指令在同一时钟周期试图使用相同的硬件资源
  数据冒险: 试图使用未准备好的数据
    一条指令的源操作数由另一条先执行的指令产生，而该条先执行的指令尚未完成，还没产生所需的源操作数
  控制冒险:试图在跳转条件未被验证以及新的PC目标地址未被计算出来的情况下，决定程序的控制流程
    分支和跳转指令，异常
通常使用等待来解决这些冒险
  流水线控制必须检测这些冒险
  并且采取行动解决这些冒险
Notes: Note that data hazards can come from R-type instructions or lw instructions
Exceptions can’t be resolved by waiting!

## Slide 34: 一个存储器也可导致结构冒险
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
lw
Inst 1
Inst 2
Inst 4
Inst 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Reading data from memory
Reading instruction from memory
有单独的指令存储器和数据存储器就解决了结构冒险这个问题 (I$ and D$)

## Slide 35: 寄存器堆的访问会如何？
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 1
Inst 2
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix register file access hazard by doing reads in the second half of the cycle and writes in the first half
add $1,
add $2,$1,
clock edge that controls register writing
clock edge that controls loading of pipeline state registers
Notes: Define register reads to occur in the second half of the cycle and register writes in the first half

## Slide 36: 寄存器的使用可引发数据冒险
I
n
s
t
r.
O
r
d
e
r
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
数据依赖导致数据冒险
Read before write 数据冒险
Notes: For class handout

## Slide 37: 寄存器的使用可引发数据冒险
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
数据依赖导致数据冒险
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Read before write 数据冒险
Notes: For lecture

## Slide 38: 装载数据引发数据冒险
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
一条指令因必须等待另一条指令的完成才能获得所需数据而导致该指令不能在预定的时钟周期内执行
装载-使用型数据冒险
Notes: Note that lw is just another example of register usage (beyond ALU ops)

## Slide 39: 分支指令导致控制冒险
I
n
s
t
r.
O
r
d
e
r
lw
Inst 4
Inst 3
beq
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
决策依赖于一条指令的结果，而其正在执行中，因此引发冒险

## Slide 40: 其他结构的流水线是否可能？
慢的乘法如何?
  Make the clock twice as slow or …
  let it take two cycles (since it doesn’t use the DM stage)
ALU
IM
Reg
DM
Reg
MUL
ALU
IM
Reg
DM1
Reg
DM2
数据存储器的访问速度比指令存储器的访问速度慢一倍如何？
  make the clock twice as slow or …
  let data memory access take two cycles (and keep the same clock rate)
Notes: Note that we don’t need the output of MUL until the WB cycle, so we can span two pipeline stages with the MUL hardware (so the multiplier is a two stage pipelined multiplier)

## Slide 41: 流水线的其他替代方案
ARM7
XScale
ALU
IM1
IM2
DM1
Reg
DM2
IM
Reg
EX
PC update
IM access
decode
reg
access
ALU op
DM access
shift/rotate
commit result
(write back)
Reg
SHFT
PC update
BTB access
start IM access
IM access
decode
reg 1 access
shift/rotate
reg 2 access
ALU op
start DM access
exception
DM write
reg write

## Slide 42: Summary
所有的现代处理器都使用了流水线技术
流水线技术并不有助于减少单条指令的执行时间，而是有助于提高指令的吞吐率。
潜在的提速: a CPI of 1 and a fast CC
流水线的处理速度受限于最慢的流水线处理阶段
  不平衡的流水线阶段会导致流水线效率低下
  对于deep pipelines 来说，流水线的“充满”时间和“排光”时间对它的加速和短代码执行是有影响的
必须检测和解决冒险
  流水线阻塞会对CPI造成不利影响 (makes CPI greater than the ideal of 1)