## Slide 1: 第四章：处理器-B
[Adapted from Computer Organization and Design, 4th Edition,
Patterson & Hennessy, © 2008, MK]
Courtesy for Mary Jane Irwin of PSU
Notes: Be aware that this first part of new chapter 4 is review for this class, so doesn’t go into detail. If your students are learning computer organization for the first time, this set of slides needs to be expanded greatly.

## Slide 2: Review:为何采用流水线技术? 为了提高性能!
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Once the pipeline is full, one instruction is completed every cycle, so CPI = 1
Time to fill the pipeline

## Slide 3: Review: MIPS流水线数据通路及其控制
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc
Notes: How many bits wide is each pipeline register?
PC – 32 bits
IF/ID – 64 bits
ID/EX – 9 + 32x4 + 10 = 147
EX/MEM – 5 + 1 + 32x3 + 5 = 107
MEM/WB – 2 + 32x2 + 5 = 71

## Slide 4: Review: 流水线是否会带来麻烦?
Yes: 流水线冒险
  结构冒险: 多条指令在同一时钟周期试图使用相同的硬件资源
  数据冒险: 试图使用未准备好的数据
    一条指令的源操作数由另一条先执行的指令产生，而该条先执行的指令尚未完成，还没产生所需的源操作数
  控制冒险:试图在跳转条件未被验证以及新的PC目标地址未被计算出来的情况下，决定程序的控制流程
    分支和跳转指令，异常
通常使用等待来解决这些冒险
  流水线控制必须检测这些冒险
  并且采取行动解决这些冒险
Notes: Note that data hazards can come from R-type instructions or lw instructions

## Slide 5: Review: 寄存器使用可以导致数据冒险
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Read before write 数据冒险
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Value of $1 10 10 10 10 10/-20 -20 -20 -20 -20

## Slide 6: 一个解决数据冒险的办法waiting – stall
stall
stall
I
n
s
t
r.
O
r
d
e
r
add $1,
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
and $6,$1,$7
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Can fix data hazard by waiting – stall – but impacts CPI

## Slide 7: 另一种解决数据冒险的方法：转发机制forwarding
I
n
s
t
r.
O
r
d
e
r
add $1,
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
and $6,$1,$7
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix data hazards by forwarding results as soon as they are available to where they are needed
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Notes: For class handout

## Slide 8: 另一种解决数据冒险的方法：转发机制forwarding
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix data hazards by forwarding results as soon as they are available to where they are needed
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
I
n
s
t
r.
O
r
d
e
r
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Notes: For lecture
Forwarding paths are valid only if the destination stage is later in time than the source stage.
Forwarding is harder if there are multiple results to forward per instruction or if they need to write a result early in the pipeline.
Notice that for now we are showing the forwarded data coming out of the ALU. After looking at the problem more closely, we will see that it is really supplied by the pipeline register EX/MEM or MEM/WB and will depict is as such.

## Slide 9: 数据转发(又称为“旁路”)
在指令完成之前，无论是在流水线的哪个状态寄存器，只要需要的数据项一旦产生，就将它转发至需要该数据项的功能单元（例如，ALU）
对于ALU来说：如果可以从任何流水线寄存器而不仅仅从ID/EX中得到ALU的输入，那么就可以转发所需的数据，这是通过下述方法实现：
  将多选器加至ALU的输入端
  加合适的控制硬件（正确的控制策略）去控制新的多选器
其它的功能单元也可能需要这些相似的转发逻辑（如DM)
通过转发，甚至在数据依赖存在的情况下也能实现CPI=1

## Slide 10: 数据转发的控制条件
EX Forward Unit:
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRs))
ForwardA = 10
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRt))
ForwardB = 10
Forwards the result from the previous instr. to either input of the ALU
Forwards the result from the second previous instr. to either input of the ALU
MEM Forward Unit:
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
ForwardA = 01
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (MEM/WB.RegisterRd = ID/EX.RegisterRt))
ForwardB = 01

## Slide 11: 转发的图示
I
n
s
t
r.
O
r
d
e
r
add $1,
sub $4,$1,$5
and $6,$7,$1
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
EX forwarding
MEM forwarding
Notes: Now we see that the forwarded data is supplied by the pipeline register EX/MEM or MEM/WB.

## Slide 12: 另一种复杂的情况
I
n
s
t
r.
O
r
d
e
r
add $1,$1,$2
ALU
IM
Reg
DM
Reg
add $1,$1,$3
add $1,$1,$4
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
当WB阶段指令的结果和MEM阶段指令产生的结果相冲突时，可能会发生另一个潜在的数据冒险-那么哪个结果该被转发呢？
Notes: For class handout

## Slide 13: 另一种复杂的情况
I
n
s
t
r.
O
r
d
e
r
add $1,$1,$2
ALU
IM
Reg
DM
Reg
add $1,$1,$3
add $1,$1,$4
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
当WB阶段指令的结果和MEM阶段指令产生的结果相冲突时，可能会发生另一个潜在的数据冒险-那么哪个结果该被转发呢？
Notes: For lecture

## Slide 14: 校正的数据转发控制条件
MEM 转发单元:
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (EX/MEM.RegisterRd != ID/EX.RegisterRs)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
ForwardA = 01
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (EX/MEM.RegisterRd != ID/EX.RegisterRt)
and (MEM/WB.RegisterRd = ID/EX.RegisterRt))
ForwardB = 01
EX 转发单元:
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRs))
ForwardA = 10
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRt))
ForwardB = 10
Forwards the result from the previous instr. to either input of the ALU
Forwards the result from the previous or second previous instr. to either input of the ALU

## Slide 15: 带有转发硬件的数据通路
PCSrc
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
Forward
Unit
Notes: For class handout

## Slide 16: 带有转发硬件的数据通路
PCSrc
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
Forward
Unit
ID/EX.RegisterRt
ID/EX.RegisterRs
EX/MEM.RegisterRd
MEM/WB.RegisterRd
Notes: For lecture.
How many bits wide is each pipeline register now?
PC – 32
IF/ID – 32*2
ID/EX – 9 + 32x4 + 10 = 147 + 10 = 157
EX/MEM – 5 + 1 + 32*3 + 5 = 107
MEM/WB – 2 + 32*2 + 5 = 71
Control line inputs to Forward Unit EX/MEM.RegWrite and MEM/WB.RegWrite not shown on diagram

## Slide 17: Memory-to-Memory Copies
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
ALU
IM
Reg
DM
Reg
sw $1,4($3)
ALU
IM
Reg
DM
Reg
可以通过在MEM/WB寄存器到数据存储器的输入间加入转发硬件，从而使存储 (memory-to-memory copies)之后马上装载的操作可以避免阻塞
  需要在MEM阶段加一个转发单元和一个多选器
Notes: What if lw was replaced with add $1, - is forwarding still needed? From where, to where?
What if $1 was used to compute the effective address (it would be a load-use data hazard and would require a stall insertion between the lw and sw)

## Slide 18: 装载-使用型数据冒险的转发
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
Notes: For class handout

## Slide 19: 装载-使用型数据冒险的转发
stall
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Will still need one stall cycle even with forwarding
Notes: For lecture
The one case where forwarding cannot save the day is when an instruction tries to read a register following a load instruction that writes the same register.

## Slide 20: 装载-使用型数据冒险检测单元
在指令译码阶段需要一个冒险检测单元，它工作在ID级，从而可以在装载指令和紧随其后需要它的结果的指令间插入阻塞
ID Hazard detection Unit:
if (ID/EX.MemRead
and ((ID/EX.RegisterRt = IF/ID.RegisterRs)
or (ID/EX.RegisterRt = IF/ID.RegisterRt)))
stall the pipeline
第一行的测试是看当前时刻在EX阶段中的指令是否为一条装载指令；接下来的两行用来检测在EX级的装载指令的目的寄存器是否与在ID级的指令的某一个源寄存器相匹配。如果条件成立，指令将阻塞一个时钟周期。
经过一周期的阻塞以后，转发逻辑就能够处理相关性并继续执行程序了

## Slide 21: 冒险/阻塞 硬件
如果处于ID级的指令被阻塞，那么处于IF级的指令也必须被阻塞。防止这两条指令继续执行的方法是保持PC寄存器和IF/ID流水线寄存器不变
  Hazard detection Unit controls the writing of the PC (PC.write) and IF/ID (IF/ID.write) registers
在EX级的lw指令和ID级的装载-使用指令之间插入“气泡”（例如，在流水线中插入空指令）
  方法是把ID/EX流水线寄存器的EX、MEM和WB级的控制信号都置为0。然后冒险控制单元控制多选器去选择这些全0和实际控制信号值。
接下来，就让lw和它之后的流水线中的指令正常进行即可

## Slide 22: 加入冒险/阻塞硬件
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
Notes: For class handout

## Slide 23: 加入冒险/阻塞硬件
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
ID/EX.RegisterRt
0
ID/EX.MemRead
PC.Write
IF/ID.Write
Notes: For lecture
In reality, only the signals RegWrite and MemWrite need to be 0, the other control signals can be don’t cares.
Another consideration is energy – where clock gating is called for.

## Slide 24: 控制冒险
当指令地址的流程不是连续的(如 PC = PC + 4); 这是由一些流程指令引发的
  无条件跳转(j, jal, jr)
  有条件跳转(beq, bne)
  异常
可用的解决方案
  阻塞(影响CPI)
  尽可能地将决策点提前，在流水线中越早做决策越好，以此来减少阻塞的周期数
  延迟决定(需要编译器支持)
  分支预测
控制冒险发生的频率要比数据冒险小，但是对于控制冒险而言，找不到像转发机制那样能有效解决数据冒险的方案出来

## Slide 25: Datapath Branch and Jump Hardware
ID/EX
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
EX/MEM
MEM/WB
Control
ALU
cntrl
Forward
Unit
Branch
PCSrc
Shift
left 2
Add
Shift
left 2
Jump
PC+4[31-28]

## Slide 26: Jumps Incur One Stall
flush
I
n
s
t
r.
O
r
d
e
r
j
j target
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
幸运的是，分支跳转发生的概率不是很高-only 3% of the SPECint instruction mix
分支决策/跳转要到ID级才译码，因此，需要一个flush （清除）。
  为了在IF级清除指令，加了一个IF.Flush的控制信号，即将IF/ID流水线寄存器的指令字段置为0.清除寄存器的结果是将预取到的指令转变为空指令
Fix jump hazard by waiting – flush
ALU
IM
Reg
DM
Reg

## Slide 27: 两种“类型”的阻塞
空指令(气泡) 插入流水线两指令之间 (正如对装载-使用情况那样做)
  Keep the instructions earlier in the pipeline (later in the code) from progressing down the pipeline for a cycle (“bounce” them in place with write control signals)
  通过在合适的阶段给流水线寄存器的控制位置零来实现插入空指令
  让流水线后面的指令正常工作
清除(又称instruction squashing)：流水线中的一条指令用一条空指令进行替换 (如处理顺序地跟在j指令之后的指令)
  将需要被清除的指令的控制位置零

## Slide 28: Supporting ID Stage Jumps
ID/EX
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
EX/MEM
MEM/WB
Control
ALU
cntrl
Forward
Unit
Branch
PCSrc
Shift
left 2
Add
Shift
left 2
Jump
PC+4[31-28]
0

## Slide 29: Review:分支指令导致控制冒险
I
n
s
t
r.
O
r
d
e
r
lw
Inst 4
Inst 3
beq
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
决策依赖于一条指令的结果，而其正在执行中，因此引发冒险

## Slide 30: 一个解决分支控制冒险的办法
flush
flush
flush
I
n
s
t
r.
O
r
d
e
r
beq
ALU
IM
Reg
DM
Reg
beq target
ALU
IM
Reg
DM
Reg
ALU
Inst 3
IM
Reg
DM
Fix branch hazard by waiting – flush – but affects CPI
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg

## Slide 31: 另一个解决分支控制冒险的办法
flush
I
n
s
t
r.
O
r
d
e
r
beq
beq target
ALU
IM
Reg
DM
Reg
Inst 3
ALU
IM
Reg
DM
Fix branch hazard by waiting – flush
ALU
IM
Reg
DM
Reg
将分支决策移至流水线中尽可能早的位置–如during the decode cycle
ALU
IM
Reg
DM
Reg
Notes: Another “solution” is to put in enough extra hardware so that we can test registers, calculate the branch address, and update the PC during the second stage of the pipeline. That would reduce the number of stalls to only one.

## Slide 32: 缩短分支的延迟
将分支决策硬件移回 EX 阶段
  将阻塞(清除) 的周期数减少至two
  Adds an and gate（与门） and a 2x1 mux（多选器） to the EX timing path
增加硬件用于计算分支目标地址，并进行分支判断和评估将分支决策提前到ID级是否值得
  将阻塞(清除) 的周期数减少至1
    但是需要在ID阶段加转发硬件
  计算分支目标地址可以和寄存器堆的读取并行 (done for all instructions – only used when needed)
  寄存器间的比较必须在寄存器堆读取之后，所以进行比较和更新PC需要给ID timing path 加上这些硬件：a mux, a comparator, and an and gate
对于深层流水线，分支决策点可以甚至在更后面，引发更多阻塞
Notes: Want a small branch penalty.
Need more forwarding and hazard detection hardware for second option (one stall implementation) since a branch depended on a result still in the pipeline (that is one of the source operands for the comparison logic) must be forwarded from the EX/MEM or MEM/WB pipeline latches.

## Slide 33: ID Branch Forwarding Issues
MEM/WB “forwarding” is taken care of by the normal RegFile（寄存器堆） write before read operation
WB add3 $1,
MEM add2 $3,
EX add1 $4,
ID beq $1,$2,Loop
IF next_seq_instr
像下面这些情况，需要从EX/MEM流水线阶段转发到 ID阶段的comparison hardware：
WB add3 $3,
MEM add2 $1,
EX add1 $4,
ID beq $1,$2,Loop
IF next_seq_instr
if (IDcontrol.Branch
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = IF/ID.RegisterRs))
ForwardC = 1
if (IDcontrol.Branch
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = IF/ID.RegisterRt))
ForwardD = 1
Forwards the result from the second previous instr. to either input of the compare

## Slide 34: ID Branch Forwarding Issues
如果分支指令的前一指令产生
分支的源操作数，则需要在beq
和add1之间插入一个阻塞，这是
因为EX阶段的ALU操作的执行时间
和ID阶段的分支比较操作的执行时间是在同一时刻
WB add3 $3,
MEM add2 $4,
EX add1 $1,
ID beq $1,$2,Loop
IF next_seq_instr
  “Bounce” the beq (in ID) and next_seq_instr (in IF) in place (ID Hazard Unit deasserts PC.Write and IF/ID.Write)
  Insert a stall between the add in the EX stage and the beq in the ID stage by zeroing the control bits going into the ID/EX pipeline register (done by the ID Hazard Unit)
如果分支发生，那么就清除当前时刻IF中的指令 (IF.Flush)

## Slide 35: Supporting ID Stage Branches
Read
Address
Instruction
Memory
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
RegFile
Read Data 1
ReadData 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
Compare
Forward
Unit
Add
IF.Flush
0
0
1
0
Notes: Now IF.Flush is generated by the Hazard Unit for both jumps and for taken branches.
Book claims that you have to forward from the MEM/WB pipeline latch, but with RegFile write before read, I don’t think that is the case!!

## Slide 36: 延迟分支
如果分支硬件已经被移至ID阶段，那么我们就可以消除延迟分支所带来的所有分支阻塞。延迟分支顺序执行下一条指令，在一条指令延迟之后再开始执行分支。
  MIPS 编译器会在延迟分支指令的后面紧跟着放一条不受该分支影响的指令（安全指令），以此来隐藏分支延迟
对于较长的流水线，分支延迟的增长需要不止一个延迟槽
  对比于更加灵活的硬件（动态）分支预测，延迟分支已经不够流行了
  可用晶体管的增长使硬件分支预测变得相对更便宜
Notes: No processor uses delayed branches of more than 1 cycle.
For longer branch delays, hardware-based branch prediction is used.

## Slide 37: 分支时间槽的调度 图4-64
A is the best choice, fills delay slot and reduces IC
In B and C, the sub instruction may need to be copied, increasing IC
In B and C, must be okay to execute sub when branch fails
add $1,$2,$3
if $2=0 then
延迟时间片
A. 使用分支前的指令填充
B. 以分支目标指令填充
C. 以分支不发生时的下一条指令填充
add $1,$2,$3
if $1=0 then
延迟时间片
add $1,$2,$3
if $1=0 then
延迟时间片
sub $4,$5,$6
sub $4,$5,$6
becomes
becomes
becomes
if $2=0 then
add $1,$2,$3
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
add $1,$2,$3
if $1=0 then
sub $4,$5,$6
Notes: Limitations on delayed-branch scheduling come from 1) restrictions on the instructions that can be moved/copied into the delay slot and 2) limited ability to predict at compile time whether a branch is likely to be taken or not.
In B and C, the use of $1 prevents the add instruction from being moved to the delay slot
In B the sub may need to be copied because it could be reached by another path. B is preferred when the branch is taken with high probability (such as loop branches

## Slide 38: 静态分支预测
通过假定一个给定的结果和行动来解决分支冒险，而不进行等待来看实际的分支结果
预测不发生– 总是预测分支不发生，继续顺序从指令流中取指，当分支发生时才执行流水线阻塞
  如果发生，分支之后执行清除（flush）
    in IF, ID, and EX stages if branch logic in MEM – three stalls
    In IF and ID stages if branch logic in EX – two stalls
    in IF stage if branch logic in ID – one stall
  ensure that those flushed instructions haven’t changed the machine state – automatic in the MIPS pipeline since machine state changing operations are at the tail end of the pipeline (MemWrite (in MEM) or RegWrite (in WB))
  当到达分支目的地时重启流水线
Notes: This is a static scheme since the same decision is always made (not taken or taken).

## Slide 39: 预测命中时的flush(不发生)
4 beq $1,$2,2
I
n
s
t
r.
O
r
d
e
r
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
8 sub $4,$1,$5
为了清除IF 级指令, 将IF.Flush控制信号，即将IF/ID流水线寄存器的指令字段置为0 (变成空指令)
Notes: For class handout

## Slide 40: 预测未命中时的flush(发生)
flush
4 beq $1,$2,2
I
n
s
t
r.
O
r
d
e
r
ALU
IM
Reg
DM
Reg
16 and $6,$1,$7
20 or r8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
8 sub $4,$1,$5
为了清除IF 级指令, 将IF.Flush控制信号，即将IF/ID流水线寄存器的指令字段置为0 (变成空指令)
Notes: For lecture
Note branch address is PC-relative branch to 4+4+2*4 = 16

## Slide 41: 分支结构
预测不发生对于循环体顶部的分支结构能取得较好的效果
Loop: beq $1,$2,Out
1nd loop instr
.
.
.
last loop instr
j Loop
Out: fall out instr
  循环体底部的分支总是会跳回到循环体的顶部– incur the jump stall overhead
预测不发生对于循环体底部的分支结构能取得的效果不好
Loop: 1st loop instr
2nd loop instr
.
.
.
last loop instr
bne $1,$2,Loop
fall out instr

## Slide 42: 静态分支预测
通过假定一个给定的结果和行动来解决分支冒险，而不进行等待来看实际的分支结果
预测发生– 预测分支总会被执行
  预测发生经常会引起一个周期的阻塞 (if branch destination hardware has been moved to the ID stage)
  有没有办法“缓存”分支目标指令的地址？
当分支带来的不利增加时 (for deeper pipelines), 简单的静态分支预测方案将会浪费大量的性能。如果有了更多硬件的支持，就可能在程序执行的时候动态地预测分支行为。
动态分支预测 –在运行的时候，观察和分析run-time 信息来预测分支。
Notes: Predict taken always incurs one stall at least – assuming the branch destination address hardware has been moved up to the ID stage.
So predict not taken is easier since sequential instruction address can be computed in the IF stage.

## Slide 43: 动态分支预测
IF阶段的分支预测缓存（又称为分支历史记录表BHT）：一小块按照分支指令的低位地址索引的存储器区，其中包括一位或者多位数据用以说明最近是否发生过分支。
  预测位可能预测不准确，我们实际不知道预测是否准确，而且它还可能由其他具有相同地址低位的分支设置，但这不影响这种方法的准确率，只影响性能。
    Branch decision occurs in the ID stage after determining that the fetched instruction is a branch and checking the prediction bit(s)
  如果预测是错的,清除流水线中不正确的指令,重启流水线中正确的指令， 并反转预测位即可。
    A 4096 bit BHT varies from 1% misprediction (nasa7, tomcatv) to 18% (eqntott)
Notes: 4096 entry table programs vary from 1% misprediction (nasa7, tomcatv) to 18% (eqntott), with spice at 9% and gcc at 12%
4096 about as good as infinite table, but 4096 is a lot of hardware

## Slide 44: 分支目标缓存
BHT（分支预测缓存）只预测了分支何时发生，却没预测在哪发生
  分支目标缓存(BTB)：一种用于缓存分支目标地址或者分支目标指令的结构，其一般形式为带标志位的cache，因而硬件开销大于简单的分支预测缓存器。
    需要一个具有两个读端口的指令存储器
如果预测是正确的，那么不管它们往哪个方向跳，阻塞都是可以避免的。
  指令寄存器在读取下一条顺序执行的指令的同时，BTB能够缓存发生的分支指令
Read
Address
Instruction
Memory
PC
0
BTB
Notes: Except for the first time the branch is encountered, when we don’t have the branch instruction loaded into the BTB
Its not quite this simple – what if the BTB instruction is for the wrong branch!! – but close enough for students at this level

## Slide 45: 1位预测位的准确性
当分支不发生时1位预测器将两次不正确
循环10次，我们有80%的预测成功率
  假设开始时预测位为 0(predict_bit = 0表明分支不发生)，循环控制是在循环体的底部
  第一次循环，预测器mispredicts 分支，这是因为分支跳转到循环体顶部；反转预测位 (predict_bit = 1)
  只要分支发生，预测就是正确的
  循环体结束时，预测器再一次mispredicts 分支，这是因为Loop结束了; 反转预测位(predict_bit = 0)
Loop: 1st loop instr
2nd loop instr
.
.
.
last loop instr
bne $1,$2,Loop
fall out instr

## Slide 46: 2位预测位
一个两位预测方案能够实现90%的准确率，这是因为在预测位改变之前，预测必须错2次
Predict
Taken
Predict
Not Taken
Predict
Taken
Predict
Not Taken
Taken
Not taken
Not taken
Not taken
Not taken
Taken
Taken
Taken
Loop: 1st loop instr
2nd loop instr
.
.
.
last loop instr
bne $1,$2,Loop
fall out instr
wrong on loop fall out
0
1
1
right 9 times
right on 1st iteration
0
BHT also stores the initial FSM state
10
11
01
00
Notes: For lecture
In a counter implementation, the counters are incremented when a branch is taken and decremented when not taken (and saturate at 00 or 11). Since we read the prediction bits on every cycle, a 2-bit predictor will need both a read and a write access port (for updating the prediction bits).

## Slide 47: 处理异常
异常(也称中断) 是另一种形式的控制冒险。异常来源有：
  R-type 算术溢出
  使用未定义指令
  I/O设备请求
  系统服务请求(如缺页异常, TLB异常等)
  硬件错误
流水必须停止正在执行的非法指令，让前面的指令都完成，清除后面的指令，并将异常的原因设置到一个寄存器，保存非法指令的地址， 并跳转到提前确定的地址 (异常处理代码的地址)
软件(OS)考虑并处理异常
Notes: For undefined instrs, hardware failure, or arith overflow – the OS normally kills the program and returns an indication of the reason to the user
For an I/O device request or an OS service call – the OS saves the state of the program, performs the desired task and, at some point in the future, restores the program to continue execution

## Slide 48: 两种类型的异常
中断 – 异步地执行程序
  由外部事件引发
  可能在指令之间处理，因而可以让流水全部完成后，再转到OS的中断处理程序
  仅仅是挂起然后恢复用户的程序
陷阱(异常) – 同步地执行程序
  由内部事件引发
  该指令的现场必须由陷阱程序补救处理，因此经常是在流水的中间停止非法指令并转到OS的陷阱处理程序
  重新执行非法指令(或由操作系统仿真)，程序可能继续运行也可能停止

## Slide 49: Where in the Pipeline Exceptions Occur
算术溢出
未定义指令
TLB错误 or 页错误
I/O 服务请求
硬件出错
ALU
IM
Reg
DM
Reg
阶段?
同步?
EX
yes
yes
yes
no
no
注意：一个时钟周期内可能会发生多个异常
ID
IF, MEM
any
any
Notes: For lecture
Note that an I/O service request is not associated with any executing instruction so can be handled when the hardware decides (to some limit) –i.e., pick the most convenient place to handle the exception

## Slide 50: 多发射流水线异常
I
n
s
t
r.
O
r
d
e
r
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
硬件会对异常进行排序，先中断处理最先出现的指令
Notes: For class handout

## Slide 51: 多发射流水线异常
I
n
s
t
r.
O
r
d
e
r
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
D$ page fault
arithmetic overflow
undefined instruction
I$ page fault
硬件会对异常进行排序，先中断处理最先出现的指令
Notes: For lecture

## Slide 52: MIPS 处理异常的数据通路和控制 (图 4-66)
Cause（状态） 寄存器：用于在一个时钟周期内记录下所有可能的异常，需要一个信号来控制该寄存器的写入 (CauseWrite)
EPC 寄存器：捕捉中断指令的地址，需要一个信号来控制该寄存器的写入 (EPCWrite)
  异常软件必须与异常指令一致
将异常处理程序的地址加载到PC
  扩展PC输入端的多选器，即新的输入端被硬连接到异常处理程序的地址 (例如8000 0180hex for arithmetic overflow)
A way to flush offending instruction and the ones that follow it

## Slide 53: 异常的数据通路控制
Read
Address
Instruction
Memory
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
RegFile
Read Data 1
ReadData 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
Branch
PCSrc
Forward
Unit
Hazard
Unit
0
1
0
Compare
Forward
Unit
Add
IF.Flush
0
8000 0180hex
Cause
EPC
EX.Flush
0
0
ID.Flush
Notes: (new) Figure 4.66

## Slide 54: 总结
所有的现代处理器都用流水技术来提高性能 (a CPI of 1 and fast a CC)
流水时钟由最慢的流水阶段决定 – 因此设计一个平衡的流水线是非常重要的
必须检测并解决冒险
  结构冒险 – 通过正确设计流水线解决
  数据冒险
    Stall (影响CPI)
    前向预测(要求硬件支持)
  控制冒险 – 将分支硬件尽可能放在流水线的前面阶段
    Stall (影响CPI)
    延迟分支 (要求编译器扶持)
    静态预测和动态预测 (要求硬件支持)
流水技术使异常处理更复杂