## Slide 1: 第四章：处理器-C
[Adapted from Computer Organization and Design, 4th Edition,
Patterson & Hennessy, © 2008, MK]
Courtesy for Mary Jane Irwin of PSU
Notes: Be aware that this first part of new chapter 4 is review for this class, so doesn’t go into detail. If your students are learning computer organization for the first time, this set of slides needs to be expanded greatly.

## Slide 2: Review: 流水线冒险
结构冒险
  通过设计流水线以消除结构冒险
数据冒险——写前读( read before write)
  在流水线内进行数据转发
  对于那些转发无法解决的数据冒险（如，装载-使用型数据冒险） 仍需要使用冒险控制硬件在指令流间插入阻塞（stall）
控制冒险– beq, bne,j,jr,jal
  阻塞 – 有损性能
  尽可能地将决策点提前，在流水线中越早做决策越好–减少阻塞的周期数，减少额外的硬件成本
  延迟决定(需要编译器的支持) –不适用于较深的流水线，（延迟决定）需要不止一个延迟槽
  预测–如果有更多的硬件支持，可进行分支预测缓存或者分支目标缓存。当(BHT)的预测正确或(BTB)缓存了分支目标指令时，控制冒险阻塞的影响会降低。

## Slide 3: 挖掘更高性能
增加流水线的深度以增加时钟速率–超流水线
  流水级越多, 就需要越多的转发/冒险硬件，也会造成更多的流水线开销- pipeline latch overhead （ pipeline latch overhead在时钟周期内所占的比例越来越大）
一个单时钟周期提取(以及执行) 多条指令(每个流水级容纳多条指令) – 多发射
  指令执行速率, CPI小于1, 因此使用IPC: 即每时钟周期执行的指令数
    例如，一个6 GHz 四路多发射微处理器能以每秒240亿指令的峰值速率执行，其最好情况下的CPI达到0.25，IPC达到4。
  假设数据通路有一条5级流水线，任何时刻能有多少条指令同时存在着？
Notes: Answer to the last question is, obviously, twenty!
Superpipelined processors have longer instruction latency than multiple issue processors which can degrade performance in the presence of true dependencies
Multiple issue processors are more susceptible to resource conflicts – but we can fix this with hardware and/or software !

## Slide 4: 并行的种类
程序中指令间的并行度(ILP)– 度量一个程序中同一时刻可并行执行的平均指令数
  很大程度上取决于与该指令有数据依赖和控制依赖关系的指令的数量
数据并行度(DLP)
DO I = 1 TO 100
A[I] = A[I] + 1
CONTINUE
处理器的机器并行度–度量处理器对程序的指令级并行(ILP)的利用能力
  取决于同一时刻可以提取和执行的指令数量
为了获得高性能，既需要ILP，又需要机器并行
Notes: The example shown has lots of data parallelism but almost no ILP. A good compiler could help with loop unrolling. If completely unrolled, and if had 100 arithmetic/addressing units and 100 memory ports, could achieve a speedup of 100 over a scalar processor

## Slide 5: 多发射处理器类型
静态多发射处理器 (亦称作 VLIW)
  (由编译器在编译期)静态地决定哪些指令要被同时执行
  例如IA-64架构的Intel 安腾和安腾2 (显式并行处理机)
    128-bit的指令包，每个指令包三条指令。 每一个指令由三个41-bits长的指令和一个5-bit长的模板字段组成(模板字段指明了每条指令所需功能单元类型)
    五类功能部件(IntALU, Mmedia, Dmem, FPALU, Branch)
    更多地支持推测和预测
动态多发射处理器 (亦成作 超标量-superscalar)
  （由硬件在运行时）动态地决定哪些指令同时执行 (in the range of 2 to 8)
  例如，IBM Power series, Pentium 4, MIPS R10K, AMD Barcelona

## Slide 6: 多发射流水线的任务
多发射流水线必须解决的问题：
  每个周期发射多少条指令– 发射槽
  存储 (数据) 依赖– 也就是数据冒险
    由于(usually) 较低的ILP，SS/VLIW多发射处理器的限制更严苛
  程序依赖 – 即控制冒险
    限制条件同上, 甚至更严格
    利用动态分支预测来解决ILP发射问题
  资源冲突– 即结构冒险
    一个SS/VLIW多发射处理器潜在更多的资源冲突
    功能单元可能需要仲裁result buses以及寄存器堆的写端口
    通过复制资源或者流水资源可以消除资源冲突
Notes: Pipelining is much less expensive than duplicating

## Slide 7: 推测
推测技术使得可能依赖于被推测指令的那些指令提早执行
  推测一条分支指令的输出结果 (branch prediction)
  推测一条load指令和它之前的那条store指令（假设store指令的地址是未知的）引用的不是同一个地址，这样load指令就可能可以在store指令执行前先得到执行。(load speculation)
必须包含的(hardware and/or software) 机制，以此来
  检测推测的正确性
  在推测错误时能消除错误推测所带来的影响。
忽略或者缓存由推测执行所引发的异常，直至可以确定异常会发生为止
Notes: In a VLIW processor the compiler can insert additional instr’s that check the accuracy of the speculation and can provide a fix-up routine to use when the speculation was incorrect
In SS, the processor buffers the speculative results until it knows they are no longer speculative, then allows the instructions to complete by allowing the contents of the buffers to be written to the registers or memory

## Slide 8: 静态多发射机 (VLIW)
静态多发射处理器 (亦称 VLIW) 使用编译器(在编译期) 静态地确定哪些指令同时发射和执行
  发射包：同一个时钟周期内发射的指令组成的集合 – 可被视为一条完成多个操作的长指令
  对一个时钟周期内能发射的多条指令有所限制 – 一条包含多个固定字段（预先定义好的字段）的长指令
  编译器通过静态分支预测和代码调度来减少或者防止冒险
VLIW’s have
  多个功能单元
  多个寄存器堆端口
  更宽的程序总线

## Slide 9: 例子: A VLIW MIPS
双发射MIPS指令
ALU Op (R format)
or
Branch (I format)
Load or Store (I format)
64 bits
指令都是成对被取指，译码和发射
  如果一对指令中的任一条不能被使用,那么用nop指令代替
需要4个读端口和2个写端口以及一个独立的加法器来计算内存地址

## Slide 10: A MIPS VLIW (双发射) 数据通路
Instruction
Memory
Add
PC
4
Write Data
Write Addr
Register
File
ALU
Add
Data
Memory
Sign
Extend
Add
Sign
Extend
没有冒险硬件
(所以不允许 load use )
Notes: Assume forwarding hardware as necessary.
What is the top mux input to the ALU doing?

## Slide 11: 代码调度的例子
考虑一下的循环代码
lp: lw $t0,0($s1) # $t0=array element
addu $t0,$t0,$s2 # add scalar in $s2
sw $t0,0($s1) # store result
addi $s1,$s1,-4 # decrement pointer
bne $s1,$0,lp # branch if $s1 != 0
必须“调度”这些指令以避免流水线阻塞
  一个指令包中的指令必须是相互独立的
  必须将装载-使用型指令与它们的loads隔开一个时钟周期
  前两条指令具有load-use相关性，后两条指令以及最后两条指令具有数据相关性
  假设硬件进行了极佳的分支预测

## Slide 12: The Scheduled Code (没展开)
四个时钟周期执行了5条指令
  CPI of 0.8 (versus the best case of 0.5)
  IPC of 1.25 (versus the best case of 2.0)
  Nop未计入性能计算中 !!
 | ALU or branch | Data transfer | CC
lp: |  | lw $t0,0($s1) | 1
 | addi $s1,$s1,-4 |  | 2
 | addu $t0,$t0,$s2 |  | 3
 | bne $s1,$0,lp | sw $t0,4($s1) | 4
 | ALU or branch | Data transfer | CC
lp: |  |  | 1
 |  |  | 2
 |  |  | 3
 |  |  | 4
 |  |  | 5
Notes: For lecture
Note that displacement value for the sw has to be adjusted because the addi has been scheduled before it rather than after it as in the original code.
Note load-use resolutions since addu is two cycles after its corresponding load

## Slide 13: 循环展开
循环展开– 循环体会被复制多份而且通过重叠不同循环体中的指令可以获得更高的指令集并行（ILP）
应用循环展开(拷贝4份循环体) ，然后调度产生的代码
  消除不必要的循环开销指令
  调度以避免load-use冒险
在循环展开过程中，编译器通过重命名寄存器(register renaming)来消除所有虚假的数据依赖

## Slide 14: Unrolled Code Example（展开）
lp: lw $t0,0($s1) # $t0=array element
lw $t1,-4($s1) # $t1=array element
lw $t2,-8($s1) # $t2=array element
lw $t3,-12($s1) # $t3=array element
addu $t0,$t0,$s2 # add scalar in $s2
addu $t1,$t1,$s2 # add scalar in $s2
addu $t2,$t2,$s2 # add scalar in $s2
addu $t3,$t3,$s2 # add scalar in $s2
sw $t0,0($s1) # store result
sw $t1,-4($s1) # store result
sw $t2,-8($s1) # store result
sw $t3,-12($s1) # store result
addi $s1,$s1,-16 # decrement pointer
bne $s1,$0,lp # branch if $s1 != 0

## Slide 15: The Scheduled Code (展开)
在8个时钟周期内执行了14条指令
  CPI of 0.57 (versus the best case of 0.5)
  IPC of 1.8 (versus the best case of 2.0)
 | ALU or branch | Data transfer | CC
lp: | addi $s1,$s1,-16 | lw $t0,0($s1) | 1
 |  | lw $t1,12($s1) | 2
 | addu $t0,$t0,$s2 | lw $t2,8($s1) | 3
 | addu $t1,$t1,$s2 | lw $t3,4($s1) | 4
 | addu $t2,$t2,$s2 | sw $t0,16($s1) | 5
 | addu $t3,$t3,$s2 | sw $t1,12($s1) | 6
 |  | sw $t2,8($s1) | 7
 | bne $s1,$0,lp | sw $t3,4($s1) | 8

## Slide 16: 谓词化
谓词化是一种通过将指令的执行与否与谓词联系起来以消除分支指令的技术，例如
  if (p) {statement 1} else {statement 2}
使用通常的编译方法，编译结果将含有两条分支指令。
谓词化后，这段代码将被编译为：
  (p) statement 1
  (~p) statement 2
(condition)部分表明其所指的代码仅在condition为真时才被执行
谓词化可以用来实现另一种消除分支的方法：推测执行
Notes: LEAVE THIS SLIDE IN HIDE MODE – NO LONGER COVERED IN BOOK AND A BIT MUCH DETAIL FOR THIS COURSE.
One conditional branch to the else portion of the code and one after code block 1 to skip the else code block

## Slide 17: 编译器对VLIW 处理器的支持
编译器将一组相互独立的指令封装形成指令包（bundle）
  通过代码重调度 (trace scheduling)
编译器通过循环展开来开发指令集并行度(ILP)
编译器通过寄存器重命名来消除名字依赖关系并确保不发生load-use 冒险
超标量处理器使用动态预测，而VLIW处理器主要依靠编译器来进行分支预测
  循环展开减少了分支条件数
  通过谓词化可以消除了if-then-else分支结构
  编译器预测memory bank references 来减少memory bank冲突

## Slide 18: VLIW 的优缺点
优点
  更简化的硬件 (潜在地消耗更少的功耗)
  可扩展性
  VLIW可以在每个指令包上包含更多的指令并增加更多的功能单元
缺点
  编程/编译复杂且需要更长的编译时间
    编译深流水线以及长延迟的程序时，编译时间不确定 (使得性能峰值不确定)
  Lock step operation：例如阻塞所有的将要发射的stall直至冒险被解决 (需要谓词化)
  目标 (二进制) 代码不兼容
  需要大量的程序内存带宽
  代码膨胀
    Nops 浪费了程序内存空间
    循环展开利用更多的程序内存空闲来开发并行度
Notes: Also need bigger RegFile since renaming uses programmer visible registers (not an RUU as with SS)

## Slide 19: 动态多发射机 (SS)
动态多发射处理器 (亦称作 SuperScalar超标量)利用硬件在运行时动态地确定同时发射以及执行的指令
指令的提取和发射– 取指并译码，然后将指令发送到功能单元执行
  Defines the Instruction lookahead capability – fetch, decode and issue instructions beyond the current instruction
指令-执行 – 只要源操作数和功能单元就绪，结果就被计算出来。
  Defines the processor lookahead capability –complete execution of issued instructions beyond the current instruction
指令-提交– 在确定安全时，将结果写回寄存器堆或者D$(例如，改变机器状态)

## Slide 20: 顺序 vs 乱序
取指令和译码单元必须能够顺序发射指令，以记录程序中的依赖关系
提交单元必须按照程序顺序将结果写回寄存器堆和存储器以使得
  当异常发生时，只有导致异常的那条指令之前的指令才能对寄存器状态进行修改
  当分支预测错误时，那些出现在错误预测的分支之后的指令不能改变机器的状态(例如，我们使用提交单元来改正不正确的推测)
虽然处理器的前端 (取指, 译码, 发射) 和后端(提交) 按照顺序操作指令, 各功能单元可以在获得所需数据的条件下随时开始执行过程
  允许乱序执行可以增加指令集并行度
Notes: To increase ILP, the processor has to be able to look beyond instructions with data, control, and structural hazards to find instructions downstream that can be executed

## Slide 21: 乱序执行
乱序执行时，后面的指令可能先于前面的指令执行，因此需要硬件解决read before write （Write after read） 以及write before write (write after write) 的数据冒险
  If the lw write to $t0 occurs after the addu write, then the sub gets an incorrect value for $t0
  The addu has an output dependency on the lw – write before write
    当它的结果能被前一个需执行更长时间的指令重写时，那么addu的发射可能要被阻塞。
lw $t0,0($s1)
addu $t0,$t1,$s2
. . .
sub $t2, $t0, $s2

## Slide 22: 反相关(Anti-dependencies)
需要处理反相关 – 当后面的指令 (较早执行) 产生的数据将会损坏前面指令(较晚执行)的源操作数
R3 := R3 * R5
R4 := R3 + 1
R3 := R5 + 1
这种约束关系类似于数据依赖, except reversed
  Instead of the later instruction using a value (not yet) produced by an earlier instruction (read before write, write after read), the later instruction produces a value that destroys a value that the earlier instruction (has not yet) used (write before read)
Antidependency (WAR)
True data dependency (RAW)
Output dependency (WAW)

## Slide 23: 复习：依赖
3种数据依赖
  真实数据依赖(read after write)
  反相关依赖(write after read)
  输出依赖(write after write)
通过使用寄存器来维持 (或是其它存储位置)
真实代表一个程序内数据和信息的流动
反相关和输出依赖的出现是因为寄存器数量有限，程序员滥用数量有限的寄存器而导致存储冲突
存储冲突
Notes: Storage conflicts, like other resource conflicts can be reduced or eliminated by duplicating the troublesome resource

## Slide 24: 存储冲突和寄存器重命名
通过增加或者复制有问题的资源可以减少或者消除存储冲突
  通过提供额外的寄存器来重建寄存器与数值之间的一致性
    在动态多发射处理器中由硬件动态地分配
寄存器重命名–重命名以消除反相关
R3b := R3a * R5a
R4a := R3b + 1
R3c := R5a + 1
  寄存器重命名，目的是为了消除一些虚假的数据依赖，而这种数据依赖并非一个真实的数据相关，只是因为重用寄存器名引起的相关，也称为名字相关。所以通过寄存器重命名可以消除。
R3 := R3 * R5
R4 := R3 + 1
R3 := R5 + 1

## Slide 25: 校正的数据转发控制条件
MEM 转发单元:
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (EX/MEM.RegisterRd != ID/EX.RegisterRs)
and (MEM/WB.RegisterRd = ID/EX.RegisterRs))
ForwardA = 01
if (MEM/WB.RegWrite
and (MEM/WB.RegisterRd != 0)
and (EX/MEM.RegisterRd != ID/EX.RegisterRt)
and (MEM/WB.RegisterRd = ID/EX.RegisterRt))
ForwardB = 01
EX 转发单元:
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRs))
ForwardA = 10
if (EX/MEM.RegWrite
and (EX/MEM.RegisterRd != 0)
and (EX/MEM.RegisterRd = ID/EX.RegisterRt))
ForwardB = 10
Forwards the result from the previous instr. to either input of the ALU
Forwards the result from the previous or second previous instr. to either input of the ALU

## Slide 26: 总结: 获取更高性能
为了获得更高的性能，即需要机器并行也需要指令级并行，通过
  Superpipelining（超流水线）
  Static multiple-issue (VLIW)（静态多发射）
  Dynamic multiple-issue (superscalar)（动态多发射）
处理器的指令发射以及执行策略会影响指令集并行度
  顺序取指、发射和提交以及乱序执行
    流水线会产生真实的依赖 (read after write)
    乱序执行产生反相关 (write after read)
    乱序执行产生输出依赖(write after write)
    顺序提交允许推测(to increase ILP)而且被要求执行准确的中断
寄存器重命名可以解决这些存储依赖
Notes: Use data forwarding and compiler scheduling to help with read before write
Use register renaming to help with write before read and write before write
Procedural dependencies – aka control hazards
  Use aggressive branch prediction (speculation)
  Use predication
Resource conflicts – aka structural hazards
  Use resource duplication or resource pipelining to reduce (or eliminate) resource conflicts
  Use arbitration for result and commit buses and register file read and write ports

## Slide 27: SimpleScalar Structure
sim-outorder: supports out-of-order execution (with in-order commit) with a Register Update Unit (RUU)
  Uses a RUU for register renaming and to hold the results of pending instructions. The RUU (aka reorder buffer (ROB)) retires (i.e., commits) completed instructions in program order to the RegFile
  Uses a LSQ for store instructions not ready to commit and load instructions waiting for access to the D$
  Loads are satisfied by either the memory or by an earlier store value residing in the LSQ if their addresses match
    Loads are issued to the memory system only when addresses of all previous loads and stores are known

## Slide 28: SS Pipeline Stage Functions
Fetch multiple instructions
Decode and issue instr
Wait for source operands to be Ready and FU free, schedule Result Bus and execute instruction
Copy Result Bus data to matching waiting sources
Write dst contents to RegFile or Data Memory
FETCH
DECODE & ISSUE
EXECUTE
WRITE
BACK
RESULT
COMMIT
In Order
In Order
Out of Order
In Order
ruu_fetch()
ruu_dispatch()
ruu_issue()
lsq_refresh()
ruu_writeback()
ruu_commit()

## Slide 29: Simulated SimpleScalar Pipeline
ruu_fetch(): fetches instr’s from one I$ line, puts them in the fetch queue, probes the cache line predictor to determine the next I$ line to access in the next cycle
    fetch:ifqsize<size>: fetch width (default is 4)
    fetch:speed<ratio>: ratio of the front end speed to the execution core (<ratio> times as many instructions fetched as decoded per cycle)
    fetch:mplat<cycles>: branch misprediction latency (default is 3)
ruu_dispatch(): decodes instr’s in the fetch queue, puts them in the dispatch (scheduler) queue, enters and links instr’s into the RUU and the LSQ, splits memory access instructions into two separate instr’s (one to compute the effective addr and one to access the memory), notes branch mispredictions
    decode:width<insts>: decode width (default is 4)

## Slide 30: SimpleScalar Pipeline, con’t
ruu_issue()and lsq_refresh(): locates and marks the instr’s ready to be executed by tracking register and memory dependencies, ready loads are issued to D$ unless there are earlier stores in LSQ with unresolved addr’s, forwards store values with matching addr to ready loads
    issue:width<insts>: maximum issue width (default is 4)
    ruu:size<insts>: RUU capacity in instr’s (default is 16, min is 2)
    lsq:size<insts>: LSQ capacity in instr’s (default is 8, min is 2)
and handles instr’s execution – collects all the ready instr’s from the scheduler queue (up to the issue width), check on FU availability, checks on access port availability, schedules writeback events based on FU latency (hardcoded in fu_config[])
    res:ialu | imult | memport | fpalu | fpmult<num>: number of FU’s (default is 4 | 1 | 2 | 4 | 1)

## Slide 31: SimpleScalar Pipeline, con’t
ruu_writeback(): determines completed instr’s, does data forwarding to dependent waiting instr’s, detects branch misprediction and on misprediction rolls the machine state back to the checkpoint and discards erroneously issued instructions
ruu_commit(): in-order commits results for instr’s (values copied from RUU to RegFile or LSQ to D$), RUU/LSQ entries for committed instr’s freed; keeps retiring instructions at the head of RUU that are ready to commit until the head instr is one that is not ready

## Slide 32: CISC vs RISC vs SS vs VLIW
 | CISC | RISC | Superscalar | VLIW
Instr size | variable size | fixed size | fixed size | fixed size (but large)
Instr format | variable format | fixed format | fixed format | fixed format
Registers | few, some special Limited # of ports | Many GP Limited # of ports | GP and rename (RUU) Many ports | many, many GP Many ports
Memory reference | embedded in many instr’s | load/store | load/store | load/store
Key Issues | decode complexity | data forwarding, hazards | hardware dependency resolution | (compiler) code scheduling

## Slide 33: Evolution of Pipelined, SS Processors
 | Year | Clock Rate | # Pipe Stages | Issue Width | OOO? | Cores/Chip | Power
Intel 486 | 1989 | 25 MHz | 5 | 1 | No | 1 | 5 W
Intel Pentium | 1993 | 66 MHz | 5 | 2 | No | 1 | 10 W
Intel Pentium Pro | 1997 | 200 MHz | 10 | 3 | Yes | 1 | 29 W
Intel Pentium 4 Willamette | 2001 | 2000 MHz | 22 | 3 | Yes | 1 | 75 W
Intel Pentium 4 Prescott | 2004 | 3600 MHz | 31 | 3 | Yes | 1 | 103 W
Intel Core | 2006 | 2930 MHz | 14 | 4 | Yes | 2 | 75 W
Sun USPARC III | 2003 | 1950 MHz | 14 | 4 | No | 1 | 90 W
Sun T1 (Niagara) | 2005 | 1200 MHz | 6 | 1 | No | 8 | 70 W