## Slide 1: 第五章：存储器层次结构-B
[Adapted from Computer Organization and Design, 4th Edition,
Patterson & Hennessy, © 2008, MK]
Courtesy for Mary Jane Irwin of PSU
Notes: Be aware that this first part of new chapter 4 is review for this class, so doesn’t go into detail. If your students are learning computer organization for the first time, this set of slides needs to be expanded greatly.

## Slide 2: Review: 一台计算机的主要部件
处理器
控制器
数据通路
存储器
设备
输入
输出
高速缓存
主存
辅助存储器
（硬盘）

## Slide 3: 处理器 – 存储器 的性能差距
“Moore’s Law”
µProc
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Processor-Memory
Performance Gap (grows 50%/year)
Notes: HIDDEN SLIDE – KEEP?
Memory baseline is a 64KB DRAM in 1980, with three years to the next generation until 1996 and then two years thereafter with a 7% per year performance improvement in latency.
Processor assumes a 35% improvement per year until 1986, then a 55% until 2003, then 5%
Need to supply an instruction and a data every clock cycle
In 1980 there were no caches (and no need for them), by 1995 most systems had 2 level caches (e.g., 60% of the transistors on the Alpha 21164 were in the cache)

## Slide 4: The “Memory Wall”
处理器和DRAM的速度差异持续增加
Clocks per instruction
Clocks per DRAM access
良好的存储器层次结构（cache）设计对系统整体性能越来越重要

## Slide 5: 存储器层次结构的目标
Fact: 容量大的存储器速度慢，速度快的存储器容量较小
我们怎么创建让人感觉又大又便宜又快的存储器？ (绝大部分时间是这样)?
  层次化
  并行

## Slide 6: 一种典型的存储器层次结构
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
ITLB
DTLB
Speed (%cycles): ½’s 1’s 10’s 100’s 10,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Cost: highest lowest
局部性原理的应用和快速发展的技术使用户能够有越来越多、越来越快的存储器可供使用。
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 7: 存储器层次结构技术
Caches 由 SRAM 实现，追求速度和技术兼容性
  快 (typical access times of 0.5 to 2.5 nsec)
  低密度 (6 transistor cells)，高功率，价钱高 ($2000 to $5000 per GB in 2008)
  静态: 内容将会“永远存在” (只要不断电)
主存由 DRAM 实现，追求容量 （大容量）
  更慢 (typical access times of 50 to 70 nsec)
  高密度 (1 transistor cells)，低功率，价钱更低 ($20 to $75 per GB in 2008)
  动态: 需要定期“刷新”(every 8 ms定期刷新)
    消耗1% to 2% DRAM 活动周期
  地址分为2半 (行和列)
    RAS or Row Access Strobe（行地址） triggering the row decoder
    CAS or Column Access Strobe （列地址）triggering the column selector
Notes: Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times

## Slide 8: 存储器层次结构: Why Does it Work?
时间局部性(locality in time)
  如果某个数据项被访问，那么在不久的将来它可能再次被访问。
   使最近被访问的数据项离处理器更近
空间局部性 (locality in space)
  如果某个内存区域的数据项被访问，那么在不久的将来，与它地址相邻的数据项可能再次被访问。
  使包含连续字的内存块离处理器更近
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 9: 存储器层次结构的一些术语
块或行(block or line): 可存在于或不存在于cache中的信息的最小单元
命中率(Hit Rate): 在高层存储器中找到目标数据的存储访问比例
  命中时间 Hit Time: 访问某存储器层次结构所需要的时间，包括了判断当前访问是命中还是缺失所需的时间
缺失率(Miss Rate): 在高层存储器中没有找到目标数据的存储访问比例 1 - (Hit Rate)
  缺失代价 Miss Penalty: 将相应的块从低层存储器替换到高层存储器所需的时间，包括访问块、将数据逐层传输、将数据插入发生缺失的层和将信息块传送给请求者的时间。
命中时间 << 缺失代价
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the Upper level. Then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.

## Slide 10: 存储器层次结构的特征
访问时间随离CPU距离的增加而增加
L1$
L2$
Main Memory
Secondary Memory
Processor
每一层中存储器的（相对）容量大小：
离处理器越远，容量越大
Inclusive– what is in L1$ is a subset of what is in L2$ is a subset of what is in MM that is a subset of is in SM (这其实是为了说明存储器是一个真正的层次结构)
4-8 bytes (word)
1 to 4 blocks
1,024+ bytes (disk sector = page)
8-32 bytes (block)
Notes: Because the upper level is smaller and built using faster memory parts, its hit time will be much smaller than the time to access the next level in the hierarchy (which is the major component of the miss penalty).

## Slide 11: 如何管理存储器层次结构
寄存器  存储器
  by 编译器(程序员?)
高速缓存  主存
  by 缓存控制器硬件
主存  硬盘（外存）
  by 操作系统 (虚拟内存)
  通过TLB实现虚拟地址到物理地址的转换
  by 程序员 (files)

## Slide 12: 高速缓存基础知识
需要解决的两个问题(in hardware):
  Q1: 怎么知道一个数据项是否在高速缓存中?
  Q2: 如果在，又怎么找到它?
直接映像
  每个主存地址对应于高速缓存中一个确定地址
    Cache中每个位置可能对应于主存中多个不同的地址
  地址映射(to answer Q2):
  ( 块地址 ) modulo ( cache中的块数 )
  由于每个高速缓存的地址可能对应于主存中多个不同的地址，我们怎么知道高速缓存中的数据项是否就是所请求的字呢？也就是说，怎么才能知道所请求的字是否在高速缓存中(问题1)？可以考虑在高速缓存中加些标记(tag)，这些标记必须包含能够判断高速缓存中的字是否为所请求字的地址信息。标记只需包含地址的高位部分，即地址中没有用作检索cache的那些位。

## Slide 13: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q2: How do we find it?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q1: Is it there?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache (cache的Tag和主存的高2位比较)
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits define the byte in the word (32b words)
(块地址) 取模 (高速缓存中块的数目)
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 14: 直接映射高速缓存
0
1
2
3
4
3
4
15
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(2)
miss
miss
miss
miss
miss
miss
hit
hit
00 Mem(0)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01
4
11
15
00 Mem(1)
00 Mem(2)
00 Mem(3)
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 6 misses
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 15: MIPS直接映射高速缓存的例子
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
What kind of locality are we taking advantage of?
（利用了哪种局部性）
20
Data
32
Hit
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 16: Multiword Block直接映射高速缓存
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
Four words/block, cache size = 1K words
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 17: 利用空间局部性
0
Let cache block hold more than one word
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
00 Mem(1) Mem(0)
miss
00 Mem(1) Mem(0)
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
01
5
4
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
miss
11
15
14
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 4 misses
Notes: For lecture
Show the 4-bit address mapping – 2-bits of tag, 1-bit of set address (index), 1-bit of word-in-block select

## Slide 18: 缺失率vs 块大小vs 高速缓存大小
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
较大的cache块能更好地利用空间局部性以降低缺失率。增加块大小通常会引起缺失率下降。而当块大小在cache容量中所占比例增加到一定程度时，缺失率会随之增加。这是因为此时cache中块的数量变得很少，导致这些块之间的竞争加大，造成一个块中的数据在被多次访问之前就被替换出cache (increasing capacity misses )。
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 19: Cache各字段大小
Cache不仅存储数据而且存储标记位 (既包括数据位，又包括标记位)
  32位字节地址
  直接映射cache，cache大小为2n 个块，因此，n位用作索引。
  块大小为2m 个字 (2m+2 个字节), m 位用于查找块中的字，两位是字节偏移信息。
标记域的大小？
标记域的大小为 32–(n+m+2)
直接映射的cache的总位数为
2n x (块大小+ 标记域大小+ 有效位域大小)
假设一个直接映射的cache，有16KB的数据，块大小为4个字，地址为32位，那么该cache总共需要多少位？
Notes: The tag field is 32 – (n+m+2)
16KB is 4K (2^12 words). With a block size of 4 words, there are 1024 (2^10) blocks. Each block has 4x32 or 128 bits of data plus a tag which is 32 – 10 -2 – 2 bits, plus a valid bit. So the total cache size is
2^10 x (4x32 +18 + 1) = 2^10 x 147 = 147Kbits (or about 1.15 times as many as needed just for storage of the data).

## Slide 20: Cache 命中处理
Read hits (指令cache和 数据cache) 读命中
  this is what we want!
Write hits (只有数据cache) 写命中
  需要高速缓存和主存一致(consistent)
    将数据同时写入cache和主存中，这就是写直达法 (write-through)。
    当一个数据在等待被写入主存时，先将它放入写缓冲(write buffer)中。写缓冲就是一个保存等待写入主存数据的缓冲队列，当写缓存满时才被阻塞。
  允许高速缓存和主存不一致(inconsistent)
    只把数据写入cache中 (写回机制write-back：当发生写操作时，新值仅仅被写入cache块中，只有当修改过的块被替换时才写到较低层存储结构)。
    当将数据写回时，对于每个cache数据块来说，需要一个dirty bit 来分辨数据是否需要被写回主存 - 可以使用写缓冲来帮助缓存这些“脏(dirty )”的数据块。
Notes: In a write-back cache, because we cannot overwrite the block (since we may not have a backup copy anywhere), stores either require two cycles (one to check for a hit, followed by one to actually do the write) or require a write buffer to hold that data (essentially pipelining the write).
By comparison, a write-through cache can always be done in one cycle assuming there is room in the write buffer. Read the tag and write the data in parallel. If the tag doesn’t match, the generate a write miss to fetch the rest of that block from the next level in the hierarchy (and update the tag field).

## Slide 21: 高速缓存缺失的来源
强制缺失:
  对从没有在cache中出现的块第一次进行访问引起的缺失
  解决方法：增大块大小(特别大的块能够增大缺失率)
容量缺失:
  由于cache容纳不了一个程序执行所需要的所有块而引起的cache缺失
  解决方案: 增大cache大小(可能增大访问时间)
冲突缺失:
  多个内存区都映射到同一个cache区域，即很多块竞争同一个组
  方案 1: 增加cache大小
  方案 2: 增加关联性(stay tuned) (可能增大访问时间)
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 22: 高速缓存缺失处理(Single Word Blocks单字)
(指令cache和数据cache) 读缺失
  stall the pipeline, fetch the block from the next level in the memory hierarchy, install it in the cache and send the requested word to the processor, then let the pipeline resume
(只有数据cache) 写缺失
  stall the pipeline, fetch the block from next level in the memory hierarchy, install it in the cache (which may involve having to evict a dirty block if using a write-back cache), write the word from the processor to the cache, then let the pipeline resume
  写分配 Write allocate – 只把字写入cache中，更新标记域和数据域字段, 没必要去检测cache是否命中，没必要去阻塞。
  写时不分配 No-write allocate – 跳过cache write ，(but must invalidate that cache block since it will now hold stale data)，只把字写入写缓冲 (最终是写入下一级存储器中), 如果写缓冲没满，是没必要阻塞的。
Notes: Let’s look at our 1KB direct mapped cache again.
Assume we do a 16-bit write to memory location 0x000000 and causes a cache miss in our 1KB direct mapped cache that has 32-byte block select.
After we write the cache tag into the cache and write the 16-bit data into Byte 0 and Byte 1, do we have to read the rest of the block (Byte 2, 3, ... Byte 31) from memory?
If we do read the rest of the block in, it is called write allocate. But stop and think for a second. Is it really necessary to bring in the rest of the block on a write miss?
True, the principle of spatial locality implies that we are likely to access them soon.
But the type of access we are going to do is likely to be another write.
So if even if we do read in the data, we may end up overwriting them anyway so it is a common practice to NOT read in the rest of the block on a write miss.
If you don’t bring in the rest of the block, or use the more technical term, Write Not Allocate, you better have some way to tell the processor the rest of the block is no longer valid.
This bring us to the topic of sub-blocking.

## Slide 23: Multiword Block Considerations
读缺失(指令cache和数据cache)
  Processed the same as for single word blocks – a miss returns the entire block from memory
  缺失代价随着块大小增大而增大
    提前重启Early restart – 当块中所需字一旦返回就马上继续执行
    请求字优先Requested word first – 重新组织存储器，使得被请求的字先从存储器传到cache中，然后再传送该块的剩余部分
  Nonblocking cache – 允许cache在处理先前的缺失时，处理器能够继续访问cache。
写缺失(数据cache)
  如果使用写分配，必须先从存储器中获取块，然后再将字写入块中 (or could end up with a “garbled” block in the cache (e.g., for 4 word blocks, a new tag, one word of data from the new block, and three words of data from the old block)
Notes: Early restart works best for instruction caches (since it works best for sequential accesses) – if the memory system can deliver a word every clock cycle, it can return words just in time. But if the processor needs another word from a different block before the previous transfer is complete, then the processor will have to stall until the memory is no longer busy.
Unless you have a nonblocking cache that come in two flavors
Hit under miss – allow additional cache hits during a miss with the goal of hiding some of the miss latency
Miss under miss – allow multiple outstanding cache misses (need a high bandwidth memory system to support it)

## Slide 24: 支持cache的存储系统
片下连接和存储器体系结构 能够很显著地影响整个系统的性能
CPU
Cache
DRAM
Memory
bus
一个字宽的存储组织
(一个字宽的总线和一个字宽的存储器)
假定
  发送地址需要一个存储器总线时钟周期
  获取DRAM块中的第1个字需要15个存储器总线时钟周期(row cycle time行周期时间), 访问第2,3,4个字需要5个存储器总线时钟周期 (column access time列访问时间)
  传送一个数据字需要1个存储器总线时钟周期
Memory-Bus to Cache bandwidth
  在每个存储器总线时钟周期内从存储器获取，并转移到cache/CPU的字节数
32-bit data
&
32-bit addr
per cycle
on-chip
Notes: We can reduce the miss penalty if we can increase the bandwidth from the memory to the cache. Allows larger block sizes to be used while still maintaining a low miss penalty.
The clock rate of this bus is usually much slower than the processor which negatively affects the miss penalty

## Slide 25: 复习: (DDR) SDRAM Operation
N rows
N cols
DRAM
Column
Address
M-bit Output
M bit planes
N x M SRAM
Row
Address
After a row is read into the SRAM register
  Input CAS as the starting “burst” address along with a burst length
  Transfers a burst of data (ideally a cache block) from a series of sequential addr’s within that row
    The memory bus clock controls transfer of successive words in the burst
+1
Row Address
CAS
RAS
Col Address
1st M-bit Access
2nd M-bit
3rd M-bit
4th M-bit
Cycle Time
Row Add

## Slide 26: 一个字宽的总线, 一个字宽的块
CPU
Cache
DRAM
Memory
bus
on-chip
If the block size is one word, then for a memory access due to a cache miss, the pipeline will have to stall for the number of cycles required to return one data word from memory 求cycle数
  用于发送地址的存储器总线时钟周期数
  用于读DRAM的存储器总线时钟周期数
  用于返回数据的存储器总线时钟周期数
  缺失代价耗费的总的时钟周期数
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle 求字节数
  1
  15
  1
  17
  4/17 = 0.235
Notes: For lecture

## Slide 27: 1个字宽的总线, 4个字宽的块
CPU
Cache
DRAM
Memory
bus
on-chip
What if the block size is four words and each word is in a different DRAM row?
  用于发送1st address的时钟周期数
  用于读 DRAM的时钟周期数
  用于返回最后一个数据字的时钟周期数
  缺失代价耗费的总的时钟周期数
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
15 cycles
15 cycles
15 cycles
15 cycles
1
  4 x 15 = 60
  1
  62
  (4 x 4)/62 = 0.258
Notes: For lecture

## Slide 28: 1个字宽的总线, 4个字宽的块
CPU
Cache
DRAM
Memory
bus
on-chip
What if the block size is four words and all words are in the same DRAM row?
  发送1st 地址的时钟周期数
  读DRAM的时钟周期数
  返回最后一个数据字的时钟周期数
  缺失代价耗费的总的时钟周期数
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
15 cycles
5 cycles
5 cycles
5 cycles
1
15 + 3*5 = 30
  1
  32
  (4 x 4)/32 = 0.5
Notes: For lecture

## Slide 29: Interleaved Memory, One Word Wide Bus
For a block size of four words
  发送 1st 地址的时钟周期数
  读DRAM banks的时钟周期数
  返回最后一个数据字的时钟周期数
  缺失代价耗费的总的时钟周期数
CPU
Cache
bus
on-chip
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
15 cycles
15 cycles
15 cycles
15 cycles
  (4 x 4)/20 = 0.8
1
15
  4*1 = 4
  20
DRAM
Memory
bank 1
DRAM
Memory
bank 0
DRAM
Memory
bank 2
DRAM
Memory
bank 3
Notes: For lecture
The width of the bus and the cache need not be changed, but sending an address to several banks permits them all to read simultaneously. Interleaving retains the advantage of incurring the full memory latency only once.
Low order interleaving (low order bits select bank, high order bits used to access DRAM banks in parallel).
Low order memory interleaving, i.e.,
Bank 0 holds addresses xx…xx00
Bank 1 holds addresses xx…xx01
Bank 2 holds addresses xx…xx10
Bank 3 holds addresses xx…xx11
May want to add another example where you also have a wide bus (e.g., a 2 word bus between the interleaved memory and the processor).

## Slide 30: DRAM 存储系统总结
匹配cache的特性很重要
  caches 一次访问一个块 ( 通常大于一个字 )
具有DRAM的特性
  使用支持快速多字访问的DRAMs 以及和cache的块大小匹配的DRAMs
具有存储器-总线的特性
  确保存储器-总线可以支持DRAM的访问速度和模式
  目标是增大Memory-Bus to Cache 的带宽

## Slide 31: Cache性能的评估
假定cache访问命中的开销是CPU正常执行周期的一部分，因此有：
CPU time = IC × CPI × CC
  = IC × (CPIideal + Memory-stall cycles) × CC
CPIstall
存储器阻塞的时钟周期来源于cache缺失 (存储器阻塞的时钟周期可以定义为读操作和写操作引起的阻塞的时钟周期数之和)
读操作阻塞的时钟周期数 =
  读的次数/程序× 读缺失率× 读缺失代价
  写操作阻塞的时钟周期数=
  (写的次数/程序× 写缺失率 ×写缺失代价) + 写缓冲区阻塞
对于采取写直达的caches, 可以简化为
存储器阻塞时钟周期= 存储器访问次数/程序× 缺失率× 缺失代价
Notes: Reasonable write buffer depth (e.g., four or more words) and a memory capable of accepting writes at a rate that significantly exceeds the average write frequency means write buffer stalls are small

## Slide 32: cache性能对处理器性能的影响
只提高处理器性能 (faster clock rate and/or lower CPI)，不改进存储系统，会使相关的cache代价增大
  主存系统不可能和处理器周期时间提高得同样快。当计算 CPIstall 时，在处理器时钟周期内cache的缺失代价是需要计算的，以用于处理cache缺失
  CPIideal 越低，时钟周期阻塞（停顿）的影响越显著
处理器的理想CPI为2，每次缺失的代价为100个时钟周期，全部load和store的频率为36%，指令cache的缺失率为2%，数据cache的缺失率为4%，有：
Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  So CPIstalls = 2 + 3.44 = 5.44
比理想的CPI两倍还多！
如果CPIideal 降为1，0.5， 0.25会怎样？
如果数据cache缺失率为为1% ， 2%会怎样?
如果处理器时钟周期速率加倍会怎样(doubling the miss penalty)?
Notes: For ideal CPI = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time (so hit time is 1 cycle) is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 33: 平均处理器访问时间(AMAT)
一个大容量的cache的访问时间会比较长。如果命中时间增加，那么可能相当于又增加了一级流水线。在某种程度上，大容量cache命中时间的增加反而会抵消命中率改进带来的好处，导致处理器性能的下降。
平均处理器访问时间(AMAT)是综合考虑了命中、缺失以及不同访问的频率后得出的访存平均时间，有：
  AMAT = 命中时间+ 缺失率x 缺失代价
处理器时钟周期的时间为20微秒， 缺失代价为50个时钟周期，缺失率为每条指令0.02次缺失，cache访问时间为1个时钟周期，求AMAT？
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 34
定量分析
· 命中率：
其中： Nc表示Cache完成存取的总次数；
Nm表示主存完成存取的总次数

## Slide 35
· Cache-主存系统的平均访问时间(ta)
若: tc表示命中Cache的访问时间
tm表示命中主存的访问时间
则ta为：
希望： ta  tC
花比较小的硬件代价

## Slide 36: #1 降低Cache缺失率
允许更灵活地放置块
在直接映射的cache中，一个内存块只能放在一个明确的位置
在另一种极端方式中：一个块是允许放置在cache中的任何位置– 全相联cache
介于直接映射和全相联之间的设计是：组相联。一个n路组相联cache由很多组构成，每个组中有n块。根据索引域，存储器中的每个块对应到cache中唯一的组，并且可以放到这个组的任意一个位置上(因为有n块，所以有n 种选择) 。
(块地址/块号) 模(cache中组的个数)
Notes: All of the tags of all of the elements of the set must be searched for a match.

## Slide 37: Another Reference String Mapping
0
4
0
4
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
01
4
00 Mem(0)
01
4
00 Mem(0)
01
4
01 Mem(4)
0
00
01 Mem(4)
0
00
Start with an empty cache - all blocks initially marked as not valid
Ping pong effect due to conflict misses - two memory locations that map into the same cache block
  8 requests, 8 misses
Notes: For class handout

## Slide 38: 组相联Cache例子
0
Cache
Main Memory
Q2: 怎么定位?
Use next 1 low order memory address bit
(红色部分,紧接着蓝色的高1位) to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q1: 是否在?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache (cache的Tag位和主存的高3位比较)
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Set
1
0
1
Way
0
1
One word blocks
Two low order bits define the byte in the word (32b words)
Notes: For lecture
This picture is as opposed to
Way 0
both red Set 0
Way 1
------------------------------------
Way 0
both green Set 1
Way 1

## Slide 39: Another Reference String Mapping
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping pong effect in a direct mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 40: 四路组相联Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 41: 组相联Cache的范围
如果cache的总大小保持不变，提高关联度就增加了每组中块的数目，即并行检索时所需同时比较的次数：关联度每增加到2倍就会使每组块数加倍而使组数减半。因此，关联度每增加1倍，就会使下标减少1位，标记增加1位。
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Tag is all the bits except
block and byte offset
只有1组，即全相联
Direct mapped
(only one way)
Smaller tags, only a single comparator
只有1路，即直接映像，只需一个比较器
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Notes: For lecture
In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs

## Slide 42: 组相联Cache的成本
当cache缺失发生时，如何选择被替换的块呢？
  最近最少使用法(LRU): 被替换的那块是最久没有使用的那一块
    需要一个硬件来追踪每一块的相对使用情况
    对于一个两路组相联cache，每个组需要保留一位 → 当某一块被访问时，就设置它所对应的的这一位 (and reset the other way’s bit)
N路组相联cache 的成本
  N个比较器(delay and area)
  在数据准备好前的多选器延迟(set selection组的选择)
  数据在多路选择 (以及 Hit/Miss decision)之后准备好. 而在直接映射cache中，在Hit/Miss decision之前， 数据已经准备好了。
  所以先假定会命中，然后等缺失发生以后进行恢复，是不可行的。
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 43: 组相联Cache的优势
选择直接映射还是组相联是取决于：丢失的代价 vs 实现的成本
Data from Hennessy & Patterson, Computer Architecture, 2003
（上图为5-30）最大的改进出现在直接映射变化到两路组相联，缺失率下降了20% - 30%
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 44: 降低cache缺失率的方法
使用多级cache结构减少缺失代价
随着先进技术的发展，芯片上已经有空间使用较大的一级cache，或者增加额外的第二级cache（有指令cache和数据cache），甚至一些情况下还有第三级cache
假定理想的CPI为2，到主存的缺失代价为100 cycle（可以理解为访问主存的时间）, 到二级cache的缺失代价为 25 cycle（可以理解为访问二级cache的时间） ，load和store的频率为36% , 在一级指令cache和一级数据cache的缺失率分别为 2% (4%), 在二级cache的缺失率为0.5%。注：缺失率定义为在某一层的缺失访问次数与从cpu的角度看，对内存总访问次数的比例。
  CPIstalls = 2 + .02×25 + .36×.04×25 + .005×100 + .36×.005×100 = 3.54 (as compared to 5.44 with no L2$)
Notes: Also reduces cache miss penalty

## Slide 45: 多级Cache的设计考虑
一级cache和二级cache的设计思想明显不同
  一级cache（单级cache）主要致力于减少命中时间而获得较短的时钟周期或者较少的流水级
    一级cache容量小
  二级cache则主要针对于改善缺失率以减少长时间的访存代价 - 二级cache容量较大
    具有较高的关联度
因为有了二级cache的存在，一级cache的缺失代价得到显著降低– 所以相对于单级cache，两级cache中第一级cache的容量更小(更快)，但是缺失率更高
对于二级cache来说，命中时间没有缺失率那么重要
  2级cache的命中时间决定了1级cache的缺失代价
  2级cache的局部缺失率 >>全局缺失率
Notes: Global miss rate – the fraction of references that miss in all levels of a multilevel cache. The global miss rate dictates how often we must access the main memory.
Local miss rate – the fraction of references to one level of a cache that miss

## Slide 46: 两个机器的Cache参数
 | Intel Nehalem | AMD Barcelona
L1 cache organization & size | Split I$ and D$; 32KB for each per core; 64B blocks | Split I$ and D$; 64KB for each per core; 64B blocks
L1 associativity | 4-way (I), 8-way (D) set assoc.; ~LRU replacement | 2-way set assoc.; LRU replacement
L1 write policy | write-back, write-allocate | write-back, write-allocate
L2 cache organization & size | Unified; 256MB (0.25MB) per core; 64B blocks | Unified; 512KB (0.5MB) per core; 64B blocks
L2 associativity | 8-way set assoc.; ~LRU | 16-way set assoc.; ~LRU
L2 write policy | write-back | write-back
L2 write policy | write-back, write-allocate | write-back, write-allocate
L3 cache organization & size | Unified; 8192KB (8MB) shared by cores; 64B blocks | Unified; 2048KB (2MB) shared by cores; 64B blocks
L3 associativity | 16-way set assoc. | 32-way set assoc.; evict block shared by fewest cores
L3 write policy | write-back, write-allocate | write-back; write-allocate

## Slide 47: 有限状态机(FSM) Cache 控制器
一个简单的一级cache的关键特征
  直接映射
  写回机制采用写分配策略
  块大小为4个字（16个字节）
  cache大小为16KB(1024 个块)
  18位的标记位，10位的cache索引位，2位的块偏移位，2位的字节偏移位，如果是组相联，还有重写位，有效位，以及LRU位
Cache
&
Cache
Controller
1-bit Read/Write
Processor
DDR SDRAM
1-bit Valid
32-bit address
32-bit data
32-bit data
1-bit Ready
1-bit Read/Write
1-bit Valid
32-bit address
128-bit data
128-bit data
1-bit Ready
Notes: A blocking cache so the processor must wait until the cache has finished this request
Memory controller will notify the Cache Controller via the Ready signal when the memory read or write is finished

## Slide 48: 四状态Cache 控制器
空闲
比较标记
如果有效且命中，那么
设置有效位和标记位；
如果是写操作，
还要设置重写位
分配
从主存读取一个
新的cache块
写回
将旧的cache块
写回到主存
Cache 命中
标识Cache 准备就绪
Cache 缺失，旧的
Cache块被重写过
主存准备就绪
主存准备就绪
主存没有
准备就绪
主存没有
准备就绪
Cache 缺失，
旧的Cache块
没有被重写过
有效的CPU 请求
Notes: Idle – waits for a Read/Write request from the Processor along with a Valid signal, FSM moves to Compare Tag state
Compare Tag – Checks to see if the request is a hit or a miss. On hit and Valid, returns data to the Processor and moves back to Idle state. On miss, if dirty goes to Write Back state or to Allocate state.
Write Back – Writes the 128-bit block to Memory. When memory write is complete move to the Allocate state.
Allocate – Fetch new block from Memory. Wait in this state until the Memory returns a Ready signal. Then write new block into the Cache and return to the Compare Tag state.

## Slide 49: 多核处理器的Cache一致性
未来的多核处理器意味着单个芯片上有多个处理器，这些处理器可能会共享一个公共的物理地址空间，这就会引起cache一致性问题
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = 0
X = 0
Read X
Read X
Write 1 to X
X = 1
X = 1
Notes: For lecture
Assumes a write through L1 cache

## Slide 50: 一个一致的存储系统
在存储器系统中读取任何一个数据项的返回结果总是最近写入的值
  一致性– 定义了读操作可以返回什么样的值
    对同一地址的写操作是串行执行的 (也就是说，任何两个处理器对同一地址的两个写操作在所有处理器看来都有相同的顺序)
  连贯性– 定义了写入的数据什么时候才能被读操作返回
为了加强一致性，caches 必须提供
  多核处理器cache共享数据的复制
    复制减少了访问延迟和读取共享数据时的竞争现象
  本地cache共享数据的迁移
    迁移不但减少了访问远程共享数据项的延迟，而且减少了对共享存储器带宽的需求 (L2 in our example)
Notes: Supporting migration and replication is critical to performance in accessing shared data.

## Slide 51: Cache 一致性协议
需要引入硬件协议来维护cache一致性，最常用的cache协议就是监听协议
  Cache可以通过一些广播媒介（总线或者网络）访问，所有的cache 控制器对媒介进行监视或者监听，来确定它们是否含有总线或者交换机上请求的数据块副本
写无效协议– 写操作时确保独占访问并且令其他副本无效
  独占访问确保了写执行时不存在其他可读或可写的数据项副本
如果两个处理器试图同时对同一个数据进行写操作，它们中的一个会在竞争中胜出，这使得另一个处理器的副本被置无效。竞争失败的处理器要完成写操作，就必须取得新的数据副本，这个副本中必须包含了更新后的数据 – 因此这个协议强制了写操作的串行化。
Notes:   Reading from multiple copies is not a problem!! Only writes cause issues. What happens if two processors try to write to the same shared data word in the same clock cycle? The bus arbiter decides which processor gets the bus first (and this will be the processor with the first exclusive access). Then the second processor will get exclusive access. Thus, bus arbitration forces sequential behavior.
  This sequential consistency is the most conservative of the memory consistency models. With it, the result of any execution is the same as if the accesses of each processor were kept in order and the accesses among different processors were interleaved.
Each block needs an additional state bit – owner - which indicates that a block may be shared, but the owning core is responsible for updating any other processors and memory when it changes the block or replaces it.
An alternative to snooping is a directory based cache coherence protocol where the directory keeps the sharing status of blocks of physical memory. They have slightly higher implementation overhead but can reduc traffic between caches and thus scale to larger core counts.

## Slide 52: 写处理
确保所有共享数据的其它处理器能被通知，并且对写操作进行下面两种方式的处理：
写-更新 (写-广播) – 执行写操作的处理器通过总线广播新数据，所有的副本进行更新
  All writes go to the bus  higher bus traffic 加大总线通信量
  Since new values appear in caches sooner, can reduce latency 降低延迟
写-无效– 执行写操作的处理器发布无效信号到总线上，cache监听检查它们是否有数据备份，如果有就使它们包含数据字的cache块无效 (允许多个readers，但是只有一个 writer)
  Uses the bus only on the first write  lower bus traffic, so better use of bus bandwidth （降低总线通信量，更好地利用总线带宽）
Notes: IN HIDE MODE – NEEDED?
All commercial machines use write-invalidate as their standard coherence protocol

## Slide 53: 监听无效的例子
When the second miss by Core 2 occurs, Core 1 responds with the value canceling the response from the L2 cache (and also updating the L2 copy)
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = 0
X = 0
Read X
Read X
Write 1 to X
X = 1
Read X
X = I
X = I
X = 1
X = 1
Notes: For lecture
Snooping bus with write-back L1 cache. Requires an additional state – called owner – which indicates that a block may be shared, but the owning core is responsible for updating any other processors and memory when it changes the block or replaces it

## Slide 54: A Write-Invalidate CC Protocol 写无效一致性协议
Shared
(clean)
Invalid
Modified
(dirty)
write-back caching protocol in black
read (miss)
write hit
read (hit or miss)
read (hit) or write (hit)
write (miss)
receives invalidate
(write miss by another core
to this block)
Write miss or write-back due to read (miss) by another core to this block
send invalidate
signals from the core in red
signals from the bus in blue
Notes: For lecture
A read miss causes the cache to acquire the bus and write back the victim block (if it was in the Modified (dirty) state). All the other caches monitor the read miss to see if this block is in their cache. If one has a copy and it is in the Modified state, then the block is written back and its state is changed to Invalid. The read miss is then satisfied by reading from the block memory, and the state of the block is set to Shared.
Read hits do not change the cache state.
A write miss to an Invalid block causes the cache to acquire the bus, read the block, modify the portion of the block being written and changing the block’s state to Modified. A write miss to a Shared block causes the cache to acquire the bus, send an invalidate signal to invalidate any other existing copies in other caches, modify the portion of the block being written and chang the block’s state to Modified.
A write hit to a Modified block causes no action. A write hit to a Shared block causes the cache to acquire the bus, send an invalidate signal to invalidate any other existing copies in other caches, modify the part of the block being written, and change the state to Modified.

## Slide 55: 数据缺失率
共享的数据具有较低的空间局部性和时间局部性
  共享数据的缺失在cache行为中占很大比重，尽管它们在数据访问中可能只占 10% - 40%
64KB 2-way set associative data cache with 32B blocks
Hennessy & Patterson, Computer Architecture: A Quantitative Approach
Notes: Compulsory misses are all very small and are included in capacity misses. The x axis is core count

## Slide 56: 块大小的影响
对多字块中的某一个字进行写操作，意味着整个块是无效的
多字块(大块)同样会引起假共享: 当两个不相关的共享变量放在相同的cache块中时，尽管每个处理器访问的是不同的变量，但是在处理器之间还是将整个块进行交换。
  写无效假共享会增加cache缺失率
编译器可以通过将高度相关的数据分配给同一cache块来减少假共享
A
B
Core1
Core2
4 word cache block

## Slide 57: 其它的一致性协议
cache 一致性协议有很多变化
用于Pentium 4 (以及其它处理器)中的写-无效协议是4状态的 MESI :
  Modified – same
  Exclusive – 只允许共享数据的一个备份被缓存; 存储器中有一个最新的备份
    因为这只有块的一个备份，所以写命中是不需要发送无效信号
  Shared – 共享数据的多个备份可能被缓存 (例如，数据允许被缓存到多个处理器上); 存储器中有一个最新的备份
  Invalid – same
Notes: For E and S book states that memory has an up-to-date version so is this not a write-back cache ???

## Slide 58: 总结:提高Cache的性能
0. 降低cache命中的时间
  减小cache的容量
  直接映射cache
  减少块的容量
  对于写操作
    没有写分配 – 没有cache 的“命中”, 只写到写缓冲
    写分配 –为了避免2个 cycles (first check for hit, then write) ，流水线写操作通过一个延迟的写缓冲写入cache
1. 降低缺失率
  增大cache的容量
  更灵活地放置块(提高关联度)
  增大块的容量(16 to 64 bytes typical)
  victim cache – 用一个小的缓冲来保持最近被丢弃的块

## Slide 59: 总结:提高Cache的性能
2. 降低缺失代价
  减少块的容量
  用一个写缓冲去保持替换下来的被重写的块，所以在读之前不必等写操作完成
  对写缓冲(and/or victim cache) 的读缺失进行检查– may get lucky
  对于大容量的块，首先取最关键的字
  使用多级cache– 2级 cache 不被CPU 时钟速率所束缚
  faster backing store/improved memory bandwidth (提高带宽)
    更宽的总线
    memory interleaving(交叉存储), DDR SDRAMs

## Slide 60: 总结: Cache的设计空间
几个相互影响的方面
  缓存大小
  块大小
  关联度
  替换策略
  写直达/写回
  写分配
折中最好
  依赖于访问特点
    工作量
    使用 (指令-cache, 数据-cache, TLB快表)
  依赖于技术 / 开销
简单的设计更好
关联度
缓存大小
块大小
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.