## Slide 1: 第五章：存储器层次结构-C
[Adapted from Computer Organization and Design, 4th Edition,
Patterson & Hennessy, © 2008, MK]
Courtesy for Mary Jane Irwin of PSU
Notes: Be aware that this first part of new chapter 4 is review for this class, so doesn’t go into detail. If your students are learning computer organization for the first time, this set of slides needs to be expanded greatly.

## Slide 2: 复习: 一台计算机的主要部件
处理器
控制器
数据通路
存储器
设备
输入
输出
高速缓存
主存
辅助存储器
（硬盘）

## Slide 3: 怎样管理存储层次结构？
寄存器  存储器
  by 编译器 (程序员?)
高速缓存  主存
  by cache控制器硬件
主存  硬盘（外存）
  by 操作系统 (虚拟存储器)
  通过快表（TLB）实现虚拟地址到物理地址的转换
  by 程序员 (files)

## Slide 4: 复习: 存储器层次结构
访问时间随离CPU距离的增加而增加
L1$
L2$
Main Memory
Secondary Memory
Processor
(Relative) size of the memory at each level
Inclusive– what is in L1$ is a subset of what is in L2$ is a subset of what is in MM that is a subset of is in SM (这其实是为了说明存储器是一个真正的层次结构)
4-8 bytes (word)
1 to 4 blocks
1,024+ bytes (disk sector = page)
8-32 bytes (block)
充分利用了局部性的原则，在最快和最廉价的技术帮助下提供给用户越来越多可用的存储空间

## Slide 5: 虚拟存储器
将主存用作辅助存储器高速缓存的技术
  允许在多道程序之间有效而安全地共享存储器
  使那些需要比物理存储器更大的存储空间的程序能够运行
  提供重定位来简化执行时的程序加载过程 (例如,允许将程序加载到主存中的任何位置)
工作原理? – 还是局部性原则
  在任何时间内，程序都是可能去访问整个地址空间内某一部分相对较小的地址空间
每个程序都是编译到它自己的地址空间–一个“虚拟”的地址空间
  在程序运行时，每个虚拟地址都是必须要转化为物理地址 (主存中的地址)
Notes: The translation from virtual to physical enforces protection of a program’s address space from other programs

## Slide 6: 共享物理内存的两个程序
Program 1
虚拟地址空间
主存储器
一个程序的地址空间划分为很多页 (所有的页固定为同一大小) or 段(大小可变)
  每个页的开始地址 (在主存中或辅存中) 包含在程序的页表中
Program 2
虚拟地址空间

## Slide 7: 地址转换
虚拟地址(VA)
页内偏移
虚拟页号
31 30 . . . 12 11 . . . 0
页内偏移
物理页号
物理地址 (PA)
29 . . . 12 11 0
地址变换
所以每个访存需求最开始都需要通过地址变换将虚拟空间转换为物理空间
  虚拟存储器中，访问缺失被称为缺页 (例如, 访问的页不在物理存储器中)
虚拟地址到物理地址的转换是需要软硬件结合
Notes: The page size is 212 = 4KB, the number of physical pages allowed in memory is 218, the physical address space is 1GB and the virtual address space is 4GB

## Slide 8: 地址转换机制
物理页的基地址
主存储器
硬盘存储器（外存）
虚拟页号
V
1
1
1
1
1
1
0
1
0
1
0
页表
(在主存中)
页内偏移
物理页号
页内偏移
页表寄存器
Notes: The page table together with the program counter and the registers specifies the state of a program – usually called a process
The operating system simply loads the page table register to point to the page table of the process it wants to make active (and loads the register file and the program counter)

## Slide 9: Virtual Addressing with a Cache
由于页表存放在主存中，因此程序多出一次额外的访存-需要一次访存以获得物理地址(通过地址变换将虚拟地址VA转换为物理地址PA)，此后的访存才是获得数据
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
这样使存储器 (缓存) 访问变得开销很大 (程序每次访存至少需要两次)
现代处理器都包含一个特殊的cache以追踪最近使用过的地址变换，这个特殊的地址转换cache就是快表Translation Lookaside Buffer (TLB) –用于记录最近使用地址的映射信息的一个较小的高速缓存，从而可以避免每次都要访问页表

## Slide 10: 加速地址转换
物理页
基地址
主存储器
硬盘存储器
虚拟页号
V
1
1
1
1
1
1
0
1
0
1
0
1
1
1
0
1
标记
物理页
基地址
V
快表
页表
(在物理存储器中)
页表寄存器

## Slide 11: Translation Lookaside Buffers (TLBs) 快表
正和其它的cache一样， TLB 的组织形式也是全相联，组相联，直接映射这几种
TLB 的访问时间通常是要比cache的访问时间短 (因为TLB比cache小很多)
  TLB 通常不会超过512项

## Slide 12: A TLB in the Memory Hierarchy
TLB 缺失–判断是缺页还是仅仅是一次TLB缺失？
  如果该页在主存中，那么TLB缺失只是一次转换缺失，处理器可以通过将页表中的变换装载到TLB并重新访问来进行缺失处理(TLB缺失既可以通过硬件处理，也可以通过软件处理)
    Takes 10’s of cycles to find and load the translation info into the TLB
  如果该页不在主存中，TLB缺失就是一次真的缺页
    Takes 1,000,000’s of cycles to service a page fault
TLB 缺失比缺页要频繁得多
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
¾ t
¼ t

## Slide 13: TLB 中可能发生的事件组合
TLB | Page Table | Cache | 可能发生么?如果可能，什么情况下发生?
Hit | Hit | Hit | 
Hit | Hit | Miss | 
Miss | Hit | Hit | 
Miss | Hit | Miss | 
Miss | Miss | Miss | 
Hit | Miss | Miss/ Hit | 
Miss | Miss | Hit | 
Yes – what we want!
Yes – although the page table is not
checked if the TLB hits
Yes – TLB miss, PA in page table
Yes – TLB miss, PA in page table, but data
not in cache
Yes – page fault
Impossible – TLB translation not possible if
page is not present in memory
Impossible – data not allowed in cache if
page is not in memory

## Slide 14: 处理一次 TLB 缺失
考虑一次TLB 缺页在存储器中发生 (例如， 设置页表中的有效位)
  TLB缺失 (缺页异常) 必须在访存发生的同一时钟周期的末尾被判定，因此下一个时钟周期就开始进行异常处理而不是继续正常的指令执行。下表见图5-27
寄存器 | CP0 寄存器号 | 说明
EPC | 14 | Where to restart after exception
Cause | 13 | Cause of exception
BadVAddr | 8 | Address that caused exception
Index | 0 | Location in TLB to be read/written
Random | 1 | Pseudorandom location in TLB
EntryLo | 2 | Physical page address and flags
EntryHi | 10 | Virtual page address
Context | 4 | Page table address & page number
Notes: For page faults …
If the page is not present in memory, then we need to transfer control to the operating system to deal with a page fault
  Must prevent the write on a store from completing when there is a page fault – deassert the write control line to memory

## Slide 15: TLB缺失处理程序（MIPS）
当TLB缺失发生时，MIPS的硬件将被引用的页号保存在一个叫BadVAddr的特殊寄存器中，然后产生异常。这个异常请求操作系统通过软件来处理缺失，控制权被转移到地址 8000 0000hex, TLB缺失处理程序的位置
TLBmiss:
mfc0 $k1, Context #copy addr of PTE into $k1
lw $k1, 0($k1) #put PTE into $k1
mtc0 $k1, EntryLo #put PTE into EntryLo
tlbwr #put EntryLo into TLB
# at Random
eret #return from exception
指令tlbwr 把控制寄存器EntryLo 中的内容复制到由控制寄存器 Random所选择的TLB表项中。
TLB 缺失大概需要花费12个时钟周期
Notes: The upper 12 bits of Context have the address of the base of the page table and the next 18 bits have the virtual address of the missing page (the last two bits are zero).
Note that the TLB miss handler does not check to see if the page table entry is valid. If the entry is invalid, another exception will occur – causing the page fault handler to run
TLB misses have a special entry point to lower the penalty for a TLB miss.

## Slide 16: 一些虚拟存储器的设计参数
 | Paged VM | TLBs
Total size | 16,000 to 250,000 words | 16 to 512 entries
Total size (KB) | 250,000 to 1,000,000,000 | 0.25 to 16
Block size (B) | 4000 to 64,000 | 4 to 8
Hit time |  | 0.5 to 1 clock cycle
Miss penalty (clocks) | 10,000,000 to 100,000,000 | 10 to 100
Miss rates | 0.00001% to 0.0001% | 0.01% to 1%

## Slide 17: 两个机器的快表参数
 | Intel Nehalem | AMD Barcelona
Address sizes | 48 bits (vir); 44 bits (phy) | 48 bits (vir); 48 bits (phy)
Page size | 4KB | 4KB
TLB organization | L1 TLB for instructions and L1 TLB for data per core; both are 4-way set assoc.; LRU L1 ITLB has 128 entries, L2 DTLB has 64 entries L2 TLB (unified) is 4-way set assoc.; LRU L2 TLB has 512 entries TLB misses handled in hardware | L1 TLB for instructions and L1 TLB for data per core; both are fully assoc.; LRU L1 ITLB and DTLB each have 48 entries L2 TLB for instructions and L2 TLB for data per core; each are 4-way set assoc.; round robin LRU Both L2 TLBs have 512 entries TLB misses handled in hardware

## Slide 18: 为什么不用虚拟寻址cache？
虚拟寻址cache只需要对cache缺失进行地址转换
data
CPU
Trans-
lation
Cache
Main
Memory
VA
hit
PA
但是
  使用虚拟地址访问cache，并且两个程序之间共享数据时，可能有别名-两个虚拟地址对应到同一个物理地址，所以在cache中有共享数据的两个备份，在TLB中有两个表项，这将导致一致性问题
    Must update all cache entries with the same physical address or the memory becomes inconsistent
Notes: Handling aliasing requires significant hardware – essentially an associative lookup on the physical address tags to see if you have multiple hits
This would benefit from a picture that showes two processes sharing data – with aliasing

## Slide 19: 减短地址变换时间
可以使cache访问和TLB访问重叠
  虚拟地址的高位用于访问TLB，低位用于cache的索引
Tag
Data
=
Tag
Data
=
Cache Hit
Desired word
VA Tag
PA
Tag
TLB Hit
2-way Associative Cache
Index
PA Tag
Block offset
Page offset
Virtual page #
Notes: Overlapped access only works as long as the address bits used to index into the cache do not change as the result of VA translation
This usually limits things to small caches, large page sizes, or high n-way set associative caches if you want a large cache

## Slide 20: The Hardware/Software Boundary
虚拟地址到物理地址的转换过程中哪些部分是需要硬件支持的呢？
  TLB快表：用于记录最近用过的地址变换的高速缓存
    TLB access time is part of the cache hit time
    May allot an extra stage in the pipeline for TLB access （多一级）
  页表存储，故障检测和更新
    Page faults result in interrupts (precise) that are then handled by the OS 缺页导致的中断由操作系统处理
    Hardware must support (i.e., update appropriately) Dirty and Reference bits (e.g., ~LRU) in the Page Tables
    硬件要支持页表中的重写位、引用位

## Slide 21: 存储器层次结构的4个问题
Q1: 一个块可以被放到何处？
  (Entry placement)
Q2: 如何找到一个块？ (Entry identification)
Q3: 当cache缺失时替换哪一块？ (Entry replacement)
Q4: 写操作如何处理？
(Write strategy)

## Slide 22: Q1&Q2: 块可以被放到哪以及如何找到一个块
 | # of sets | Entries per set
Direct mapped | # of entries | 1
Set associative | (# of entries)/ associativity | Associativity (typically 2 to 16)
Fully associative | 1 | # of entries
 | Location method | # of comparisons
Direct mapped | Index | 1
Set associative | Index the set; compare set’s tags | Degree of associativity
Fully associative | Compare all entries’ tags Separate lookup (page) table | # of entries 0
这两个图见P324

## Slide 23: Q3:当cache缺失时替换哪一块？
直接映射很简单– 只有一个可以替换的候选者
组相联或者全相联
  随机法
  最近最少使用算法LRU
对于两路组相联，使用随机替换算法的缺失率比LRU替换算法的缺失率高1.1倍
在关联度不低(> 4-way)的层次结构中实现LRU的代价太高了，这是因为追踪使用信息的代价很高。

## Slide 24: Q4:写操作如何处理？
写直达– 信息被同时写到cache的块和存储器层次结构较低层的块中（对cache来说是主存）
  总是和一个写缓冲结合在一起，所以写到下一个存储器层次时的写等待可以被消除 (只要写缓冲没被充满)
写回 – 信息仅仅是写到cache中的块。被改写的块只有在它被替换时才写回到存储器层次结构的较低层中。
  需要一个重写位来跟踪块是否被重写
  虚拟存储器系统通常采用写回策略
各自的特点：
  写直达: 读缺失不要求向下一层写，缺失代价小，比写回更易于实现
  写回: 写操作能以cache的速度执行；多次写同一块的字只需对存储器层次结构较低层进行一次写操作
Notes: The rate at which writes are generated by a processor generally exceed the rate at which the memory system can process them, even allowing for physically and logically wider memories and burst modes for DRAMs. Subsequently, most of today’s caches use write-back

## Slide 25: 总结
局部性原理:
  在任何时间内，程序访问的只是地址空间相对较小的一部分内容
    时间局部性: Locality in Time
    空间局部性: Locality in Space
Cache，TLB，虚拟存储器都可以通过对4个问题的各自解答来理解
  一个块可以被放在何处?
  如何找到一个块?
  当cache缺失时替换哪一块?
  写操作如何处理?
页表将虚拟地址映射到物理地址
  TLBs 对加速地址转化很重要
Notes: Let’s summarize today’s lecture. I know you have heard this many times and many ways but it is still worth repeating.
Memory hierarchy works because of the Principle of Locality which says a program will access a relatively small portion of the address space at any instant of time.
There are two types of locality: temporal locality, or locality in time and spatial locality, or locality in space.
So far, we have covered three major categories of cache misses.
Compulsory misses are cache misses due to cold start. You cannot avoid them but if you are going to run billions of instructions anyway, compulsory misses usually don’t bother you.
Conflict misses are misses caused by multiple memory location being mapped to the same cache location.
The nightmare scenario is the ping pong effect when a block is read into the cache but before we have a chance to use it, it was immediately forced out by another conflict miss.
You can reduce Conflict misses by either increase the cache size or increase the associativity, or both.
Finally, Capacity misses occurs when the cache is not big enough to contains all the cache blocks required by the program. You can reduce this miss rate by making the cache larger.
There are two write policy as far as cache write is concerned. Write through requires a write buffer and a nightmare scenario is when the store occurs so frequent that you saturates your write buffer.
The second write polity is write back. In this case, you only write to the cache and only when the cache block is being replaced do you write the cache block back to memory.
+3 = 77 min. (Y:57)