## Slide 1: Computer Architecture Chapter 2: Instructions: Language of the Computer
[Adapted from Computer Organization and Design,
Patterson & Hennessy
Notes: Be aware that this chapter is review for this class, so doesn’t go into detail. If your students are learning assembly language programming for the first time, this set of slides needs to be expanded greatly.
Combinations to AV system, etc. 0808 (1988 in 113 IST)
Call AV hot line at 8-777-0035

## Slide 2: Two Key Principles of Machine Design
  Instructions are represented as numbers and, as such, are indistinguishable from data
  Programs are stored in alterable memory (that can be read or written to) just like data
Stored-program concept
  Programs can be shipped as files of binary numbers – binary compatibility
  Computers can inherit ready-made software provided they are compatible with an existing ISA – leads industry to align around a small number of ISAs
Accounting prg (machine code)
C compiler (machine code)
Payroll data
Source code in C for Acct prg
Memory

## Slide 3: MIPS-32 ISA
Instruction Categories
  Computational
  Load/Store
  Jump and Branch
  Floating Point
    coprocessor
  Memory Management
  Special
R0 - R31
PC
HI
LO
Registers
op
op
op
rs
rt
rd
sa
funct
rs
rt
immediate
jump target
3 Instruction Formats: all 32 bits wide
R format
I format
J format

## Slide 4: MIPS (RISC) Design Principles
Simplicity favors regularity
  fixed size instructions
  small number of instruction formats
  opcode always the first 6 bits
Smaller is faster
  limited instruction set
  limited number of registers in register file
  limited number of addressing modes
Make the common case fast
  arithmetic operands from the register file (load-store machine)
  allow instructions to contain immediate operands
Good design demands good compromises
  three instruction formats

## Slide 5: MIPS Arithmetic Instructions
MIPS assembly language arithmetic statement
add $t0, $s1, $s2
sub $t0, $s1, $s2
Each arithmetic instruction performs one operation
Each specifies exactly three operands that are all contained in the datapath’s register file ($t0,$s1,$s2)
  destination  source1 op source2
Instruction Format (R format)
0 17 18 8 0 0x22
Notes: Register designators (numbers) in decimal
Op codes and function fields in hex (0x designation)

## Slide 6: MIPS Instruction Fields
MIPS fields are given names to make them easier to refer to
op rs rt rd shamt funct
op 6-bits opcode that specifies the operation
rs 5-bits register file address of the first source operand
rt 5-bits register file address of the second source operand
rd 5-bits register file address of the result’s destination
shamt 5-bits shift amount (for shift instructions)
funct 6-bits function code augmenting the opcode

## Slide 7: MIPS Register File
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
locations
32
5
32
5
5
32
Holds thirty-two 32-bit registers
  Two read ports and
  One write port
Registers are
  Faster than main memory
    But register files with more locations are slower (e.g., a 64 word file could be as much as 50% slower than a 32 word file)
    Read/write port increase impacts speed quadratically
  Easier for a compiler to use
    e.g., (A*B) – (C*D) – (E*F) can do multiplies in any order vs. stack
  Can hold variables so that
    code density improves (since register are named with fewer bits than a memory location)
write control
Notes: All machines (since 1975) have used general purpose registers

## Slide 8: Aside: MIPS Register Convention
Name | Register Number | Usage | Preserve on call?
$zero | 0 | constant 0 (hardware) | n.a.
$at | 1 | reserved for assembler | n.a.
$v0 - $v1 | 2-3 | returned values | no
$a0 - $a3 | 4-7 | arguments | yes
$t0 - $t7 | 8-15 | temporaries | no
$s0 - $s7 | 16-23 | saved values | yes
$t8 - $t9 | 24-25 | temporaries | no
$gp | 28 | global pointer | yes
$sp | 29 | stack pointer | yes
$fp | 30 | frame pointer | yes
$ra | 31 | return addr (hardware) | yes

## Slide 9: MIPS Memory Access Instructions
MIPS has two basic data transfer instructions for accessing memory
lw $t0, 4($s3) #load word from memory
sw $t0, 8($s3) #store word to memory
The data is loaded into (lw) or stored from (sw) a register in the register file – a 5 bit address
The memory address – a 32 bit address – is formed by adding the contents of the base address register to the offset value
  A 16-bit field meaning access is limited to memory locations within a region of 213 or 8,192 words (215 or 32,768 bytes) of the address in the base register
Notes: Note that the offset can be positive or negative.
Offsets must be able to access bytes as well, so word offsets will have two low-order zeros in them.

## Slide 10: Machine Language - Load Instruction
Load/Store Instruction Format (I format):
lw $t0, 24($s3)
35 19 8 2410
Memory
data
word address (hex)
0x00000000
0x00000004
0x00000008
0x0000000c
0xf f f f f f f f
$s3
0x12004094
2410 + $s3 =
. . . 0001 1000
+ . . . 1001 0100
. . . 1010 1100 =
0x120040ac
0x120040ac
$t0
Notes: destination address no longer in the rd field - now in the rt field
offset limited to 16 bits - so can’t get to every location in memory (with a fixed base address)

## Slide 11: Byte Addresses
Since 8-bit bytes are so useful, most architectures address individual bytes in memory
  Alignment restriction - the memory address of a word must be on natural word boundaries (a multiple of 4 in MIPS-32)
Big Endian: leftmost byte is word address
    IBM 360/370, Motorola 68k, MIPS, Sparc, HP PA
Little Endian: rightmost byte is word address
    Intel 80x86, DEC Vax, DEC Alpha (Windows NT)
msb
lsb
3 2 1 0
little endian byte 0
0 1 2 3
big endian byte 0
Notes: Talk about the reasons (performance) for the word/byte alignment restriction

## Slide 12: Aside: Loading and Storing Bytes
MIPS provides special instructions to move bytes
lb $t0, 1($s3) #load byte from memory
sb $t0, 6($s3) #store byte to memory
0x28 19 8 16 bit offset
What 8 bits get loaded and stored?
  load byte places the byte from memory in the rightmost 8 bits of the destination register
    what happens to the other bits in the register?
  store byte takes the byte from the rightmost 8 bits of a register and writes it to a byte in memory
    what happens to the other bits in the memory word?
Notes: load byte takes the contents of the byte at the memory address specified, zero-extends it, and loads it into the register
Store byte leaves the other bits in the memory word intact.

## Slide 13: MIPS Immediate Instructions
addi $sp, $sp, 4 #$sp = $sp + 4
slti $t0, $s2, 15 #$t0 = 1 if $s2<15
Machine format (I format):
0x0A 18 8 0x0F
Small constants are used often in typical code
Possible approaches?
  put “typical constants” in memory and load them
  create hard-wired registers (like $zero) for constants like 1
  have special instructions that contain constants !
The constant is kept inside the instruction itself!
  Immediate format limits values to the range +215–1 to -215
Notes: in gcc 52% of arithmetic operations involve constants – in spice its 69%
have the students answer why not – speed and limited number of registers
much faster than if loaded from memory
addi and slti do sign extend of immediate operand into the leftmost bits of the destination register (ie., copies the leftmost bit of the 16-bit immediate value into the upper 16 bits)
by contrast, ori and andi loads zero’s into the upper 16 bits and so is usually used (instead of the addi) to build 32 bit constants

## Slide 14: Aside: How About Larger Constants?
We'd also like to be able to load a 32 bit constant into a register, for this we must use two instructions
a new "load upper immediate" instruction
lui $t0, 1010101010101010
Then must get the lower order bits right, use ori $t0, $t0, 1010101010101010
16 0 8 10101010101010102
1010101010101010
0000000000000000
1010101010101010
0000000000000000
1010101010101010 1010101010101010
Notes: For lecture
sets the upper 16 bits of a constant in a register, allowing the next instruction to specify the lower 16 bits of the constant
note that lui fills the lower 16 bits of the register with zero’s
why can’t addi be used as the second instruction for this 32 bit constant?
also note – the assembler lets me specify constants larger than 16 bits in one instruction and then expands the code into two instructions (lui and ori) automatically

## Slide 15: Review: Unsigned Binary Representation
Hex | Binary | Decimal
0x00000000 | 0…0000 | 0
0x00000001 | 0…0001 | 1
0x00000002 | 0…0010 | 2
0x00000003 | 0…0011 | 3
0x00000004 | 0…0100 | 4
0x00000005 | 0…0101 | 5
0x00000006 | 0…0110 | 6
0x00000007 | 0…0111 | 7
0x00000008 | 0…1000 | 8
0x00000009 | 0…1001 | 9
 | … | 
0xFFFFFFFC | 1…1100 | 
0xFFFFFFFD | 1…1101 | 
0xFFFFFFFE | 1…1110 | 
0xFFFFFFFF | 1…1111 | 
232 - 1
232 - 2
232 - 3
232 - 4
232 - 1
1 1 1 . . . 1 1 1 1 bit
31 30 29 . . . 3 2 1 0 bit position
231 230 229 . . . 23 22 21 20 bit weight
1 0 0 0 . . . 0 0 0 0 - 1
Notes: All positive numbers - no sign bit
last entry is most significant byte address
fourth from last entry is most significant word address

## Slide 16: Review: Signed Binary Representation
2’sc binary | decimal
1000 | -8
1001 | -7
1010 | -6
1011 | -5
1100 | -4
1101 | -3
1110 | -2
1111 | -1
0000 | 0
0001 | 1
0010 | 2
0011 | 3
0100 | 4
0101 | 5
0110 | 6
0111 | 7
23 - 1 =
-(23 - 1) =
-23 =
1010
complement all the bits
1011
and add a 1
complement all the bits
0101
and add a 1
0110
Notes: Signed numbers – assuming 2’s complement representation – for eight bits
Note that msb of 1 indicates a negative number, the bit string all 0’s is zero, that the largest positive number that can be represented is 7 (2**(n-1) –1 for n bits) whereas the largest negative number that can be represented is –8 (-2**(n-1) for n bits)

## Slide 17: MIPS Shift Operations
Need operations to pack and unpack 8-bit characters into 32-bit words
Shifts move all the bits in a word left or right
sll $t2, $s0, 8 #$t2 = $s0 << 8 bits
srl $t2, $s0, 8 #$t2 = $s0 >> 8 bits
Instruction Format (R format)
Such shifts are called logical because they fill with zeros
  Notice that a 5-bit shamt field is enough to shift a 32-bit value 25 – 1 or 31 bit positions
0 16 10 8 0x00
Notes: also have sllv, srlv, and srav

## Slide 18: MIPS Logical Operations
There are a number of bit-wise logical operations in the MIPS ISA
and $t0, $t1, $t2 #$t0 = $t1 & $t2
or $t0, $t1, $t2 #$t0 = $t1 | $t2
nor $t0, $t1, $t2 #$t0 = not($t1 | $t2)
Instruction Format (R format)
andi $t0, $t1, 0xFF00 #$t0 = $t1 & ff00
ori $t0, $t1, 0xFF00 #$t0 = $t1 | ff00
Instruction Format (I format)
0 9 10 8 0 0x24
0x0D 9 8 0xFF00

## Slide 19: MIPS Control Flow Instructions
MIPS conditional branch instructions:
bne $s0, $s1, Lbl #go to Lbl if $s0$s1 beq $s0, $s1, Lbl #go to Lbl if $s0=$s1
  Ex: if (i==j) h = i + j;
bne $s0, $s1, Lbl1 add $s3, $s0, $s1 Lbl1: ...
Instruction Format (I format):
0x05 16 17 16 bit offset
How is the branch destination address specified?

## Slide 20: Specifying Branch Destinations
Use a register (like in lw and sw) added to the 16-bit offset
  which register? Instruction Address Register (the PC)
    its use is automatically implied by instruction
    PC gets updated (PC+4) during the fetch cycle so that it holds the address of the next instruction
  limits the branch distance to -215 to +215-1 (word) instructions from the (instruction after the) branch instruction, but most branches are local anyway
PC
Add
32
32
32
32
32
offset
16
32
00
sign-extend
from the low order 16 bits of the branch instruction
branch dst
address
?
Add
4
32
Notes: Note that two low order 0’s are concatenated to the 16 bit field giving an eighteen bit address
0111111111111111 00 = 2**15 –1 words (2**17 – 1 bytes)

## Slide 21: In Support of Branch Instructions
We have beq, bne, but what about other kinds of branches (e.g., branch-if-less-than)? For this, we need yet another instruction, slt
Set on less than instruction:
slt $t0, $s0, $s1 # if $s0 < $s1 then # $t0 = 1 else # $t0 = 0
Instruction format (R format):
Alternate versions of slt
slti $t0, $s0, 25 # if $s0 < 25 then $t0=1 ...
sltu $t0, $s0, $s1 # if $s0 < $s1 then $t0=1 ...
sltiu $t0, $s0, 25 # if $s0 < 25 then $t0=1 ...
2
0 16 17 8 0x24
Notes: Unsigned (u) versus signed integer comparison

## Slide 22: Aside: More Branch Instructions
Can use slt, beq, bne, and the fixed value of 0 in register $zero to create other conditions
  less than blt $s1, $s2, Label
  less than or equal to ble $s1, $s2, Label
  greater than bgt $s1, $s2, Label
  great than or equal to bge $s1, $s2, Label
slt $at, $s1, $s2 #$at set to 1 if
bne $at, $zero, Label #$s1 < $s2
Such branches are included in the instruction set as pseudo instructions - recognized (and expanded) by the assembler
  Its why the assembler needs a reserved register ($at)
Notes: For lecture
blt $s1,$s2 Label =
slt $at,$s1,$s2 #at gets 1 if $s1 < $s2
bne $at,$zero,Label

## Slide 23: Bounds Check Shortcut
Treating signed numbers as if they were unsigned gives a low cost way of checking if 0 ≤ x < y (index out of bounds for arrays)
sltu $t0, $s1, $t2 # $t0 = 0 if # $s1 > $t2 (max) # or $s1 < 0 (min) beq $t0, $zero, IOOB # go to IOOB if # $t0 = 0
The key is that negative integers in two’s complement look like large numbers in unsigned notation. Thus, an unsigned comparison of x < y also checks if x is negative as well as if x is less than y.

## Slide 24: Other Control Flow Instructions
MIPS also has an unconditional branch instruction or jump instruction: j label #go to label
Instruction Format (J Format):
0x02 26-bit address
PC
4
32
26
32
00
from the low order 26 bits of the jump instruction
Notes: If-then-else code compilation

## Slide 25: Aside: Branching Far Away
What if the branch destination is further away than can be captured in 16 bits?
The assembler comes to the rescue – it inserts an unconditional jump to the branch target and inverts the condition
beq $s0, $s1, L1
becomes
bne $s0, $s1, L2
j L1
L2:

## Slide 26: Instructions for Accessing Procedures
MIPS procedure call instruction: jal ProcedureAddress #jump and link
Saves PC+4 in register $ra to have a link to the next instruction for the procedure return
Machine format (J format):
Then can do procedure return with a
jr $ra #return
Instruction format (R format):
0x03 26 bit address
0 31 0x08
Notes: jr jumps to the address stored in the register – in this case $ra – which is just what we want.

## Slide 27: Six Steps in Execution of a Procedure
Main routine (caller) places parameters in a place where the procedure (callee) can access them
  $a0 - $a3: four argument registers
Caller transfers control to the callee
Callee acquires the storage resources needed
Callee performs the desired task
Callee places the result value in a place where the caller can access it
  $v0 - $v1: two value registers for result values
Callee returns control to the caller
  $ra: one return address register to return to the point of origin

## Slide 28: Aside: Spilling Registers
What if the callee needs to use more registers than allocated to argument and return values?
  callee uses a stack – a last-in-first-out queue
low addr
high addr
$sp
One of the general registers, $sp ($29), is used to address the stack (which “grows” from high address to low address)
  add data onto the stack – push
    $sp = $sp – 4 data on stack at new $sp
  remove data from the stack – pop
    data from stack at $sp $sp = $sp + 4
top of stack
Notes: Note that temporary registers $t0 through $t9 can also be used as by MIPS convention they are not preserved by the callee (kept intact) across subroutine boundaries
However, saved registers $s0 through $s7 must be preserved by the calle - I.e., if the callee uses one, it must first save it and then restore it to its old value before returning control to the caller

## Slide 29: Aside: Allocating Space on the Stack
The segment of the stack containing a procedure’s saved registers and local variables is its procedure frame (aka activation record)
  The frame pointer ($fp) points to the first word of the frame of a procedure – providing a stable “base” register for the procedure
    $fp is initialized using $sp on a call and $sp is restored using $fp on a return
low addr
high addr
$sp
Saved argument regs (if any)
Saved return addr
Saved local regs (if any)
Local arrays & structures (if any)
$fp
Notes: On the other hand, the stack pointer (sp) might change during the procedure (not the case for all of our examples) so references to a local variable in memory might have different offsets wrt the sp depending on where they are in the procedure.

## Slide 30: Aside: Allocating Space on the Heap
Static data segment for constants and other static variables (e.g., arrays)
Dynamic data segment (aka heap) for structures that grow and shrink (e.g., linked lists)
  Allocate space on the heap with malloc() and free it with free() in C
Memory
0x 0000 0000
Text
(Your code)
Reserved
Static data
0x 0040 0000
0x 1000 0000
0x 1000 8000
0x 7f f f f f f c
Stack
Dynamic data
(heap)
$sp
$gp
PC
Notes: Stack and heap grow towards each other.
Malloc() allocates space on the heap and returns a pointer to it. Memory allocation is controlled by programs (in C) and is the source of many common and difficult bugs. Forgetting to free space leads to “memory leak” and the need for “garbage collection” and freeing space to early to “dangling pointers”.

## Slide 31: MIPS Instruction Classes Distribution
Frequency of MIPS instruction classes for SPEC2006
Instruction Class | Frequency | 
 | Integer | Ft. Pt.
Arithmetic | 16% | 48%
Data transfer | 35% | 36%
Logical | 12% | 4%
Cond. Branch | 34% | 8%
Jump | 2% | 0%

## Slide 32: Atomic Exchange Support
Need hardware support for synchronization mechanisms to avoid data races where the results of the program can change depending on how events happen to occur
  Two memory accesses from different threads to the same location, and at least one is a write
Atomic exchange (atomic swap) – interchanges a value in a register for a value in memory atomically, i.e., as one operation (instruction)
  Implementing an atomic exchange would require both a memory read and a memory write in a single, uninterruptable instruction. An alternative is to have a pair of specially configured instructions
ll $t1, 0($s1) #load linked
sc $t0, 0($s1) #store conditional

## Slide 33: Automic Exchange with ll and sc
If the contents of the memory location specified by the ll are changed before the sc to the same address occurs, the sc fails (returns a zero)
try: add $t0, $zero, $s4 #$t0=$s4 (exchange value)
ll $t1, 0($s1) #load memory value to $t1
sc $t0, 0($s1) #try to store exchange #value to memory, if fail #$t0 will be 0
beq $t0, $zero, try #try again on failure
add $s4, $zero, $t1 #load value in $s4
If the value in memory between the ll and the sc instructions changes, then sc returns a 0 in $t0 causing the code sequence to try again.
Notes: Use care when inserting instructions between the ll and sc. Only register-register instructions can be safely permitted, otherwise it is possible to create deadlock where the processor can never complete the sc because of repeated page faults.

## Slide 34: The C Code Translation Hierarchy
C program
compiler
assembly code
assembler
object code
library routines
executable
linker
loader
memory
machine code
Notes: Four logical phases all programs go through
C code – x.c or .TXT
assembly code – x.s or .ASM
object code – x.o or .OBJ
executable – a.out or .EXE

## Slide 35: Compiler Benefits
Comparing performance for bubble (exchange) sort
  To sort 100,000 words with the array initialized to random values on a Pentium 4 with a 3.06 clock rate, a 533 MHz system bus, with 2 GB of DDR SDRAM, using Linux version 2.4.20
gcc opt | Relative performance | Clock cycles (M) | Instr count (M) | CPI
None | 1.00 | 158,615 | 114,938 | 1.38
O1 (medium) | 2.37 | 66,990 | 37,470 | 1.79
O2 (full) | 2.38 | 66,521 | 39,993 | 1.66
O3 (proc mig) | 2.41 | 65,747 | 44,993 | 1.46
The unoptimized code has the best CPI, the O1 version has the lowest instruction count, but the O3 version is the fastest. Why?

## Slide 36: The Java Code Translation Hierarchy
Java program
compiler
Class files (Java bytecodes)
Just In Time (JIT) compiler
Compiled Java methods (machine code)
Java library routines (machine code)
Java Virtual Machine

## Slide 37: Sorting in C versus Java
Comparing performance for two sort algorithms in C and Java
  The JVM/JIT is Sun/Hotspot version 1.3.1/1.3.1
 | Method | Opt | Bubble | Quick | Speedup quick vs bubble
 |  |  | Relative performance |  | 
C | Compiler | None | 1.00 | 1.00 | 2468
C | Compiler | O1 | 2.37 | 1.50 | 1562
C | Compiler | O2 | 2.38 | 1.50 | 1555
C | Compiler | O3 | 2.41 | 1.91 | 1955
Java | Interpreted |  | 0.12 | 0.05 | 1050
Java | JIT compiler |  | 2.13 | 0.29 | 338
Observations?
Notes: Unoptimized C prgram is 8.3 times faster than the interpreted Java code for bubble.
Using JIT makes Java 2.1 times faster than the unoptimized C and within a factor of 1.13 of the highest optimized C code.
Ratio’s aren’t as close for quick, presumably because it is harder to amortize the cost of runtime compilation over the shorter execution time.
The last column demonstrates the impact of a better algorithm

## Slide 38: Addressing Modes Illustrated
1. Register addressing
op rs rt rd funct
Register
word operand
op rs rt offset
2. Base (displacement) addressing
base register
Memory
word or byte operand
3. Immediate addressing
op rs rt operand
4. PC-relative addressing
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
5. Pseudo-direct addressing
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 39: MIPS Organization So Far
Processor
Memory
32 bits
230
words
read/write
addr
read data
write data
word address
(binary)
0…0000
0…0100
0…1000
0…1100
1…1100
Register File
src1 addr
src2 addr
dst addr
write data
32 bits
src1
data
src2
data
32
registers
($zero - $ra)
32
32
32
32
32
32
5
5
5
PC
ALU
32
32
32
32
32
0
1
2
3
7
6
5
4
byte address
(big Endian)
Fetch
PC = PC+4
Decode
Exec
Add
32
32
4
Add
32
32
branch offset