## Slide 1: Computer Architecture Chapter 3: Arithmetic for Computers
[Adapted from Computer Organization and Design,
Patterson & Hennessy]

## Slide 2: Review: MIPS (RISC) Design Principles
Simplicity favors regularity
  fixed size instructions
  small number of instruction formats
  opcode always the first 6 bits
Smaller is faster
  limited instruction set
  limited number of registers in register file
  limited number of addressing modes
Make the common case fast
  arithmetic operands from the register file (load-store machine)
  allow instructions to contain immediate operands
Good design demands good compromises
  three instruction formats

## Slide 3: Review: MIPS Addressing Modes Illustrated
1. Register addressing
op rs rt rd funct
Register
word operand
op rs rt offset
2. Base (displacement) addressing
base register
Memory
word or byte operand
3. Immediate addressing
op rs rt operand
4. PC-relative addressing
op rs rt offset
Program Counter (PC)
Memory
branch destination instruction
5. Pseudo-direct addressing
op jump address
Program Counter (PC)
Memory
jump destination instruction
||

## Slide 4: Number Representations
32-bit signed numbers (2’s complement): 0000 0000 0000 0000 0000 0000 0000 0000two = 0ten 0000 0000 0000 0000 0000 0000 0000 0001two = + 1ten ...
0111 1111 1111 1111 1111 1111 1111 1110two = + 2,147,483,646ten 0111 1111 1111 1111 1111 1111 1111 1111two = + 2,147,483,647ten 1000 0000 0000 0000 0000 0000 0000 0000two = – 2,147,483,648ten 1000 0000 0000 0000 0000 0000 0000 0001two = – 2,147,483,647ten ...
1111 1111 1111 1111 1111 1111 1111 1110two = – 2ten 1111 1111 1111 1111 1111 1111 1111 1111two = – 1ten
maxint
minint
Converting <32-bit values into 32-bit values
  copy the most significant bit (the sign bit) into the “empty” bits 0010 -> 0000 0010 1010 -> 1111 1010
  sign extend versus zero extend (lb vs. lbu)
MSB
LSB

## Slide 5: MIPS Arithmetic Logic Unit (ALU)
Must support the Arithmetic/Logic operations of the ISA
  add, addi, addiu, addu
  sub, subu
  mult, multu, div, divu
  sqrt
  and, andi, nor, or, ori, xor, xori
  beq, bne, slt, slti, sltiu, sltu
32
32
32
m (operation)
result
A
B
ALU
4
zero
ovf
1
1
With special handling for
  sign extend – addi, addiu, slti, sltiu
  zero extend – andi, ori, xori
  overflow detection – add, addi, sub

## Slide 6: Dealing with Overflow
Operation | Operand A | Operand B | Result indicating overflow
A + B | ≥ 0 | ≥ 0 | < 0
A + B | < 0 | < 0 | ≥ 0
A - B | ≥ 0 | < 0 | < 0
A - B | < 0 | ≥ 0 | ≥ 0
Overflow occurs when the result of an operation cannot be represented in 32-bits, i.e., when the sign bit contains a value bit of the result and not the proper sign bit
  When adding operands with different signs or when subtracting operands with the same sign, overflow can never occur
MIPS signals overflow with an exception (aka interrupt) – an unscheduled procedure call where the EPC contains the address of the instruction that caused the exception

## Slide 7: A MIPS ALU Implementation
+
A1
B1
result1
less
+
A0
B0
result0
less
+
A31
B31
result31
less
. . .
0
0
set
Enable overflow bit setting for signed arithmetic (add, addi, sub)
add/subt
op
ovf
zero
. . .
Zero detect (slt, slti, sltiu, sltu, beq, bne)
Notes: For slt (and slti and sltiu and sltu)
“No integer overflow exception occurs under any circumstances. The comparison is valid even if the subtraction used during the comparison overflows.”
The way I read this is that if the result overflows during the subtraction, no attempt is made to correct the set line to reflect that!
Otherwise, you would need to add additional logic in front of the set line to do the correction in case of overflow. Like exoring the overflow bit with the sign bit.

## Slide 8: But What about Performance?
Critical path of n-bit ripple-carry adder is n*CP
Design trick – throw hardware at it (Carry Lookahead)
A0
B0
1-bit
ALU
result0
CarryIn0
CarryOut0
A1
B1
1-bit
ALU
result1
CarryIn1
CarryOut1
A2
B2
1-bit
ALU
result2
CarryIn2
CarryOut2
A3
B3
1-bit
ALU
result3
CarryIn3
CarryOut3

## Slide 9: Multiply
Binary multiplication is just a bunch of right shifts and adds
multiplicand
multiplier
partial
product
array
double precision product
n
2n
n
can be formed in parallel and added in parallel for faster multiplication

## Slide 10: Add and Right Shift Multiplier Hardware
multiplicand
32-bit ALU
multiplier
Control
add
shift
right
product
0 1 1 0 = 6
0 0 0 0 0 1 0 1 = 5
add 0 1 1 0 0 1 0 1
0 0 1 1 0 0 1 0
add 0 0 1 1 0 0 1 0
0 0 0 1 1 0 0 1
add 0 1 1 1 1 0 0 1
0 0 0 1 1 1 1 0
add 0 0 1 1 1 1 0 0
0 0 1 1 1 1 0 0
= 30
Notes: For lecture

## Slide 11: MIPS Multiply Instruction
Multiply (mult and multu) produces a double precision product
mult $s0, $s1 # hi||lo = $s0 * $s1
  Low-order word of the product is left in processor register lo and the high-order word is left in register hi
  Instructions mfhi rd and mflo rd are provided to move the product to (user accessible) registers in the register file
0 16 17 0 0 0x18
Multiplies are usually done by fast, dedicated hardware and are much more complex (and slower) than adders
Notes: multu – does multiply unsigned
Both multiplies ignore overflow, so its up to the software to check to see if the product is too big to fit into 32 bits. There is no overflow if hi is 0 for multu or the replicated sign of lo for mult.

## Slide 12: Fast Multiplication Hardware
Can build a faster multiplier by using a parallel tree of adders with one 32-bit adder for each bit of the multiplier at the base
32-bit ALU
32-bit ALU
32-bit ALU
32-bit ALU
32-bit ALU
33-bit ALU
33-bit ALU
33-bit ALU
36-bit ALU
43-bit ALU
59-bit ALU
product0
‘ier0*’icand
‘ier1*’icand
‘ier2*’icand
‘ier3*’icand
‘ier4*’icand
‘ier5*’icand
‘ier6*’icand
‘ier7*’icand
‘ier30*’icand
. . .
. . .
. . .
product1
product2
product3
product63 . . . product5
product4

## Slide 13: Division
Division is just a bunch of quotient digit guesses and left shifts and subtracts
dividend = quotient x divisor + remainder
dividend
divisor
partial
remainder
array
quotient
n
n
remainder
n
0
0
0
0
0
0

## Slide 14: Left Shift and Subtract Division Hardware
divisor
32-bit ALU
quotient
Control
subtract
shift
left
dividend
remainder
0 0 1 0 = 2
0 0 0 0 0 1 1 0 = 6
0 0 0 0 1 1 0 0
sub 1 1 1 0 1 1 0 0
rem neg, so ‘ient bit = 0
0 0 0 0 1 1 0 0
restore remainder
0 0 0 1 1 0 0 0
sub 1 1 1 1 1 1 0 0
rem neg, so ‘ient bit = 0
0 0 0 1 1 0 0 0
restore remainder
0 0 1 1 0 0 0 0
sub 0 0 0 1 0 0 0 1
rem pos, so ‘ient bit = 1
0 0 1 0 0 0 1 0
sub 0 0 0 0 0 0 1 1
rem pos, so ‘ient bit = 1
= 3 with 0 remainder
Notes: For lecture

## Slide 15: MIPS Divide Instruction
Divide (div and divu) generates the reminder in hi and the quotient in lo
div $s0, $s1 # lo = $s0 / $s1
# hi = $s0 mod $s1
  Instructions mfhi rd and mflo rd are provided to move the quotient and reminder to (user accessible) registers in the register file
As with multiply, divide ignores overflow so software must determine if the quotient is too large. Software must also check the divisor to avoid division by 0.
0 16 17 0 0 0x1A
Notes: Seems odd to me that the machine doesn’t support a double precision dividend in hi || lo but it looks like it doesn’t

## Slide 16: Representing Big (and Small) Numbers
What if we want to encode the approx. age of the earth?
  4,600,000,000 or 4.6 x 109
or the weight in kg of one a.m.u. (atomic mass unit)
  0.0000000000000000000000000166 or 1.6 x 10-27
There is no way we can encode either of the above in a 32-bit integer.
Floating point representation (-1)sign x F x 2E
  Still have to fit everything in 32 bits (single precision)
s E (exponent) F (fraction)
1 bit 8 bits 23 bits
  The base (2, not 10) is hardwired in the design of the FPALU
  More bits in the fraction (F) or the exponent (E) is a trade-off between precision (accuracy of the number) and range (size of the number)
Notes: Notice that in scientific notation the mantissa is represented in normalized form (no leading zeros)

## Slide 17: Exception Events in Floating Point
Overflow (floating point) happens when a positive exponent becomes too large to fit in the exponent field
Underflow (floating point) happens when a negative exponent becomes too large to fit in the exponent field
s E (exponent) F (fraction)
1 bit 11 bits 20 bits
F (fraction continued)
32 bits
One way to reduce the chance of underflow or overflow is to offer another format that has a larger exponent field
  Double precision – takes two MIPS words
+∞
-∞
+ largestE +largestF
+ largestE -largestF
- largestE +smallestF
- largestE -smallestF

## Slide 18: IEEE 754 FP Standard
Most (all?) computers these days conform to the IEEE 754 floating point standard (-1)sign x (1+F) x 2E-bias
  Formats for both single and double precision
  F is stored in normalized format where the msb in F is 1 (so there is no need to store it!) – called the hidden bit
  To simplify sorting FP numbers, E comes before F in the word and E is represented in excess (biased) notation where the bias is -127 (-1023 for double precision) so the most negative is 00000001 = 21-127 = 2-126 and the most positive is 11111110 = 2254-127 = 2+127
Examples (in normalized format)
  Smallest+: 0 00000001 1.00000000000000000000000 = 1 x 21-127
  Zero: 0 00000000 00000000000000000000000 = true 0
  Largest+: 0 11111110 1.11111111111111111111111 = 2-2-23 x 2254-127
  1.02 x 2-1 =
  0.7510 x 24 =
0 01111110 1.00000000000000000000000
0 10000010 1.10000000000000000000000
Notes: Book distinguishes between the representation with the hidden bit there – significand (the 24 bit version) , and the one with the hidden bit removed – fraction (the 23 bit version)
.75 = 0.11 base 2 = 1.1 and decrement the exponent base 2
Excess exponents (128 64 32 16 8 4 2 1)
0000 0000 reserved for true zero (with F=0) or denorms (with F != 0)
0000 0001 1-127 so -126
0000 0010 2-127 so -125
…
0111 1101 125-127 so -2
0111 1110 126-127 so -1
0111 1111 127-127 so 0 (e.g., so can represent 1 x 2^0 )
1000 0000 128-127 so +1
1000 0001 129-127 so +2
1000 0010 130-127 so +3
…
1111 1110 254-127 so +127
1111 1111 255-127 so +128, but reserved for infinity with F = 0 and NAN with F != 0

## Slide 19: IEEE 754 FP Standard Encoding
Special encodings are used to represent unusual events
  ± infinity for division by zero
  NAN (not a number) for the results of invalid operations such as 0/0
  True zero is the bit string all zero
Single Precision |  | Double Precision |  | Object Represented
E (8) | F (23) | E (11) | F (52) | 
0000 0000 | 0 | 0000 … 0000 | 0 | true zero (0)
0000 0000 | nonzero | 0000 … 0000 | nonzero | ± denormalized number
1-254 | anything | 0111 …1111 to +1023,-1022 | anything | ± floating point number
255 | 0 | 1111 … 1111 | -0 | ± infinity
255 | nonzero | 1111 … 1111 | nonzero | not a number (NaN)
Notes: The E notations must not be given in bias, but in unsigned binary form in the book? I decided it was less confusing to give the bias representations (i.e., the unsigned number minus the bias).
Note that the # value for denorms is interpreted to be -126 to give a smooth transistion into the denorm space (not as -127)

## Slide 20: Support for Accurate Arithmetic
Rounding (except for truncation) requires the hardware to include extra F bits during calculations
  Guard bit – used to provide one F bit when shifting left to normalize a result (e.g., when normalizing F after division or subtraction)
  Round bit – used to improve rounding accuracy
  Sticky bit – used to support Round to nearest even; is set to a 1 whenever a 1 bit shifts (right) through it (e.g., when aligning F during addition/subtraction)
IEEE 754 FP rounding modes
  Always round up (toward +∞)
  Always round down (toward -∞)
  Truncate
  Round to nearest even (when the Guard || Round || Sticky are 100) – always creates a 0 in the least significant (kept) bit of F
F = 1 . xxxxxxxxxxxxxxxxxxxxxxx G R S

## Slide 21: Floating Point Addition
Addition (and subtraction)
(F1  2E1) + (F2  2E2) = F3  2E3
  Step 0: Restore the hidden bit in F1 and in F2
  Step 1: Align fractions by right shifting F2 by E1 - E2 positions (assuming E1  E2) keeping track of (three of) the bits shifted out in G R and S
  Step 2: Add the resulting F2 to F1 to form F3
  Step 3: Normalize F3 (so it is in the form 1.XXXXX …)
    If F1 and F2 have the same sign  F3 [1,4)  1 bit right shift F3 and increment E3 (check for overflow)
    If F1 and F2 have different signs  F3 may require many left shifts each time decrementing E3 (check for underflow)
  Step 4: Round F3 and possibly normalize F3 again
  Step 5: Rehide the most significant bit of F3 before storing the result
Notes: Note that the smaller fraction is the one shifted (while increasing its exponent until it is equal to the larger exponent)

## Slide 22: Floating Point Addition Example
Add
(0.5 = 1.0000  2-1) + (-0.4375 = -1.1100 2-2)
  Step 0:
  Step 1:
  Step 2:
  Step 3:
  Step 4:
  Step 5:
Hidden bits restored in the representation above
Shift significand with the smaller exponent (1.1100) right until its exponent matches the larger exponent (so once)
Add significands
1.0000 + (-0.111) = 1.0000 – 0.111 = 0.001
Normalize the sum, checking for exponent over/underflow
0.001 x 2-1 = 0.010 x 2-2 = .. = 1.000 x 2-4
The sum is already rounded, so we’re done
Rehide the hidden bit before storing
Notes: For lecture
Note that these are the same examples as used in the book. Would be good to use a different example, but I ran out of energy/time to do that.

## Slide 23: Floating Point Multiplication
Multiplication
(F1  2E1) x (F2  2E2) = F3  2E3
  Step 0: Restore the hidden bit in F1 and in F2
  Step 1: Add the two (biased) exponents and subtract the bias from the sum, so E1 + E2 – 127 = E3
  also determine the sign of the product (which depends on the sign of the operands (most significant bits))
  Step 2: Multiply F1 by F2 to form a double precision F3
  Step 3: Normalize F3 (so it is in the form 1.XXXXX …)
    Since F1 and F2 come in normalized  F3 [1,4)  1 bit right shift F3 and increment E3
    Check for overflow/underflow
  Step 4: Round F3 and possibly normalize F3 again
  Step 5: Rehide the most significant bit of F3 before storing the result

## Slide 24: Floating Point Multiplication Example
Multiply
(0.5 = 1.0000  2-1) x (-0.4375 = -1.1100 2-2)
  Step 0:
  Step 1:
  Step 2:
  Step 3:
  Step 4:
  Step 5:
Hidden bits restored in the representation above
Add the exponents (not in bias would be -1 + (-2) = -3 and in bias would be (-1+127) + (-2+127) – 127 = (-1 -2) + (127+127-127) = -3 + 127 = 124
Multiply the significands
1.0000 x 1.110 = 1.110000
Normalized the product, checking for exp over/underflow
1.110000 x 2-3 is already normalized
The product is already rounded, so we’re done
Rehide the hidden bit before storing
Notes: For lecture

## Slide 25: MIPS Floating Point Instructions
MIPS has a separate Floating Point Register File ($f0, $f1, …, $f31) (whose registers are used in pairs for double precision values) with special instructions to load to and store from them
lwcl $f1,54($s2) #$f1 = Memory[$s2+54]
swcl $f1,58($s4) #Memory[$s4+58] = $f1
And supports IEEE 754 single
add.s $f2,$f4,$f6 #$f2 = $f4 + $f6
and double precision operations
add.d $f2,$f4,$f6 #$f2||$f3 = $f4||$f5 + $f6||$f7
similarly for sub.s, sub.d, mul.s, mul.d, div.s, div.d
Notes: The benefits of separate floating point registers are having twice as many registers without using up more bits in the instruction format, having twice the registers bandwidth by having separate integer and floating point register sets, and being able to customize registers for floating point.
The major impact is having to create a separate set of data transfer instructions to move data between the floating point registers and memory

## Slide 26: MIPS Floating Point Instructions, Con’t
And floating point single precision comparison operations
c.x.s $f2,$f4 #if($f2 < $f4) cond=1; else cond=0
where x may be eq, neq, lt, le, gt, ge
and double precision comparison operations
c.x.d $f2,$f4 #$f2||$f3 < $f4||$f5 cond=1; else cond=0
And floating point branch operations
bclt 25 #if(cond==1) go to PC+4+25
bclf 25 #if(cond==0) go to PC+4+25

## Slide 27: Frequency of Common MIPS Instructions
Only included those with >3% and >1%
 | SPECint | SPECfp
addu | 5.2% | 3.5%
addiu | 9.0% | 7.2%
or | 4.0% | 1.2%
sll | 4.4% | 1.9%
lui | 3.3% | 0.5%
lw | 18.6% | 5.8%
sw | 7.6% | 2.0%
lbu | 3.7% | 0.1%
beq | 8.6% | 2.2%
bne | 8.4% | 1.4%
slt | 9.9% | 2.3%
slti | 3.1% | 0.3%
sltu | 3.4% | 0.8%
 | SPECint | SPECfp
add.d | 0.0% | 10.6%
sub.d | 0.0% | 4.9%
mul.d | 0.0% | 15.0%
add.s | 0.0% | 1.5%
sub.s | 0.0% | 1.8%
mul.s | 0.0% | 2.4%
l.d | 0.0% | 17.5%
s.d | 0.0% | 4.9%
l.s | 0.0% | 4.2%
s.s | 0.0% | 1.1%
lhu | 1.3% | 0.0%