## Slide 1: Computer Architecture Chapter 4A: The Processor, Part A
[Adapted from Computer Organization and Design,
Patterson & Hennessy]
Notes: Be aware that this first part of new chapter 4 is review for this class, so doesn’t go into detail. If your students are learning computer organization for the first time, this set of slides needs to be expanded greatly.

## Slide 2: The Processor: Datapath & Control
Our implementation of the MIPS is simplified
  memory-reference instructions: lw, sw
  arithmetic-logical instructions: add, sub, and, or, slt
  control flow instructions: beq, j
Generic implementation
  use the program counter (PC) to supply the instruction address and fetch the instruction from memory (and update the PC)
  decode the instruction (and read registers)
  execute the instruction
All instructions (except j) use the ALU after reading the registers
How? memory-reference? arithmetic? control flow?
Fetch
PC = PC+4
Decode
Exec
Notes: memory reference use ALU to compute addresses
arithmetic use the ALU to do the require arithmetic
control use the ALU to compute branch conditions.

## Slide 3: Aside: Clocking Methodologies
The clocking methodology defines when data in a state element is valid and stable relative to the clock
  State elements - a memory element such as a register
  Edge-triggered – all state changes occur on a clock edge
Typical execution
  read contents of state elements -> send values through combinational logic -> write results to one or more state elements
State
element
1
State
element
2
Combinational
logic
clock
one clock cycle
Assumes state elements are written on every clock cycle; if not, need explicit write control signal
  write occurs only when both the write control is asserted and the clock edge occurs
Notes: State elements (a memory element) – instruction memory, data memory, registers
With edge-triggered state elements, there is no worry about feedback within a single clock cycle (it’s a single-sided clock constraint (just have to worry about making sure the clock is long enough, don’t have to worry about it being too short))

## Slide 4: Fetching Instructions
Fetching instructions involves
  reading the instruction from the Instruction Memory
  updating the PC value to be the address of the next (sequential) instruction
Read
Address
Instruction
Instruction
Memory
Add
PC
4
  PC is updated every clock cycle, so it does not need an explicit write control signal just a clock signal
  Reading from the Instruction Memory is a combinational activity, so it doesn’t need an explicit read control signal
Fetch
PC = PC+4
Decode
Exec
clock

## Slide 5: Decoding Instructions
Decoding instructions involves
  sending the fetched instruction’s opcode and function field bits to the control unit
  and
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
Control
Unit
  reading two values from the Register File
    Register File addresses are contained in the instruction
Fetch
PC = PC+4
Decode
Exec

## Slide 6: Executing R Format Operations
R format operations (add, sub, slt, and, or)
  perform operation (op and funct) on values in rs and rt
  store the result back into the Register File (into location rd)
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
  Note that Register File is not written every cycle (e.g. sw), so we need an explicit write control signal for the Register File
Fetch
PC = PC+4
Decode
Exec
Notes: Since writes to the register file are edge-triggered, we can legally read and write the same register within a clock cycle – the read will get the value written in an earlier clock cycle, which the value written will be available to a read in a subsequent cycle.

## Slide 7: Executing Load and Store Operations
Load and store operations involves
  compute memory address by adding the base register (read from the Register File during decode) to the 16-bit signed-extended offset field in the instruction
  store value (read from the Register File during decode) written to the Data Memory
  load value, read from the Data Memory, written to the Register File
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
overflow
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
Sign
Extend
MemWrite
MemRead
16
32
Notes: Note there are separate read and write controls to the memory – only one of which may be asserted on any given clock cycle. The memory unit needs a read signal, since, unlike the register file, reading the value of an invalid address can cause problems as we will see later. (Standard memory chips actually have a write enable signal that is used for writes.)

## Slide 8: Executing Branch Operations
Branch operations involves
  compare the operands read from the Register File during decode for equality (zero ALU output)
  compute the branch target address by adding the updated PC to the 16-bit signed-extended offset field in the instr
Instruction
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
zero
ALU control
Sign
Extend
16
32
Shift
left 2
Add
4
Add
PC
Branch
target
address
(to branch control logic)

## Slide 9: Executing Jump Operations
Jump operation involves
  replace the lower 28 bits of the PC with the lower 26 bits of the fetched instruction shifted left by 2 bits
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Shift
left 2
Jump
address
26
4
28

## Slide 10: Creating a Single Datapath from the Parts
Assemble the datapath segments and add control lines and multiplexors as needed
Single cycle design – fetch, decode and execute each instructions in one clock cycle
  no datapath resource can be used more than once per instruction, so some must be duplicated (e.g., separate Instruction Memory and Data Memory, several adders)
  multiplexors needed at the input of shared elements with control lines to do the selection
  write signals to control writing to the Register File and Data Memory
Cycle time is determined by length of the longest path

## Slide 11: Fetch, R, and Memory Access Portions
MemtoReg
Read
Address
Instruction
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
ALU control
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
ALUSrc

## Slide 12: Adding the Control
Selecting the operations to perform (ALU, Register File and Memory read/write)
Controlling the flow of data (multiplexor inputs)
I-Type:
op
rs
rt
address offset
31
25
20
15
0
R-type:
31
25
20
15
5
0
op
rs
rt
rd
funct
shamt
10
Observations
  op field always in bits 31-26
  addr of registers to be read are always specified by the rs field (bits 25-21) and rt field (bits 20-16); for lw and sw rs is the base register
  addr. of register to be written is in one of two places – in rt (bits 20-16) for lw; in rd (bits 15-11) for R-type instructions
  offset for beq, lw, and sw always in bits 15-0
J-type:
31
25
0
op
target address

## Slide 13: Single Cycle Datapath with Control Unit
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch

## Slide 14: R-type Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 15: Load Word Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 16: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For class handout – have a student come forward and mark the connections in the datapath that are active. And show the state of the control lines.

## Slide 17: Branch Instruction Data/Control Flow
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Notes: For lecture

## Slide 18: Adding the Jump Operation
Read
Address
Instr[31-0]
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
ALU
ovf
zero
RegWrite
Data
Memory
Address
Write Data
Read Data
MemWrite
MemRead
Sign
Extend
16
32
MemtoReg
ALUSrc
Shift
left 2
Add
PCSrc
RegDst
ALU
control
1
1
1
0
0
0
0
1
ALUOp
Instr[5-0]
Instr[15-0]
Instr[25-21]
Instr[20-16]
Instr[15 -11]
Control
Unit
Instr[31-26]
Branch
Shift
left 2
0
1
Jump
32
Instr[25-0]
26
PC+4[31-28]
28
Notes: For lecture
Good exam questions
Add jalr rs,rd 0 rs 0 rd 0 9
jump to instr whose addr is in rs and save addr of next inst (PC+4) in rd
Add the PowerPC addressing modes of update addressing and indexed addressing (will have to expand the RegFile to be three read port and two write port)
Add andi, ori, addi - have to have both a signextend and a zeroextend and choose between the two, will have to augment the ALUop encoding (since can’t get the op information out of the funct bits as with R-type)
Add mult rs, rt with the result being left in hi|lo - so also include the mfhi and mflo instructions (will have to add a multiplier, the hi and lo registers and then a couple of muxes and their control).
Add barrel shifter

## Slide 19: Instruction Times (Critical Paths)
Instr. | I Mem | Reg Rd | ALU Op | D Mem | Reg Wr | Total
R-type |  |  |  |  |  | 
load |  |  |  |  |  | 
store |  |  |  |  |  | 
beq |  |  |  |  |  | 
jump |  |  |  |  |  | 
What is the clock cycle time assuming negligible delays for muxes, control unit, sign extend, PC access, shift left 2, wires, setup and hold times except:
  Instruction and Data Memory (200 ps)
  ALU and adders (200 ps)
  Register File access (reads or writes) (100 ps)
Notes: For class handout

## Slide 20: Instruction Critical Paths
Instr. | I Mem | Reg Rd | ALU Op | D Mem | Reg Wr | Total
R-type |  |  |  |  |  | 
load |  |  |  |  |  | 
store |  |  |  |  |  | 
beq |  |  |  |  |  | 
jump |  |  |  |  |  | 
200 | 100 | 200 |  | 100 | 600
200 | 100 | 200 | 200 | 100 | 800
What is the clock cycle time assuming negligible delays for muxes, control unit, sign extend, PC access, shift left 2, wires, setup and hold times except:
  Instruction and Data Memory (200 ps)
  ALU and adders (200 ps)
  Register File access (reads or writes) (100 ps)
200 | 100 | 200 | 200 |  | 700
200 | 100 | 200 |  |  | 500
200 |  |  |  |  | 200
Notes: For lecture
Note that PC is updated during I Mem read

## Slide 21: Single Cycle Disadvantages & Advantages
Uses the clock cycle inefficiently – the clock cycle must be timed to accommodate the slowest instruction
  especially problematic for more complex instructions like floating point multiply
May be wasteful of area since some functional units (e.g., adders) must be duplicated since they can not be shared during a clock cycle
but
Is simple and easy to understand
Clk
lw
sw
Waste
Cycle 1
Cycle 2
Notes: In the Single Cycle implementation, the cycle time is set to accommodate the longest instruction, the Load instruction.
Since the cycle time has to be long enough for the load instruction, it is too long for the store instruction so the last part of the cycle here is wasted.

## Slide 22: How Can We Make It Faster?
Fetch (and execute) more than one instruction at a time
  Superscalar processing – stay tuned
Start fetching and executing the next instruction before the current one has completed
  Pipelining – (all?) modern processors are pipelined for performance
  Remember the performance equation: CPU time = CPI * CC * IC
Under ideal conditions and with a large number of instructions, the speedup from pipelining is approximately equal to the number of pipe stages
  A five stage pipeline is nearly five times faster because the CC is nearly five times faster
Notes: In reality the time per instruction in a pipeline processor is longer than the minimum possible because 1) the pipeline stages may not be perfectly balanced and 2) pipelining involves some overhead (like pipeline stage isolation registers).

## Slide 23: The Five Stages of Load Instruction
IFetch: Instruction Fetch and Update PC
Dec: Registers Fetch and Instruction Decode
Exec: Execute R-type; calculate memory address
Mem: Read/write the data from/to the Data Memory
WB: Write the result data into the register file
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
Notes: As shown here, each of these five steps will take one clock cycle to complete.

## Slide 24: A Pipelined MIPS Processor
Start the next instruction before the current one has completed
  improves throughput - total amount of work done in a given time
  instruction latency (execution time, delay time, response time - time from the start of an instruction to its completion) is not reduced
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 5
IFetch
Dec
Exec
Mem
WB
lw
Cycle 7
Cycle 6
Cycle 8
sw
IFetch
Dec
Exec
Mem
WB
R-type
IFetch
Dec
Exec
Mem
WB
    clock cycle (pipeline stage time) is limited by the slowest stage
      for some stages don’t need the whole clock cycle (e.g., WB)
      for some instructions, some stages are wasted cycles (i.e., nothing is done during that cycle for that instruction)
Notes: Latency = execution time (delay or response time) – the total time from start to finish of ONE instruction
For processors one important measure is THROUGHPUT (or the execution bandwidth) – the total amount of work done in a given amount of time
For memories one important measure is BANDWIDTH – the amount of information communicated across an interconnect (e.g., bus) per unit time; the number of operations performed per second (the WIDTH of the operation and the RATE of the operation)

## Slide 25: Single Cycle versus Pipeline
lw
IFetch
Dec
Exec
Mem
WB
Pipeline Implementation (CC = 200 ps):
IFetch
Dec
Exec
Mem
WB
sw
IFetch
Dec
Exec
Mem
WB
R-type
Clk
Single Cycle Implementation (CC = 800 ps):
lw
sw
Waste
Cycle 1
Cycle 2
To complete an entire instruction in the pipelined case takes 1000 ps (as compared to 800 ps for the single cycle case). Why ?
How long does each take to complete 1,000,000 adds ?
400 ps
Notes: 1,000,000 adds for single cycle = 800,000,000 ps
1,000,000 adds for pipelined = 200,000,000 ps + 800 ps (fill or flush time)

## Slide 26: Pipelining the MIPS ISA
What makes it easy
  all instructions are the same length (32 bits)
    can fetch in the 1st stage and decode in the 2nd stage
  few instruction formats (three) with symmetry across formats
    can begin reading register file in 2nd stage
  memory operations occur only in loads and stores
    can use the execute stage to calculate memory addresses
  each instruction writes at most one result (i.e., changes the machine state) and does it in the last few pipeline stages (MEM or WB)
  operands must be aligned in memory so a single data transfer takes only one data memory access

## Slide 27: MIPS Pipeline Datapath Additions/Mods
State registers between each pipeline stage to isolate them
IF:IFetch
ID:Dec
EX:Execute
MEM:
MemAccess
WB:
WriteBack
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
System Clock
Notes: Any info that is needed in a later pipe stage must be passed to that stage via a pipeline register (e.g., need to preserve the destination register address in the pipeline state registers)
Note two exceptions to right-to-left flow
WB that writes the result back into the register file in the middle of the datapath
Selection of the next value of the PC, one input comes from the calculated branch address from the MEM stage
Only later instructions in the pipeline can be influenced by these two REVERSE data movements.
The first one (WB to ID) leads to data hazards.
The second one (MEM to IF) leads to control hazards.
All instructions must update some state in the processor – the register file, the memory, or the PC – so separate pipeline registers are redundant to the state that is updated (not needed).
PC can be thought of as a pipeline register: the one that feeds the IF stage of the pipeline. Unlike all of the other pipeline registers, the PC is part of the visible architecture state – its content must be saved when an exception occurs (the contents of the other pipe registers are discarded).

## Slide 28: MIPS Pipeline Control Path Modifications
All control signals can be determined during Decode
  and held in the state registers between pipeline stages
Read
Address
Instruction
Memory
Add
PC
4
Write Data
Read Addr 1
Read Addr 2
Write Addr
Register
File
Read
Data 1
Read
Data 2
16
32
ALU
Shift
left 2
Add
Data
Memory
Address
Write Data
Read
Data
IF/ID
Sign
Extend
ID/EX
EX/MEM
MEM/WB
Control
ALU
cntrl
RegWrite
MemRead
MemtoReg
RegDst
ALUOp
ALUSrc
Branch
PCSrc

## Slide 29: Pipeline Control
IF Stage: read Instr Memory (always asserted) and write PC (on System Clock)
ID Stage: no optional control signals to set
 | EX Stage |  |  |  | MEM Stage |  |  | WB Stage | 
 | RegDst | ALUOp1 | ALUOp0 | ALUSrc | Brch | MemRead | MemWrite | RegWrite | Mem toReg
R | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0
lw | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 1 | 1
sw | X | 0 | 0 | 1 | 0 | 0 | 1 | 0 | X
beq | X | 0 | 1 | 0 | 1 | 0 | 0 | 0 | X

## Slide 30: Graphically Representing MIPS Pipeline
Can help with answering questions like:
  How many cycles does it take to execute this code?
  What is the ALU doing during cycle 4?
  Is there a hazard, why does it occur, and how can it be fixed?
ALU
IM
Reg
DM
Reg

## Slide 31: Why Pipeline? For Performance!
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 0
Inst 1
Inst 2
Inst 4
Inst 3
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Once the pipeline is full, one instruction is completed every cycle, so CPI = 1
Time to fill the pipeline

## Slide 32: Can Pipelining Get Us Into Trouble?
Yes: Pipeline Hazards
  structural hazards: attempt to use the same resource by two different instructions at the same time
  data hazards: attempt to use data before it is ready
    An instruction’s source operand(s) are produced by a prior instruction still in the pipeline
  control hazards: attempt to make a decision about program control flow before the condition has been evaluated and the new PC target address calculated
    branch and jump instructions, exceptions
Can usually resolve hazards by waiting
  pipeline control must detect the hazard
  and take action to resolve hazards
Notes: Note that data hazards can come from R-type instructions or lw instructions
Exceptions can’t be resolved by waiting!

## Slide 33: A Single Memory Would Be a Structural Hazard
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
lw
Inst 1
Inst 2
Inst 4
Inst 3
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
ALU
Mem
Reg
Mem
Reg
Reading data from memory
Reading instruction from memory
Fix with separate instr and data memories (I$ and D$)

## Slide 34: How About Register File Access?
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Inst 1
Inst 2
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Fix register file access hazard by doing reads in the second half of the cycle and writes in the first half
add $1,
add $2,$1,
clock edge that controls register writing
clock edge that controls loading of pipeline state registers
Notes: Define register reads to occur in the second half of the cycle and register writes in the first half

## Slide 35: Register Usage Can Cause Data Hazards
I
n
s
t
r.
O
r
d
e
r
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
Read before write data hazard
Notes: For class handout

## Slide 36: Register Usage Can Cause Data Hazards
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
add $1,
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
Read before write data hazard
Notes: For lecture

## Slide 37: Loads Can Cause Data Hazards
I
n
s
t
r.
O
r
d
e
r
lw $1,4($2)
sub $4,$1,$5
and $6,$1,$7
xor $4,$1,$5
or $8,$1,$9
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards
Load-use data hazard
Notes: Note that lw is just another example of register usage (beyond ALU ops)

## Slide 38: Branch Instructions Cause Control Hazards
I
n
s
t
r.
O
r
d
e
r
lw
Inst 4
Inst 3
beq
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
ALU
IM
Reg
DM
Reg
Dependencies backward in time cause hazards

## Slide 39: Other Pipeline Structures Are Possible
What about the (slow) multiply operation?
  Make the clock twice as slow or …
  let it take two cycles (since it doesn’t use the DM stage)
ALU
IM
Reg
DM
Reg
MUL
ALU
IM
Reg
DM1
Reg
DM2
What if the data memory access is twice as slow as the instruction memory?
  make the clock twice as slow or …
  let data memory access take two cycles (and keep the same clock rate)
Notes: Note that we don’t need the output of MUL until the WB cycle, so we can span two pipeline stages with the MUL hardware (so the multiplier is a two stage pipelined multiplier)

## Slide 40: Other Sample Pipeline Alternatives
ARM7
XScale
ALU
IM1
IM2
DM1
Reg
DM2
IM
Reg
EX
PC update
IM access
decode
reg
access
ALU op
DM access
shift/rotate
commit result
(write back)
Reg
SHFT
PC update
BTB access
start IM access
IM access
decode
reg 1 access
shift/rotate
reg 2 access
ALU op
start DM access
exception
DM write
reg write

## Slide 41: Summary
All modern day processors use pipelining
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Potential speedup: a CPI of 1 and fast a CC
Pipeline rate limited by slowest pipeline stage
  Unbalanced pipe stages makes for inefficiencies
  The time to “fill” pipeline and time to “drain” it can impact speedup for deep pipelines and short code runs
Must detect and resolve hazards
  Stalling negatively affects CPI (makes CPI less than the ideal of 1)