## Slide 1: Computer Architecture Chapter 5A: Exploiting the Memory Hierarchy, Part 1
[Adapted from Computer Organization and Design,
Patterson & Hennessy]

## Slide 2: Review: Major Components of a Computer
Processor
Control
Datapath
Memory
Devices
Input
Output
Cache
Main Memory
Secondary Memory
(Disk)

## Slide 3: Processor-Memory Performance Gap
“Moore’s Law”
µProc
55%/year
(2X/1.5yr)
DRAM
7%/year
(2X/10yrs)
Processor-Memory
Performance Gap (grows 50%/year)
Notes: HIDDEN SLIDE – KEEP?
Memory baseline is a 64KB DRAM in 1980, with three years to the next generation until 1996 and then two years thereafter with a 7% per year performance improvement in latency.
Processor assumes a 35% improvement per year until 1986, then a 55% until 2003, then 5%
Need to supply an instruction and a data every clock cycle
In 1980 there were no caches (and no need for them), by 1995 most systems had 2 level caches (e.g., 60% of the transistors on the Alpha 21164 were in the cache)

## Slide 4: The “Memory Wall”
Processor vs DRAM speed disparity continues to grow
Clocks per instruction
Clocks per DRAM access
Good memory hierarchy (cache) design is increasingly important to overall performance

## Slide 5: The Memory Hierarchy Goal
Fact: Large memories are slow and fast memories are small
How do we create a memory that gives the illusion of being large, cheap and fast (most of the time)?
  With hierarchy
  With parallelism

## Slide 6: A Typical Memory Hierarchy
Second
Level
Cache
(SRAM)
Control
Datapath
Secondary
Memory
(Disk)
On-Chip Components
RegFile
Main
Memory
(DRAM)
Data
Cache
Instr
Cache
ITLB
DTLB
Speed (%cycles): ½’s 1’s 10’s 100’s 10,000’s
Size (bytes): 100’s 10K’s M’s G’s T’s
Cost: highest lowest
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology
Notes: Instead, the memory system of a modern computer consists of a series of black boxes ranging from the fastest to the slowest.
Besides variation in speed, these boxes also varies in size (smallest to biggest) and cost.
What makes this kind of arrangement work is one of the most important principle in computer design. The principle of locality. The principle of locality states that programs access a relatively small portion of the address space at any instant of time.
The design goal is to present the user with as much memory as is available in the cheapest technology (points to the disk).
While by taking advantage of the principle of locality, we like to provide the user an average access speed that is very close to the speed that is offered by the fastest technology.
(We will go over this slide in detail in the next lectures on caches).

## Slide 7: Memory Hierarchy Technologies
Caches use SRAM for speed and technology compatibility
  Fast (typical access times of 0.5 to 2.5 nsec)
  Low density (6 transistor cells), higher power, expensive ($2000 to $5000 per GB in 2008)
  Static: content will last “forever” (as long as power is left on)
Main memory uses DRAM for size (density)
  Slower (typical access times of 50 to 70 nsec)
  High density (1 transistor cells), lower power, cheaper ($20 to $75 per GB in 2008)
  Dynamic: needs to be “refreshed” regularly (~ every 8 ms)
    consumes1% to 2% of the active cycles of the DRAM
  Addresses divided into 2 halves (row and column)
    RAS or Row Access Strobe triggering the row decoder
    CAS or Column Access Strobe triggering the column selector
Notes: Size comparison: DRAM/SRAM is 4 to 8 times
Cost/cycle time comparison SRAM/DRAM is 8 to 16 times

## Slide 8: The Memory Hierarchy: Why Does it Work?
Temporal Locality (locality in time)
  If a memory location is referenced then it will tend to be referenced again soon
   Keep most recently accessed data items closer to the processor
Spatial Locality (locality in space)
  If a memory location is referenced, the locations with nearby addresses will tend to be referenced soon
   Move blocks consisting of contiguous words closer to the processor
Notes: How does the memory hierarchy work? Well it is rather simple, at least in principle.
In order to take advantage of the temporal locality, that is the locality in time, the memory hierarchy will keep those more recently accessed data items closer to the processor because chances are (points to the principle), the processor will access them again soon.
In order to take advantage of the spatial locality, not ONLY do we move the item that has just been accessed to the upper level, but we ALSO move the data items that are adjacent to it.
+1 = 15 min. (X:55)

## Slide 9: The Memory Hierarchy: Terminology
Block (or line): the minimum unit of information that is present (or not) in a cache
Hit Rate: the fraction of memory accesses found in a level of the memory hierarchy
  Hit Time: Time to access that level which consists of
    Time to access the block + Time to determine hit/miss
Miss Rate: the fraction of memory accesses not found in a level of the memory hierarchy  1 - (Hit Rate)
  Miss Penalty: Time to replace a block in that level with the corresponding block from a lower level which consists of
    Time to access the block in the lower level + Time to transmit that block to the level that experienced the miss + Time to insert the block in that level + Time to pass the block to the requestor
Hit Time << Miss Penalty
Notes: A HIT is when the data the processor wants to access is found in the upper level (Blk X).
The fraction of the memory access that are HIT is defined as HIT rate.
HIT Time is the time to access the Upper Level where the data is found (X). It consists of:
(a) Time to access this level.
(b) AND the time to determine if this is a Hit or Miss.
If the data the processor wants cannot be found in the Upper level. Then we have a miss and we need to retrieve the data (Blk Y) from the lower level.
By definition (definition of Hit: Fraction), the miss rate is just 1 minus the hit rate.
This miss penalty also consists of two parts:
(a) The time it takes to replace a block (Blk Y to BlkX) in the upper level.
(b) And then the time it takes to deliver this new block to the processor.
It is very important that your Hit Time to be much much smaller than your miss penalty. Otherwise, there will be no reason to build a memory hierarchy.

## Slide 10: Characteristics of the Memory Hierarchy
Increasing distance from the processor in access time
L1$
L2$
Main Memory
Secondary Memory
Processor
(Relative) size of the memory at each level
Inclusive– what is in L1$ is a subset of what is in L2$ is a subset of what is in MM that is a subset of is in SM
4-8 bytes (word)
1 to 4 blocks
1,024+ bytes (disk sector = page)
8-32 bytes (block)
Notes: Because the upper level is smaller and built using faster memory parts, its hit time will be much smaller than the time to access the next level in the hierarchy (which is the major component of the miss penalty).

## Slide 11: How is the Hierarchy Managed?
registers  memory
  by compiler (programmer?)
cache  main memory
  by the cache controller hardware
main memory  disks
  by the operating system (virtual memory)
  virtual to physical address mapping assisted by the hardware (TLB)
  by the programmer (files)

## Slide 12: Cache Basics
Two questions to answer (in hardware):
  Q1: How do we know if a data item is in the cache?
  Q2: If it is, how do we find it?
Direct mapped
  Each memory block is mapped to exactly one block in the cache
    lots of lower level blocks must share blocks in the cache
  Address mapping (to answer Q2):
  (block address) modulo (# of blocks in the cache)
  Have a tag associated with each cache block that contains the address information (the upper portion of the address) required to identify the block (to answer Q1)

## Slide 13: Caching: A Simple First Example
00
01
10
11
Cache
Main Memory
Q2: How do we find it?
Use next 2 low order memory address bits – the index – to determine which cache block (i.e., modulo the number of blocks in the cache)
Tag
Data
Q1: Is it there?
Compare the cache tag to the high order 2 memory address bits to tell if the memory block is in the cache
Valid
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
One word blocks
Two low order bits define the byte in the word (32b words)
(block address) modulo (# of blocks in the cache)
Index
Notes: For lecture
Valid bit indicates whether an entry contains valid information – if the bit is not set, there cannot be a match for this block

## Slide 14: Direct Mapped Cache
0
1
2
3
4
3
4
15
Consider the main memory word reference string
  0 1 2 3 4 3 4 15
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(2)
miss
miss
miss
miss
miss
miss
hit
hit
00 Mem(0)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01
4
11
15
00 Mem(1)
00 Mem(2)
00 Mem(3)
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 6 misses
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 15: MIPS Direct Mapped Cache Example
One word blocks, cache size = 1K words (or 4KB)
20
Tag
10
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
1021
1022
1023
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
What kind of locality are we taking advantage of?
20
Data
32
Hit
Notes: Let’s use a specific example with realistic numbers: assume we have a 1 K word (4Kbyte) direct mapped cache with block size equals to 4 bytes (1 word).
In other words, each block associated with the cache tag will have 4 bytes in it (Row 1).
With Block Size equals to 4 bytes, the 2 least significant bits of the address will be used as byte select within the cache block.
Since the cache size is 1K word, the upper 32 minus 10+2 bits, or 20 bits of the address will be stored as cache tag.
The rest of the (10) address bits in the middle, that is bit 2 through 11, will be used as Cache Index to select the proper cache entry
Temporal!

## Slide 16: Multiword Block Direct Mapped Cache
8
Index
Data
Index
Tag
Valid
0
1
2
.
.
.
253
254
255
31 30 . . . 13 12 11 . . . 4 3 2 1 0
Byte offset
20
20
Tag
Hit
Data
32
Block offset
Four words/block, cache size = 1K words
What kind of locality are we taking advantage of?
Notes: to take advantage for spatial locality want a cache block that is larger than word word in size.

## Slide 17: Taking Advantage of Spatial Locality
0
Let cache block hold more than one word
  0 1 2 3 4 3 4 15
1
2
3
4
3
4
15
00 Mem(1) Mem(0)
miss
00 Mem(1) Mem(0)
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
01
5
4
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
miss
11
15
14
Start with an empty cache - all blocks initially marked as not valid
  8 requests, 4 misses
Notes: For lecture
Show the 4-bit address mapping – 2-bits of tag, 1-bit of set address (index), 1-bit of word-in-block select

## Slide 18: Miss Rate vs Block Size vs Cache Size
Chart: Block size (bytes)
| 16 | 32 | 64 | 128 | 256
8 KB | 8.5 | 7.5 | 7.25 | 7.75 | 9.5
16 KB | 4 | 2.75 | 2.75 | 3 | 3.5
64 KB | 2 | 1.7 | 1.55 | 1.4 | 1.4
256 KB | 1 | 0.7 | 0.5 | 0.5 | 0.6
Miss rate goes up if the block size becomes a significant fraction of the cache size because the number of blocks that can be held in the same size cache is smaller (increasing capacity misses)
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 19: Cache Field Sizes
The number of bits in a cache includes both the storage for data and for the tags
  32-bit byte address
  For a direct mapped cache with 2n blocks, n bits are used for the index
  For a block size of 2m words (2m+2 bytes), m bits are used to address the word within the block and 2 bits are used to address the byte within the word
What is the size of the tag field?
The total number of bits in a direct-mapped cache is then
  2n x (block size + tag field size + valid field size)
How many total bits are required for a direct mapped cache with 16KB of data and 4-word blocks assuming a 32-bit address?
Notes: The tag field is 32 – (n+m+2)
16KB is 4K (2^12 words). With a block size of 4 words, there are 1024 (2^10) blocks. Each block has 4x32 or 128 bits of data plus a tag which is 32 – 10 -2 – 2 bits, plus a valid bit. So the total cache size is
2^10 x (4x32 +18 + 1) = 2^10 x 147 = 147Kbits (or about 1.15 times as many as needed just for storage of the data).

## Slide 20: Handling Cache Hits
Read hits (I$ and D$)
  this is what we want!
Write hits (D$ only)
  require the cache and memory to be consistent
    always write the data into both the cache block and the next level in the memory hierarchy (write-through)
    writes run at the speed of the next level in the memory hierarchy – so slow! – or can use a write buffer and stall only if the write buffer is full
  allow cache and memory to be inconsistent
    write the data only into the cache block (write-back the cache block to the next level in the memory hierarchy when that cache block is “evicted”)
    need a dirty bit for each data cache block to tell if it needs to be written back to memory when it is evicted – can use a write buffer to help “buffer” write-backs of dirty blocks
Notes: In a write-back cache, because we cannot overwrite the block (since we may not have a backup copy anywhere), stores either require two cycles (one to check for a hit, followed by one to actually do the write) or require a write buffer to hold that data (essentially pipelining the write).
By comparison, a write-through cache can always be done in one cycle assuming there is room in the write buffer. Read the tag and write the data in parallel. If the tag doesn’t match, the generate a write miss to fetch the rest of that block from the next level in the hierarchy (and update the tag field).

## Slide 21: Sources of Cache Misses
Compulsory (cold start or process migration, first reference):
  First access to a block, “cold” fact of life, not a whole lot you can do about it. If you are going to run “millions” of instruction, compulsory misses are insignificant
  Solution: increase block size (increases miss penalty; very large blocks could increase miss rate)
Capacity:
  Cache cannot contain all blocks accessed by the program
  Solution: increase cache size (may increase access time)
Conflict (collision):
  Multiple memory locations mapped to the same cache location
  Solution 1: increase cache size
  Solution 2: increase associativity (stay tuned) (may increase access time)
Notes: (Capacity miss) That is the cache misses are due to the fact that the cache is simply not large enough to contain all the blocks that are accessed by the program.
The solution to reduce the Capacity miss rate is simple: increase the cache size.
Here is a summary of other types of cache miss we talked about.
First is the Compulsory misses. These are the misses that we cannot avoid. They are caused when we first start the program.
Then we talked about the conflict misses. They are the misses that caused by multiple memory locations being mapped to the same cache location.
There are two solutions to reduce conflict misses. The first one is, once again, increase the cache size. The second one is to increase the associativity.
For example, say using a 2-way set associative cache instead of directed mapped cache.
But keep in mind that cache miss rate is only one part of the equation. You also have to worry about cache access time and miss penalty. Do NOT optimize miss rate alone.
Finally, there is another source of cache miss we will not cover today. Those are referred to as invalidation misses caused by another process, such as IO , update the main memory so you have to flush the cache to avoid inconsistency between memory and cache.
+2 = 43 min. (Y:23)

## Slide 22: Handling Cache Misses (Single Word Blocks)
Read misses (I$ and D$)
  stall the pipeline, fetch the block from the next level in the memory hierarchy, install it in the cache and send the requested word to the processor, then let the pipeline resume
Write misses (D$ only)
  stall the pipeline, fetch the block from next level in the memory hierarchy, install it in the cache (which may involve having to evict a dirty block if using a write-back cache), write the word from the processor to the cache, then let the pipeline resume
  or
  Write allocate – just write the word into the cache updating both the tag and data, no need to check for cache hit, no need to stall
  or
  No-write allocate – skip the cache write (but must invalidate that cache block since it will now hold stale data) and just write the word to the write buffer (and eventually to the next memory level), no need to stall if the write buffer isn’t full
Notes: Let’s look at our 1KB direct mapped cache again.
Assume we do a 16-bit write to memory location 0x000000 and causes a cache miss in our 1KB direct mapped cache that has 32-byte block select.
After we write the cache tag into the cache and write the 16-bit data into Byte 0 and Byte 1, do we have to read the rest of the block (Byte 2, 3, ... Byte 31) from memory?
If we do read the rest of the block in, it is called write allocate. But stop and think for a second. Is it really necessary to bring in the rest of the block on a write miss?
True, the principle of spatial locality implies that we are likely to access them soon.
But the type of access we are going to do is likely to be another write.
So if even if we do read in the data, we may end up overwriting them anyway so it is a common practice to NOT read in the rest of the block on a write miss.
If you don’t bring in the rest of the block, or use the more technical term, Write Not Allocate, you better have some way to tell the processor the rest of the block is no longer valid.
This bring us to the topic of sub-blocking.

## Slide 23: Multiword Block Considerations
Read misses (I$ and D$)
  Processed the same as for single word blocks – a miss returns the entire block from memory
  Miss penalty grows as block size grows
    Early restart – processor resumes execution as soon as the requested word of the block is returned
    Requested word first – requested word is transferred from the memory to the cache (and processor) first
  Nonblocking cache – allows the processor to continue to access the cache while the cache is handling an earlier miss
Write misses (D$)
  If using write allocate must first fetch the block from memory and then write the word to the block (or could end up with a “garbled” block in the cache (e.g., for 4 word blocks, a new tag, one word of data from the new block, and three words of data from the old block)
Notes: Early restart works best for instruction caches (since it works best for sequential accesses) – if the memory system can deliver a word every clock cycle, it can return words just in time. But if the processor needs another word from a different block before the previous transfer is complete, then the processor will have to stall until the memory is no longer busy.
Unless you have a nonblocking cache that come in two flavors
Hit under miss – allow additional cache hits during a miss with the goal of hiding some of the miss latency
Miss under miss – allow multiple outstanding cache misses (need a high bandwidth memory system to support it)

## Slide 24: Memory Systems that Support Caches
The off-chip interconnect and memory architecture can affect overall system performance in dramatic ways
CPU
Cache
DRAM
Memory
bus
One word wide organization (one word wide bus and one word wide memory)
Assume
  1 memory bus clock cycle to send the addr
  15 memory bus clock cycles to get the 1st word in the block from DRAM (row cycle time), 5 memory bus clock cycles for 2nd, 3rd, 4th words (column access time)
  1 memory bus clock cycle to return a word of data
Memory-Bus to Cache bandwidth
  number of bytes accessed from memory and transferred to cache/CPU per memory bus clock cycle
32-bit data
&
32-bit addr
per cycle
on-chip
Notes: We can reduce the miss penalty if we can increase the bandwidth from the memory to the cache. Allows larger block sizes to be used while still maintaining a low miss penalty.
The clock rate of this bus is usually much slower than the processor which negatively affects the miss penalty

## Slide 25: Review: (DDR) SDRAM Operation
N rows
N cols
DRAM
Column
Address
M-bit Output
M bit planes
N x M SRAM
Row
Address
After a row is read into the SRAM register
  Input CAS as the starting “burst” address along with a burst length
  Transfers a burst of data (ideally a cache block) from a series of sequential addr’s within that row
    The memory bus clock controls transfer of successive words in the burst
+1
Row Address
CAS
RAS
Col Address
1st M-bit Access
2nd M-bit
3rd M-bit
4th M-bit
Cycle Time
Row Add

## Slide 26: One Word Wide Bus, One Word Blocks
CPU
Cache
DRAM
Memory
bus
on-chip
If the block size is one word, then for a memory access due to a cache miss, the pipeline will have to stall for the number of cycles required to return one data word from memory
  memory bus clock cycle to send address
  memory bus clock cycles to read DRAM
  memory bus clock cycle to return data
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per memory bus clock cycle
  1
  15
  1
  17
  4/17 = 0.235
Notes: For lecture

## Slide 27: One Word Wide Bus, Four Word Blocks
CPU
Cache
DRAM
Memory
bus
on-chip
What if the block size is four words and each word is in a different DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
15 cycles
15 cycles
15 cycles
15 cycles
1
  4 x 15 = 60
  1
  62
  (4 x 4)/62 = 0.258
Notes: For lecture

## Slide 28: One Word Wide Bus, Four Word Blocks
CPU
Cache
DRAM
Memory
bus
on-chip
What if the block size is four words and all words are in the same DRAM row?
  cycle to send 1st address
  cycles to read DRAM
  cycles to return last data word
  total clock cycles miss penalty
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
15 cycles
5 cycles
5 cycles
5 cycles
1
15 + 3*5 = 30
  1
  32
  (4 x 4)/32 = 0.5
Notes: For lecture

## Slide 29: Interleaved Memory, One Word Wide Bus
For a block size of four words
  cycle to send 1st address
  cycles to read DRAM banks
  cycles to return last data word
  total clock cycles miss penalty
CPU
Cache
bus
on-chip
Number of bytes transferred per clock cycle (bandwidth) for a single miss is
  bytes per clock
15 cycles
15 cycles
15 cycles
15 cycles
  (4 x 4)/20 = 0.8
1
15
  4*1 = 4
  20
DRAM
Memory
bank 1
DRAM
Memory
bank 0
DRAM
Memory
bank 2
DRAM
Memory
bank 3
Notes: For lecture
The width of the bus and the cache need not be changed, but sending an address to several banks permits them all to read simultaneously. Interleaving retains the advantage of incurring the full memory latency only once.
Low order interleaving (low order bits select bank, high order bits used to access DRAM banks in parallel).
Low order memory interleaving, i.e.,
Bank 0 holds addresses xx…xx00
Bank 1 holds addresses xx…xx01
Bank 2 holds addresses xx…xx10
Bank 3 holds addresses xx…xx11
May want to add another example where you also have a wide bus (e.g., a 2 word bus between the interleaved memory and the processor).

## Slide 30: DRAM Memory System Summary
Its important to match the cache characteristics
  caches access one block at a time (usually more than one word)
with the DRAM characteristics
  use DRAMs that support fast multiple word accesses, preferably ones that match the block size of the cache
with the memory-bus characteristics
  make sure the memory-bus can support the DRAM access rates and patterns
  with the goal of increasing the Memory-Bus to Cache bandwidth

## Slide 31: Measuring Cache Performance
Assuming cache hit costs are included as part of the normal CPU execution cycle, then
  CPU time = IC × CPI × CC
  = IC × (CPIideal + Memory-stall cycles) × CC
CPIstall
Memory-stall cycles come from cache misses (a sum of read-stalls and write-stalls)
  Read-stall cycles = reads/program × read miss rate × read miss penalty
  Write-stall cycles = (writes/program × write miss rate × write miss penalty)
  + write buffer stalls
For write-through caches, we can simplify this to
Memory-stall cycles = accesses/program × miss rate × miss penalty
Notes: Reasonable write buffer depth (e.g., four or more words) and a memory capable of accepting writes at a rate that significantly exceeds the average write frequency means write buffer stalls are small

## Slide 32: Impacts of Cache Performance
Relative cache penalty increases as processor performance improves (faster clock rate and/or lower CPI)
  The memory speed is unlikely to improve as fast as processor cycle time. When calculating CPIstall, the cache miss penalty is measured in processor clock cycles needed to handle a miss
  The lower the CPIideal, the more pronounced the impact of stalls
A processor with a CPIideal of 2, a 100 cycle miss penalty, 36% load/store instr’s, and 2% I$ and 4% D$ miss rates
  Memory-stall cycles = 2% × 100 + 36% × 4% × 100 = 3.44
  So CPIstalls = 2 + 3.44 = 5.44
more than twice the CPIideal !
What if the CPIideal is reduced to 1? 0.5? 0.25?
What if the D$ miss rate went up 1%? 2%?
What if the processor clock rate is doubled (doubling the miss penalty)?
Notes: For ideal CPI = 1, then CPIstall = 4.44 and the amount of execution time spent on memory stalls would have risen from 3.44/5.44 = 63% to 3.44/4.44 = 77%
For miss penalty of 200, memory stall cycles = 2% 200 + 36% x 4% x 200 = 6.88 so that CPIstall = 8.88
This assumes that hit time (so hit time is 1 cycle) is not a factor in determining cache performance. A larger cache would have a longer access time (if a lower miss rate), meaning either a slower clock cycle or more stages in the pipeline for memory access.

## Slide 33: Average Memory Access Time (AMAT)
A larger cache will have a longer access time. An increase in hit time will likely add another stage to the pipeline. At some point the increase in hit time for a larger cache will overcome the improvement in hit rate leading to a decrease in performance.
Average Memory Access Time (AMAT) is the average to access memory considering both hits and misses
  AMAT = Time for a hit + Miss rate x Miss penalty
What is the AMAT for a processor with a 20 psec clock, a miss penalty of 50 clock cycles, a miss rate of 0.02 misses per instruction and a cache access time of 1 clock cycle?
Notes: AMAT = 1 + 0.02x50 = 2

## Slide 34: Reducing Cache Miss Rates #1
Allow more flexible block placement
In a direct mapped cache a memory block maps to exactly one cache block
At the other extreme, could allow a memory block to be mapped to any cache block – fully associative cache
A compromise is to divide the cache into sets each of which consists of n “ways” (n-way set associative). A memory block maps to a unique set (specified by the index field) and can be placed in any way of that set (so there are n choices)
  (block address) modulo (# sets in the cache)
Notes: All of the tags of all of the elements of the set must be searched for a match.

## Slide 35: Another Reference String Mapping
0
4
0
4
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
miss
miss
miss
miss
miss
miss
miss
miss
00 Mem(0)
00 Mem(0)
01
4
01 Mem(4)
0
00
00 Mem(0)
01
4
00 Mem(0)
01
4
00 Mem(0)
01
4
01 Mem(4)
0
00
01 Mem(4)
0
00
Start with an empty cache - all blocks initially marked as not valid
Ping pong effect due to conflict misses - two memory locations that map into the same cache block
  8 requests, 8 misses
Notes: For class handout

## Slide 36: Set Associative Cache Example
0
Cache
Main Memory
Q2: How do we find it?
Use next 1 low order memory address bit to determine which cache set (i.e., modulo the number of sets in the cache)
Tag
Data
Q1: Is it there?
Compare all the cache tags in the set to the high order 3 memory address bits to tell if the memory block is in the cache
V
0000xx
0001xx
0010xx
0011xx
0100xx
0101xx
0110xx
0111xx
1000xx
1001xx
1010xx
1011xx
1100xx
1101xx
1110xx
1111xx
Set
1
0
1
Way
0
1
One word blocks
Two low order bits define the byte in the word (32b words)
Notes: For lecture
This picture is as opposed to
Way 0
both red Set 0
Way 1
------------------------------------
Way 0
both green Set 1
Way 1

## Slide 37: Another Reference String Mapping
0
4
0
4
Consider the main memory word reference string
  0 4 0 4 0 4 0 4
miss
miss
hit
hit
000 Mem(0)
000 Mem(0)
Start with an empty cache - all blocks initially marked as not valid
010 Mem(4)
010 Mem(4)
000 Mem(0)
000 Mem(0)
010 Mem(4)
Solves the ping pong effect in a direct mapped cache due to conflict misses since now two memory locations that map into the same cache set can co-exist!
  8 requests, 2 misses
Notes: For lecture
Another sample string to try 0 1 2 3 0 8 11 0 3

## Slide 38: Four-Way Set Associative Cache
28 = 256 sets each with four ways (each with one block)
31 30 . . . 13 12 11 . . . 2 1 0
Byte offset
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Data
Tag
V
0
1
2
.
.
.
253
254
255
Index
Data
Tag
V
0
1
2
.
.
.
253
254
255
8
Index
22
Tag
Hit
Data
32
4x1 select
Way 0
Way 1
Way 2
Way 3
Notes: This is called a 4-way set associative cache because there are four cache entries for each cache index. Essentially, you have four direct mapped cache working in parallel.
This is how it works: the cache index selects a set from the cache. The four tags in the set are compared in parallel with the upper bits of the memory address.
If no tags match the incoming address tag, we have a cache miss.
Otherwise, we have a cache hit and we will select the data from the way where the tag matches occur.
This is simple enough. What is its disadvantages?
+1 = 36 min. (Y:16)

## Slide 39: Range of Set Associative Caches
For a fixed size cache, each increase by a factor of two in associativity doubles the number of blocks per set (i.e., the number or ways) and halves the number of sets – decreases the size of the index by 1 bit and increases the size of the tag by 1 bit
Block offset
Byte offset
Index
Tag
Decreasing associativity
Fully associative
(only one set)
Tag is all the bits except
block and byte offset
Direct mapped
(only one way)
Smaller tags, only a single comparator
Increasing associativity
Selects the set
Used for tag compare
Selects the word in the block
Notes: For lecture
In 2008, the greater size and power consumption of CAMs generally leads to 2-way and 4-way set associativity being built from standard SRAMs with comparators with 8-way and above being built using CAMs

## Slide 40: Costs of Set Associative Caches
When a miss occurs, which way’s block do we pick for replacement?
  Least Recently Used (LRU): the block replaced is the one that has been unused for the longest time
    Must have hardware to keep track of when each way’s block was used relative to the other blocks in the set
    For 2-way set associative, takes one bit per set → set the bit when a block is referenced (and reset the other way’s bit)
N-way set associative cache costs
  N comparators (delay and area)
  MUX delay (set selection) before data is available
  Data available after set selection (and Hit/Miss decision). In a direct mapped cache, the cache block is available before the Hit/Miss decision
    So its not possible to just assume a hit and continue and recover later if it was a miss
Notes: First of all, a N-way set associative cache will need N comparators instead of just one comparator (use the right side of the diagram for direct mapped cache).
A N-way set associative cache will also be slower than a direct mapped cache because of this extra multiplexer delay.
Finally, for a N-way set associative cache, the data will be available AFTER the hit/miss signal becomes valid because the hit/mis is needed to control the data MUX.
For a direct mapped cache, that is everything before the MUX on the right or left side, the cache block will be available BEFORE the hit/miss signal (AND gate output) because the data does not have to go through the comparator.
This can be an important consideration because the processor can now go ahead and use the data without knowing if it is a Hit or Miss. Just assume it is a hit.
Since cache hit rate is in the upper 90% range, you will be ahead of the game 90% of the time and for those 10% of the time that you are wrong, just make sure you can recover.
You cannot play this speculation game with a N-way set-associative cache because as I said earlier, the data will not be available to you until the hit/miss signal is valid.
+2 = 38 min. (Y:18)

## Slide 41: Benefits of Set Associative Caches
The choice of direct mapped or set associative depends on the cost of a miss versus the cost of implementation
Data from Hennessy & Patterson, Computer Architecture, 2003
Largest gains are in going from direct mapped to 2-way (20%+ reduction in miss rate)
Notes: As cache sizes grow, the relative improvement from associativity increases only slightly; since the overall miss rate of a larger cache is lower, the opportunity for improving the miss rate decreases and the absolute improvement in miss rate from associativity shrinks significantly.

## Slide 42: Reducing Cache Miss Rates #2
Use multiple levels of caches
With advancing technology have more than enough room on the die for bigger L1 caches or for a second level of caches – normally a unified L2 cache (i.e., it holds both instructions and data) and in some cases even a unified L3 cache
For our example, CPIideal of 2, 100 cycle miss penalty (to main memory) and a 25 cycle miss penalty (to UL2$), 36% load/stores, a 2% (4%) L1 I$ (D$) miss rate, add a 0.5% UL2$ miss rate
  CPIstalls = 2 + .02×25 + .36×.04×25 + .005×100 + .36×.005×100 = 3.54 (as compared to 5.44 with no L2$)
Notes: Also reduces cache miss penalty

## Slide 43: Multilevel Cache Design Considerations
Design considerations for L1 and L2 caches are very different
  Primary cache should focus on minimizing hit time in support of a shorter clock cycle
    Smaller with smaller block sizes
  Secondary cache(s) should focus on reducing miss rate to reduce the penalty of long main memory access times
    Larger with larger block sizes
    Higher levels of associativity
The miss penalty of the L1 cache is significantly reduced by the presence of an L2 cache – so it can be smaller (i.e., faster) but have a higher miss rate
For the L2 cache, hit time is less important than miss rate
  The L2$ hit time determines L1$’s miss penalty
  L2$ local miss rate >> than the global miss rate
Notes: Global miss rate – the fraction of references that miss in all levels of a multilevel cache. The global miss rate dictates how often we must access the main memory.
Local miss rate – the fraction of references to one level of a cache that miss

## Slide 44: Two Machines’ Cache Parameters
 | Intel Nehalem | AMD Barcelona
L1 cache organization & size | Split I$ and D$; 32KB for each per core; 64B blocks | Split I$ and D$; 64KB for each per core; 64B blocks
L1 associativity | 4-way (I), 8-way (D) set assoc.; ~LRU replacement | 2-way set assoc.; LRU replacement
L1 write policy | write-back, write-allocate | write-back, write-allocate
L2 cache organization & size | Unified; 256MB (0.25MB) per core; 64B blocks | Unified; 512KB (0.5MB) per core; 64B blocks
L2 associativity | 8-way set assoc.; ~LRU | 16-way set assoc.; ~LRU
L2 write policy | write-back | write-back
L2 write policy | write-back, write-allocate | write-back, write-allocate
L3 cache organization & size | Unified; 8192KB (8MB) shared by cores; 64B blocks | Unified; 2048KB (2MB) shared by cores; 64B blocks
L3 associativity | 16-way set assoc. | 32-way set assoc.; evict block shared by fewest cores
L3 write policy | write-back, write-allocate | write-back; write-allocate

## Slide 45: FSM Cache Controller
Key characteristics for a simple L1 cache
  Direct mapped
  Write-back using write-allocate
  Block size of 4 32-bit words (so 16B); Cache size of 16KB (so 1024 blocks)
  18-bit tags, 10-bit index, 2-bit block offset, 2-bit byte offset, dirty bit, valid bit, LRU bits (if set associative)
Cache
&
Cache
Controller
1-bit Read/Write
Processor
DDR SDRAM
1-bit Valid
32-bit address
32-bit data
32-bit data
1-bit Ready
1-bit Read/Write
1-bit Valid
32-bit address
128-bit data
128-bit data
1-bit Ready
Notes: A blocking cache so the processor must wait until the cache has finished this request
Memory controller will notify the Cache Controller via the Ready signal when the memory read or write is finished

## Slide 46: Four State Cache Controller
Idle
Compare Tag
If Valid && Hit
Set Valid, Set Tag,
If Write set Dirty
Allocate
Read new block
from memory
Write Back
Write old block
to memory
Cache Hit
Mark Cache Ready
Cache Miss
Old block is
Dirty
Memory Ready
Memory Ready
Memory
Not Ready
Memory
Not Ready
Cache Miss
Old block is
clean
Valid CPU request
Notes: Idle – waits for a Read/Write request from the Processor along with a Valid signal, FSM moves to Compare Tag state
Compare Tag – Checks to see if the request is a hit or a miss. On hit and Valid, returns data to the Processor and moves back to Idle state. On miss, if dirty goes to Write Back state or to Allocate state.
Write Back – Writes the 128-bit block to Memory. When memory write is complete move to the Allocate state.
Allocate – Fetch new block from Memory. Wait in this state until the Memory returns a Ready signal. Then write new block into the Cache and return to the Compare Tag state.

## Slide 47: Cache Coherence in Multicores
In future multicore processors its likely that the cores will share a common physical address space, causing a cache coherence problem
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = 0
X = 0
Read X
Read X
Write 1 to X
X = 1
X = 1
Notes: For lecture
Assumes a write through L1 cache

## Slide 48: A Coherent Memory System
Any read of a data item should return the most recently written value of the data item
  Coherence – defines what values can be returned by a read
    Writes to the same location are serialized (two writes to the same location must be seen in the same order by all cores)
  Consistency – determines when a written value will be returned by a read
To enforce coherence, caches must provide
  Replication of shared data items in multiple cores’ caches
    Replication reduces both latency and contention for a read shared data item
  Migration of shared data items to a core’s local cache
    Migration reduced the latency of the access the data and the bandwidth demand on the shared memory (L2 in our example)
Notes: Supporting migration and replication is critical to performance in accessing shared data.

## Slide 49: Cache Coherence Protocols
Need a hardware protocol to ensure cache coherence the most popular of which is snooping
  The cache controllers monitor (snoop) on the broadcast medium (e.g., bus) with duplicate address tag hardware (so they don’t interfere with core’s access to the cache) to determine if their cache has a copy of a block that is requested
Write invalidate protocol – writes require exclusive access and invalidate all other copies
  Exclusive access ensure that no other readable or writable copies of an item exists
If two processors attempt to write the same data at the same time, one of them wins the race causing the other core’s copy to be invalidated. For the other core to complete, it must obtain a new copy of the data which must now contain the updated value – thus enforcing write serialization
Notes:   Reading from multiple copies is not a problem!! Only writes cause issues. What happens if two processors try to write to the same shared data word in the same clock cycle? The bus arbiter decides which processor gets the bus first (and this will be the processor with the first exclusive access). Then the second processor will get exclusive access. Thus, bus arbitration forces sequential behavior.
  This sequential consistency is the most conservative of the memory consistency models. With it, the result of any execution is the same as if the accesses of each processor were kept in order and the accesses among different processors were interleaved.
Each block needs an additional state bit – owner - which indicates that a block may be shared, but the owning core is responsible for updating any other processors and memory when it changes the block or replaces it.
An alternative to snooping is a directory based cache coherence protocol where the directory keeps the sharing status of blocks of physical memory. They have slightly higher implementation overhead but can reduc traffic between caches and thus scale to larger core counts.

## Slide 50: Handling Writes
Ensuring that all other processors sharing data are informed of writes can be handled two ways:
Write-update (write-broadcast) – writing processor broadcasts new data over the bus, all copies are updated
  All writes go to the bus  higher bus traffic
  Since new values appear in caches sooner, can reduce latency
Write-invalidate – writing processor issues invalidation signal on bus, cache snoops check to see if they have a copy of the data, if so they invalidate their cache block containing the word (this allows multiple readers but only one writer)
  Uses the bus only on the first write  lower bus traffic, so better use of bus bandwidth
Notes: IN HIDE MODE – NEEDED?
All commercial machines use write-invalidate as their standard coherence protocol

## Slide 51: Example of Snooping Invalidation
When the second miss by Core 2 occurs, Core 1 responds with the value canceling the response from the L2 cache (and also updating the L2 copy)
Core 1
Core 2
L1 I$
L1 D$
Unified (shared) L2
L1 I$
L1 D$
X = 0
X = 0
X = 0
Read X
Read X
Write 1 to X
X = 1
Read X
X = I
X = I
X = 1
X = 1
Notes: For lecture
Snooping bus with write-back L1 cache. Requires an additional state – called owner – which indicates that a block may be shared, but the owning core is responsible for updating any other processors and memory when it changes the block or replaces it

## Slide 52: A Write-Invalidate CC Protocol
Shared
(clean)
Invalid
Modified
(dirty)
write-back caching protocol in black
read (miss)
write (hit or miss)
read (hit or miss)
read (hit) or write (hit)
write (miss)
send invalidate
receives invalidate
(write by another core
to this block)
write-back due to read (miss) by another core to this block
send invalidate
signals from the core in red
signals from the bus in blue
Notes: For lecture
A read miss causes the cache to acquire the bus and write back the victim block (if it was in the Modified (dirty) state). All the other caches monitor the read miss to see if this block is in their cache. If one has a copy and it is in the Modified state, then the block is written back and its state is changed to Invalid. The read miss is then satisfied by reading from the block memory, and the state of the block is set to Shared.
Read hits do not change the cache state.
A write miss to an Invalid block causes the cache to acquire the bus, read the block, modify the portion of the block being written and changing the block’s state to Modified. A write miss to a Shared block causes the cache to acquire the bus, send an invalidate signal to invalidate any other existing copies in other caches, modify the portion of the block being written and chang the block’s state to Modified.
A write hit to a Modified block causes no action. A write hit to a Shared block causes the cache to acquire the bus, send an invalidate signal to invalidate any other existing copies in other caches, modify the part of the block being written, and change the state to Modified.

## Slide 53: Data Miss Rates
Shared data has lower spatial and temporal locality
  Share data misses often dominate cache behavior even though they may only be 10% to 40% of the data accesses
64KB 2-way set associative data cache with 32B blocks
Hennessy & Patterson, Computer Architecture: A Quantitative Approach
Notes: Compulsory misses are all very small and are included in capacity misses. The x axis is core count

## Slide 54: Block Size Effects
Writes to one word in a multi-word block mean that the full block is invalidated
Multi-word blocks can also result in false sharing: when two cores are writing to two different variables that happen to fall in the same cache block
  With write-invalidate false sharing increases cache miss rates
Compilers can help reduce false sharing by allocating highly correlated data to the same cache block
A
B
Core1
Core2
4 word cache block

## Slide 55: Other Coherence Protocols
There are many variations on cache coherence protocols
Another write-invalidate protocol used in the Pentium 4 (and many other processors) is MESI with four states:
  Modified – same
  Exclusive – only one copy of the shared data is allowed to be cached; memory has an up-to-date copy
    Since there is only one copy of the block, write hits don’t need to send invalidate signal
  Shared – multiple copies of the shared data may be cached (i.e., data permitted to be cached with more than one processor); memory has an up-to-date copy
  Invalid – same
Notes: For E and S book states that memory has an up-to-date version so is this not a write-back cache ???

## Slide 56: Summary: Improving Cache Performance
0. Reduce the time to hit in the cache
  smaller cache
  direct mapped cache
  smaller blocks
  for writes
    no write allocate – no “hit” on cache, just write to write buffer
    write allocate – to avoid two cycles (first check for hit, then write) pipeline writes via a delayed write buffer to cache
1. Reduce the miss rate
  bigger cache
  more flexible placement (increase associativity)
  larger blocks (16 to 64 bytes typical)
  victim cache – small buffer holding most recently discarded blocks

## Slide 57: Summary: Improving Cache Performance
2. Reduce the miss penalty
  smaller blocks
  use a write buffer to hold dirty blocks being replaced so don’t have to wait for the write to complete before reading
  check write buffer (and/or victim cache) on read miss – may get lucky
  for large blocks fetch critical word first
  use multiple cache levels – L2 cache not tied to CPU clock rate
  faster backing store/improved memory bandwidth
    wider buses
    memory interleaving, DDR SDRAMs

## Slide 58: Summary: The Cache Design Space
Several interacting dimensions
  cache size
  block size
  associativity
  replacement policy
  write-through vs write-back
  write allocation
The optimal choice is a compromise
  depends on access characteristics
    workload
    use (I-cache, D-cache, TLB)
  depends on technology / cost
Simplicity often wins
Associativity
Cache Size
Block Size
Bad
Good
Less
More
Factor A
Factor B
Notes: No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
No fancy replacement policy is needed for the direct mapped cache.
As a matter of fact, that is what cause direct mapped trouble to begin with: only one place to go in the cache--causes conflict misses.
Besides working at Sun, I also teach people how to fly whenever I have time.
Statistic have shown that if a pilot crashed after an engine failure, he or she is more likely to get killed in a multi-engine light airplane than a single engine airplane.
The joke among us flight instructors is that: sure, when the engine quit in a single engine stops, you have one option: sooner or later, you land. Probably sooner.
But in a multi-engine airplane with one engine stops, you have a lot of options. It is the need to make a decision that kills those people.