## Slide 1: Computer Architecture Chapter 5B: Exploiting the Memory Hierarchy, Part 2
[Adapted from Computer Organization and Design,
Patterson & Hennessy]

## Slide 2: Review: Major Components of a Computer
Processor
Control
Datapath
Memory
Devices
Input
Output
Cache
Main Memory
Secondary Memory
(Disk)

## Slide 3: How is the Hierarchy Managed?
registers  memory
  by compiler (programmer?)
cache  main memory
  by the cache controller hardware
main memory  disks
  by the operating system (virtual memory)
  virtual to physical address mapping assisted by the hardware (TLB)
  by the programmer (files)

## Slide 4: Review: The Memory Hierarchy
Increasing distance from the processor in access time
L1$
L2$
Main Memory
Secondary Memory
Processor
(Relative) size of the memory at each level
Inclusive– what is in L1$ is a subset of what is in L2$ is a subset of what is in MM that is a subset of is in SM
4-8 bytes (word)
1 to 4 blocks
1,024+ bytes (disk sector = page)
8-32 bytes (block)
Take advantage of the principle of locality to present the user with as much memory as is available in the cheapest technology at the speed offered by the fastest technology

## Slide 5: Virtual Memory
Use main memory as a “cache” for secondary memory
  Allows efficient and safe sharing of memory among multiple programs
  Provides the ability to easily run programs larger than the size of physical memory
  Simplifies loading a program for execution by providing for code relocation (i.e., the code can be loaded anywhere in main memory)
What makes it work? – again the Principle of Locality
  A program is likely to access a relatively small portion of its address space during any period of time
Each program is compiled into its own address space – a “virtual” address space
  During run-time each virtual address must be translated to a physical address (an address in main memory)
Notes: The translation from virtual to physical enforces protection of a program’s address space from other programs

## Slide 6: Two Programs Sharing Physical Memory
Program 1
virtual address space
main memory
A program’s address space is divided into pages (all one fixed size) or segments (variable sizes)
  The starting location of each page (either in main memory or in secondary memory) is contained in the program’s page table
Program 2
virtual address space

## Slide 7: Address Translation
Virtual Address (VA)
Page offset
Virtual page number
31 30 . . . 12 11 . . . 0
Page offset
Physical page number
Physical Address (PA)
29 . . . 12 11 0
Translation
So each memory request first requires an address translation from the virtual space to the physical space
  A virtual memory miss (i.e., when the page is not in physical memory) is called a page fault
A virtual address is translated to a physical address by a combination of hardware and software
Notes: The page size is 212 = 4KB, the number of physical pages allowed in memory is 218, the physical address space is 1GB and the virtual address space is 4GB

## Slide 8: Address Translation Mechanisms
Physical page
base addr
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
Page Table
(in main memory)
Offset
Physical page #
Offset
Page table register
Notes: The page table together with the program counter and the registers specifies the state of a program – usually called a process
The operating system simply loads the page table register to point to the page table of the process it wants to make active (and loads the register file and the program counter)

## Slide 9: Virtual Addressing with a Cache
Thus it takes an extra memory access to translate a VA to a PA
CPU
Trans-
lation
Cache
Main
Memory
VA
PA
miss
hit
data
This makes memory (cache) accesses very expensive (if every access was really two accesses)
The hardware fix is to use a Translation Lookaside Buffer (TLB) – a small cache that keeps track of recently used address mappings to avoid having to do a page table lookup

## Slide 10: Making Address Translation Fast
Physical page
base addr
Main memory
Disk storage
Virtual page #
V
1
1
1
1
1
1
0
1
0
1
0
1
1
1
0
1
Tag
Physical page
base addr
V
TLB
Page Table
(in physical memory)
Page table register

## Slide 11: Translation Lookaside Buffers (TLBs)
Just like any other cache, the TLB can be organized as fully associative, set associative, or direct mapped
V Virtual Page # Physical Page # Dirty Ref Access
TLB access time is typically smaller than cache access time (because TLBs are much smaller than caches)
  TLBs are typically not more than 512 entries even on high end machines

## Slide 12: A TLB in the Memory Hierarchy
A TLB miss – is it a page fault or merely a TLB miss?
  If the page is loaded into main memory, then the TLB miss can be handled (in hardware or software) by loading the translation information from the page table into the TLB
    Takes 10’s of cycles to find and load the translation info into the TLB
  If the page is not in main memory, then it’s a true page fault
    Takes 1,000,000’s of cycles to service a page fault
TLB misses are much more frequent than true page faults
CPU
TLB
Lookup
Cache
Main
Memory
VA
PA
miss
hit
data
Trans-
lation
hit
miss
¾ t
¼ t

## Slide 13: TLB Event Combinations
TLB | Page Table | Cache | Possible? Under what circumstances?
Hit | Hit | Hit | 
Hit | Hit | Miss | 
Miss | Hit | Hit | 
Miss | Hit | Miss | 
Miss | Miss | Miss | 
Hit | Miss | Miss/ Hit | 
Miss | Miss | Hit | 
Yes – what we want!
Yes – although the page table is not
checked if the TLB hits
Yes – TLB miss, PA in page table
Yes – TLB miss, PA in page table, but data
not in cache
Yes – page fault
Impossible – TLB translation not possible if
page is not present in memory
Impossible – data not allowed in cache if
page is not in memory

## Slide 14: Handling a TLB Miss
Consider a TLB miss for a page that is present in memory (i.e., the Valid bit in the page table is set)
  A TLB miss (or a page fault exception) must be asserted by the end of the same clock cycle that the memory access occurs so that the next clock cycle will begin exception processing
Register | CP0 Reg # | Description
EPC | 14 | Where to restart after exception
Cause | 13 | Cause of exception
BadVAddr | 8 | Address that caused exception
Index | 0 | Location in TLB to be read/written
Random | 1 | Pseudorandom location in TLB
EntryLo | 2 | Physical page address and flags
EntryHi | 10 | Virtual page address
Context | 4 | Page table address & page number
Notes: For page faults …
If the page is not present in memory, then we need to transfer control to the operating system to deal with a page fault
  Must prevent the write on a store from completing when there is a page fault – deassert the write control line to memory

## Slide 15: A MIPS Software TLB Miss Handler
When a TLB miss occurs, the hardware saves the address that caused the miss in BadVAddr and transfers control to 8000 0000hex, the location of the TLB miss handler
TLBmiss:
mfc0 $k1, Context #copy addr of PTE into $k1
lw $k1, 0($k1) #put PTE into $k1
mtc0 $k1, EntryLo #put PTE into EntryLo
tlbwr #put EntryLo into TLB
# at Random
eret #return from exception
tlbwr copies from EntryLo into the TLB entry selected by the control register Random
A TLB miss takes about a dozen clock cycles to handle
Notes: The upper 12 bits of Context have the address of the base of the page table and the next 18 bits have the virtual address of the missing page (the last two bits are zero).
Note that the TLB miss handler does not check to see if the page table entry is valid. If the entry is invalid, another exception will occur – causing the page fault handler to run
TLB misses have a special entry point to lower the penalty for a TLB miss.

## Slide 16: Some Virtual Memory Design Parameters
 | Paged VM | TLBs
Total size | 16,000 to 250,000 words | 16 to 512 entries
Total size (KB) | 250,000 to 1,000,000,000 | 0.25 to 16
Block size (B) | 4000 to 64,000 | 4 to 8
Hit time |  | 0.5 to 1 clock cycle
Miss penalty (clocks) | 10,000,000 to 100,000,000 | 10 to 100
Miss rates | 0.00001% to 0.0001% | 0.01% to 1%

## Slide 17: Two Machines’ TLB Parameters
 | Intel Nehalem | AMD Barcelona
Address sizes | 48 bits (vir); 44 bits (phy) | 48 bits (vir); 48 bits (phy)
Page size | 4KB | 4KB
TLB organization | L1 TLB for instructions and L1 TLB for data per core; both are 4-way set assoc.; LRU L1 ITLB has 128 entries, L2 DTLB has 64 entries L2 TLB (unified) is 4-way set assoc.; LRU L2 TLB has 512 entries TLB misses handled in hardware | L1 TLB for instructions and L1 TLB for data per core; both are fully assoc.; LRU L1 ITLB and DTLB each have 48 entries L2 TLB for instructions and L2 TLB for data per core; each are 4-way set assoc.; round robin LRU Both L2 TLBs have 512 entries TLB misses handled in hardware

## Slide 18: Why Not a Virtually Addressed Cache?
A virtually addressed cache would only require address translation on cache misses
data
CPU
Trans-
lation
Cache
Main
Memory
VA
hit
PA
but
  Two programs which are sharing data will have two different virtual addresses for the same physical address – aliasing – so have two copies of the shared data in the cache and two entries in the TBL which would lead to coherence issues
    Must update all cache entries with the same physical address or the memory becomes inconsistent
Notes: Handling aliasing requires significant hardware – essentially an associative lookup on the physical address tags to see if you have multiple hits
This would benefit from a picture that showes two processes sharing data – with aliasing

## Slide 19: Reducing Translation Time
Can overlap the cache access with the TLB access
  Works when the high order bits of the VA are used to access the TLB while the low order bits are used as index into cache
Tag
Data
=
Tag
Data
=
Cache Hit
Desired word
VA Tag
PA
Tag
TLB Hit
2-way Associative Cache
Index
PA Tag
Block offset
Page offset
Virtual page #
Notes: Overlapped access only works as long as the address bits used to index into the cache do not change as the result of VA translation
This usually limits things to small caches, large page sizes, or high n-way set associative caches if you want a large cache

## Slide 20: The Hardware/Software Boundary
What parts of the virtual to physical address translation is done by or assisted by the hardware?
  Translation Lookaside Buffer (TLB) that caches the recent translations
    TLB access time is part of the cache hit time
    May allot an extra stage in the pipeline for TLB access
  Page table storage, fault detection and updating
    Page faults result in interrupts (precise) that are then handled by the OS
    Hardware must support (i.e., update appropriately) Dirty and Reference bits (e.g., ~LRU) in the Page Tables
  Disk placement
    Bootstrap (e.g., out of disk sector 0) so the system can service a limited number of page faults before the OS is even loaded

## Slide 21: 4 Questions for the Memory Hierarchy
Q1: Where can a entry be placed in the upper level? (Entry placement)
Q2: How is a entry found if it is in the upper level? (Entry identification)
Q3: Which entry should be replaced on a miss? (Entry replacement)
Q4: What happens on a write? (Write strategy)

## Slide 22: Q1&Q2: Where can a entry be placed/found?
 | # of sets | Entries per set
Direct mapped | # of entries | 1
Set associative | (# of entries)/ associativity | Associativity (typically 2 to 16)
Fully associative | 1 | # of entries
 | Location method | # of comparisons
Direct mapped | Index | 1
Set associative | Index the set; compare set’s tags | Degree of associativity
Fully associative | Compare all entries’ tags Separate lookup (page) table | # of entries 0

## Slide 23: Q3: Which entry should be replaced on a miss?
Easy for direct mapped – only one choice
Set associative or fully associative
  Random
  LRU (Least Recently Used)
For a 2-way set associative, random replacement has a miss rate about 1.1 times higher than LRU
LRU is too costly to implement for high levels of associativity (> 4-way) since tracking the usage information is costly

## Slide 24: Q4: What happens on a write?
Write-through – The information is written to the entry in the current memory level and to the entry in the next level of the memory hierarchy
  Always combined with a write buffer so write waits to next level memory can be eliminated (as long as the write buffer doesn’t fill)
Write-back – The information is written only to the entry in the current memory level. The modified entry is written to next level of memory only when it is replaced.
  Need a dirty bit to keep track of whether the entry is clean or dirty
  Virtual memory systems always use write-back of dirty pages to disk
Pros and cons of each?
  Write-through: read misses don’t result in writes (so are simpler and cheaper), easier to implement
  Write-back: writes run at the speed of the cache; repeated writes require only one write to lower level
Notes: The rate at which writes are generated by a processor generally exceed the rate at which the memory system can process them, even allowing for physically and logically wider memories and burst modes for DRAMs. Subsequently, most of today’s caches use write-back

## Slide 25: Summary
The Principle of Locality:
  Program likely to access a relatively small portion of the address space at any instant of time.
    Temporal Locality: Locality in Time
    Spatial Locality: Locality in Space
Caches, TLBs, Virtual Memory all understood by examining how they deal with the four questions
  Where can entry be placed?
  How is entry found?
  What entry is replaced on miss?
  How are writes handled?
Page tables map virtual address to physical address
  TLBs are important for fast translation
Notes: Let’s summarize today’s lecture. I know you have heard this many times and many ways but it is still worth repeating.
Memory hierarchy works because of the Principle of Locality which says a program will access a relatively small portion of the address space at any instant of time.
There are two types of locality: temporal locality, or locality in time and spatial locality, or locality in space.
So far, we have covered three major categories of cache misses.
Compulsory misses are cache misses due to cold start. You cannot avoid them but if you are going to run billions of instructions anyway, compulsory misses usually don’t bother you.
Conflict misses are misses caused by multiple memory location being mapped to the same cache location.
The nightmare scenario is the ping pong effect when a block is read into the cache but before we have a chance to use it, it was immediately forced out by another conflict miss.
You can reduce Conflict misses by either increase the cache size or increase the associativity, or both.
Finally, Capacity misses occurs when the cache is not big enough to contains all the cache blocks required by the program. You can reduce this miss rate by making the cache larger.
There are two write policy as far as cache write is concerned. Write through requires a write buffer and a nightmare scenario is when the store occurs so frequent that you saturates your write buffer.
The second write polity is write back. In this case, you only write to the cache and only when the cache block is being replaced do you write the cache block back to memory.
+3 = 77 min. (Y:57)